## Slide 1: Proposals on unused bandwidth utilization
Date: 2020-04-27
Authors:
Name | Affiliations | Address | Phone | Email
Sindhu Verma | Broadcom |  |  | sindhu.verma@broadcom.com
Shubhodeep Adhikari |  |  |  | shubhodeep.adhikari@broadcom.com
Matthew Fischer |  |  |  | matthew.fischer@broadcom.com
Vinko Erceg |  |  |  | vinko.erceg@broadcom.com

## Slide 2: Abstract
This contribution discusses changes required to enable a device to transmit on the DL or enable transmission on the UL, on any subset of channels that are a part of its operating bandwidth and are idle, even when the primary channel is busy.
Two scenarios are considered:
Scenario 1: Untriggered transmissions: Device finds the primary channel busy, either due to transmissions within its own BSS or OBSS, but still performs CCA on the other channels and transmits on these channels on completion of CCA.
Scenario 2: Triggered transmissions: Device (a AP in this case) triggers UL transmissions but realizes that a subset of the channels has not been utilized by the non-AP STA(s) (due to CCA failure or other reasons), in which case the device regains the unoccupied channels for its own DL/UL transmissions.
Prerequisites:
Device should be capable of performing CCA on channels in presence of reception on other channels.
Transmissions that exclude the primary channel should be allowed.

## Slide 3: Scenario 1: Untriggered transmissions when the primary channel is not idle (1)
APs or non-AP STAs can make use of the scheme.
Types of busy detection and corresponding actions.
  When the primary channel is busy due to transmissions from own BSS1
    Transmission on the non-primary channels that have been reacquired and the ongoing transmission on the primary channel should have the same end time. This helps realigning the availability of primary and other channels for wideband operation and aids any other devices in the network that are not capable of performing independent Tx/Rx/CCA on the channels.
  When the primary channel is busy due to transmission from OBSS1
    It is desirable that the transmission on the non-primary channels that have been reacquired and the ongoing transmission on the primary channel have the same end time, so that devices that are unable to do CCA on the primary channel due to transmission on other channels have an opportunity to reoccupy the primary channel
  When the primary channel is detected busy using only ED
    It is still useful to occupy the unused channels. The primary channel may be busy due to transmissions from another technology, for which the duration of transmission may not be available. In this case, the device can either transmit for an entire TXOP or have shorter bursts of transmission while polling the primary periodically
1 The BSS/OBSS distinction is made via preamble detection.

## Slide 4: Scenario 1: Untriggered transmissions when the primary channel is not idle (2)
To be able to transmit on any combination of non-primary channels, full CCA1 needs to be running on each of the 20 MHz channels. This is required by the ETSI harmonized standard for 5 GHz (EN 301893).
  Option 1: Whenever the device wins access on any one channel using full CCA, it is allowed to do PIFS CCA on the other channels and transmit on the set of idle channels, if the set of channels are part of an 802.11 bonded channel set.
  Option 2: The device starts the full CCA on another channel after the device determines the primary channel is busy and some other channels are idle. However, this may delay gaining access to these channels, compared to a device that can run full CCA in parallel on all channels compared to a device which can run parallel full CCA on all channels
If the device needs to align the end of its own transmission with the end of ongoing transmission on the primary channel, it needs to read the duration from the PHY header of the primary channel transmission. The device can either start its own transmission on the other channels after it reads the duration from the PHY header or it can start with a short packet until the duration information is available.
  As proposed in IEEE 802.11-20/0362r0 , a mode can be defined to enable a device to transmit consecutive AMPDUs, separated by SIFS gap or even without any gap, without any immediate Block Ack from the receiver after each AMPDU. This will allow the device to meaningfully occupy the medium with transmission of short AMPDU(s) until it is reads the duration of the current Primary channel transmission.
CCA (either ED or ED+PD) with truncated exponential backoff

## Slide 5: Scenario 2: Triggered transmissions when the primary channel is not idle (1)
This case arises at the AP when it triggers multiple non-AP STAs using OFDMA or a non-AP STA using multi-RU allocations and some of the triggered UL PPDUs are not transmitted by the intended non-AP STAs due to failure of CCA or any other reasons
  The CCA failure case arises when the AP mandates CCA in the SIFS gap between the trigger and UL transmission by setting CS Required to 1.
  Multi-RU support in 802.11be can lead to a situation where for example, only one 40 MHz RU of two allocated 40 MHz RUs is occupied.
Spectrum utilization can be improved in the AP regains the unused channels.
However, the AP has to restart transmitting on the unused channel(s) soon enough, in order to satisfy channel occupancy rules of operating within the same TXOP.
As per the current ETSI harmonized standard for 5 GHz, the AP has to reacquire the channel and start transmissions within 25us of the end of the trigger transmission. The decision to transmit can be based on Energy Detection for the last 9us in the 25us gap.

## Slide 6: Scenario 2: Triggered transmissions when the primary channel is not idle (2)
If the AP delays access to the channel beyond 25 us of the end of the trigger, it can do a 25us PIFS CCA to reoccupy the channel. However, a gap > 25us is not permitted by ETSI harmonized standard.
As in the earlier scenario, it is beneficial for the AP to align the end times of such transmissions with the transmission on the primary channel. It is easy for the AP to do so since it is aware of the duration of the ongoing primary channel transmission (since the AP itself transmitted the trigger that set the duration).
An AP capable of simultaneously transmitting and receiving on the used channels and the reacquired channels can do the above
For an AP not capable of transmitting and receiving simultaneously, other mechanisms need to be considered:
  Option 1: Other non-AP STAs in the BSS can detect and utilize the unused channels for TDLS (device-to-device type) transmissions without any consideration of hidden nodes.
  Option 2: The AP can facilitate the usage of the unused channels by initiating the transmission with a trigger for a short duration in order to detect which channels will not be used. Once, the AP observes which channels are not responded on, it follows up with a trigger for the the normal duration only on those channels on which it received a response.
    This subsequent trigger can additionally be modified to indicate which channels the AP is not allocating Uplink.
    This information (or even auto-detection) can be used by the other non-AP STAs to ascertain that those channels are free and transmit on them (say, for TDLS) without creating any hidden node issues within the BSS

## Slide 7
Straw Poll 1
Do you support the following as an option to utilize unused bandwidth in 11be?:
A device can perform full CCA (truncated random exponential backoff) simultaneously on multiple 20MHz channels in its operating bandwidth
  On finding the primary channel as busy through virtual CCA, it can transmit on any combination of channels where the full CCA succeeded and the transmission can be for a duration less than or equal to the duration indicated in the NAV on the primary channel.
  On finding the primary channel as busy through ED, it can transmit on any combination of channels where the full CCA succeeded and the transmission can be for a duration less than or equal to X where X is TBD.
Y/N/A

## Slide 8
Straw Poll 2
Do you support the following as an option to utilize unused bandwidth in 11be?:
On finding the primary channel as busy, a device can perform full CCA (truncated random exponential backoff) on another 20MHz channel of its operating bandwidth
  If the primary channel was detected as busy through virtual CCA and if the full CCA on this other channel is successful, it can transmit on the other channel for a duration less than or equal to the duration indicated in the NAV
  If the primary channel was detected as busy through ED and if the full CCA on this other channel is successful, it can transmit on the other channel for a duration less than or equal to X where X is TBD
Y/N/A