## Slide 1: Improved Secure LTF
Date: 2020-03-02
Authors:

## Slide 2: Entropy of D2.0 Secure LTF Symbol
Entropy of each IEEE 802.11az D2.0 Secure LTF symbol is shown below:
Since secured LTF is transmitted without any coding, there is a high probability that a Rx will NOT receive all the bits correctly
So detection algorithms at Rx will need to specify a lower threshold (≪ 100%), thereby reducing the overall effective entropy of system
Channel BW (MHz) | P | 4P+3 | Entropy (bits)
20 | 7 | 31 | 31
40 | 8 | 35 | 35
80 | 9 | 39 | 39
160 | 10 | 43 | 43

## Slide 3: Random Attacker
An example of how a threshold setting can affect entropy:
An effective entropy of:
  24 bits of 31 bits is equivalent to ~1/600 chance that a random attacker can break the system
  34 bits of 43 bits is equivalent to ~1/11,800 chance that a random attacker can break the system
Note:
  Possible to set a higher threshold, but doing so will reduce effective range of the system
  Also random attack does not consider structure of OFDM waveform
Probability that a random attacker can break secure LTF is not insignificant
Entropy (bits) | Threshold | ⌊Effective Entropy⌋ (bits)
31 | 80% | 24
35 | 80% | 28
39 | 80% | 31
43 | 80% | 34

## Slide 4: Intelligent Attacker
In [1], a more intelligent approach is presented that increases the probability of attacking the secure LTF
  Algorithm exploits: (1) low entropy of secure LTF; (2) inherent structure of the IFFT; and (3) structured Golay sequences which introduces a lot of redundancy
  Golay structure is equivalent to rate 1/15 code
    Possible to recover signal even with most of time domain samples punctured
  Approach allows an attacker to listen to a small portion of LTF symbol, and then predict the remaining samples of LTF symbol with high probability
  Probability that an intelligent attacker can attack the secure LTF is significantly higher!
Conclusion: entropy of secure LTF, as described in D2.0, is too low to protect high value assets, such as laptops, home, cars, etc.
Need a better solution!

## Slide 5
Because of limited entropy, the mapping between LTF sequence and the first few time-domain samples is one-to-one. Therefore, it is possible to estimate the LTF sequence from the first few time-domain samples
LTF Sequence 1
LTF Sequence 2

## Slide 6: Improved Secure LTF (1)
To improve the secure LTF, we must increase the overall entropy each symbol
Proposal:
  As defined in D2.0, zero-padded prefix to prevent against replay attack
  Map approximately 2P+1 random bits onto QPSK
  Map resulting QPSK symbols onto each tone of 2x HE-LTF
  As defined in D2.0, use an additional P random bits to generate a random cyclic shift (CS) per secure LTF
  P = 7, 8, 9, 10 for 20, 40, 80, 160/80+80 MHz, respectively
Key point: proposal eliminates the structured Golay encoding, ensuring that the data mapped on the LTF is significantly more random and has higher entropy

## Slide 7: Improved Secure LTF (2)
Overall entropy for proposal:
Significantly higher entropy – order(s) of magnitude higher
Therefore, much more resistant to attack → better security
Channel BW (MHz) | P | Breakdown of Entropy (bits) | Entropy (bits)
20 | 7 | 2×122 + 7 | 251
40 | 8 | 2×242 + 8 | 492
80 | 9 | 2×498 + 9 | 1005
160 | 10 | 2×996 + 10 | 2002

## Slide 8: Attacker
Same example as before:
An effective entropy of:
  200 bits of 251 bits is equivalent to ~ 1/4,100,000,000,000,000,000,000 chance that a random attacker can break the system
  1601 bits of 2002 bits is equivalent to ~0 chance that a random attacker can break the system
Increased entropy also greatly expands the overall search space, which helps to prevent against attacks from intelligent attackers
Entropy (bits) | Threshold | ⌊Effective Entropy⌋ (bits)
251 | 80% | 200
492 | 80% | 393
1005 | 80% | 804
2002 | 80% | 1601

## Slide 9: PAPR of Secured LTF
PAPR for Golay sequences are comparable to 11ax HE-LTF sequences
PAPR for random QPSK sequences is approximately 5 dB higher than 11ax HE-LTF sequences
Requiring secured ranging to work at the cell edge is not a reasonable expectation
  Unlocking a device from 100 meters away is not a realistic use case
  It should be acceptable for the range of the secured LTF to be less than the cell edge
Trading PAPR for better security is a good technical decision!

## Slide 10: Straw Poll
Do you agree to replace current D2.0 secure LTF with the proposed solution described in slide 6?
Y/N/A: //

## Slide 11: References
[1] 802.11-20/0374r0 Computational Attacks on 11az PHY Secure Ranging