## Slide 1: P-matrix based LTFs for EHT
Date: 2020-03-15
Authors:
Name | Affiliations | Address | Phone | Email
Zoong Doan | Qualcomm |  |  | 
Sameer Vermani |  |  |  | 
Bin Tian |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
In [1], authors show that P-matrix based LTFs work well for Joint Processing multi-AP transmissions (JT)
  To ensure best performance for JT, residual AP-AP CFO needs to be <= 50Hz for the NDP
There were still some concerns about robustness of P-matrix based LTFs to CFO spreads seen across STAs for UL MU-MIMO
  Especially when the number of LTFs grows as streams approach 16
In these slides we show the performance of P-matrix based LTFs for UL MU-MIMO
  Especially the sensitivity to frequency offsets
  Based on our performance evaluation, propose to use P-matrix based LTF design for all spatial multiplexing modes in EHT
    Minimal changes to existing 802.11 LTF design

## Slide 3: Simulation Assumptions
20MHz, D-NLOS channel, 12x16 MIMO
6 users in UL MU-MIMO
  Each user: Nss=2, NTx=2, MCS=9
  CFO spread among users = A Hz
    Half of users have CFO = A/2; the other half have CFO = -A/2
  CP = 1.6usec
  16x16 P-matrix based EHT-LTFs  To mimic longest LTF duration possible (for 16SS case)
    {1x, 2x, 4x} LTFs
  No PA impairment
AP:
  NRx = 16
  No impairments other than CFO
  MMSE receiver, channel smoothing ON
  Phase tracking during EHT-LTFs done using SU pilots in LTF symbols, when ON

## Slide 4: Results for frequency offset tolerance
Observations
  Doing tracking with 1x-LTFs is not a good idea
    Channel interpolation around pilots becomes an issue
    However, even without tracking, start seeing PER floors above 500Hz CFO spread
  For 2x and 4x LTFs, tracking is needed (unless CFO spread is very small) and works pretty well
    Not much difference from the “No CFO tracking curve at the zero CFO point” is seen even at CFO spreads of 1200Hz
General Conclusion
  P-matrix based LTFs work fine with 16LTFs for UL MU-MIMO

## Slide 5: Summary
Analyzed the performance of 16LTF based 12ss UL MU-MIMO to see the sensitivity of P-matrix based LTF design to CFO spreads
  Good robustness to CFOs is seen
Prior contribution [1] has already shown robustness of the P-matrix approach for JT
Recommend adopting the P-matrix based design for all spatial multiplexing modes in EHT

## Slide 6: SP1
Do you agree to adopt P-matrix based modulation of EHT-LTFs for all spatial multiplexing modes (both UL and DL)in EHT?
  All spatial streams are active during EHT-LTFs on every non-zero LTF tone
  Applicable to multi-AP transmission modes as well

## Slide 7: References
[1] Doc 11-20/0075r0, “Performance Comparison of LTF
Designs in JT”, Ron Porat (Broadcom)