## Slide 1: Some Passive Ranging Considerations
Date: 2020-04-01
Authors:

## Slide 2: CIDs 3102 and 3283
CID | Subclause | P.L | Comment | Proposed change | Resolution
3102 | 9.3.1.22.10 | 46.0 | It would make the implementation of "Common Info Subfield" of the Ranging Trigger Variant" simpler and also provide TSF synchronization for the Passive TB Ranging if we align the two cases of Ranging Trigger for non-passive and passive case. | Change the phrase to "and is set only to 0 in non-secure variant of the TB Ranging measurement exchange" | Revised. Make Passive TB Ranging altogether more similar to TB Ranging as described in 11-20/385. [For discussion]
3282 | 9.3.1.22.10 | 46.6 | The Trigger Dependent Common Info subfield of the Ranging Trigger frame of subvariant Passive TB Sounding, depicted in Figure 9-61d.y, is different from the Trigger Dependent Common Info subfield for the Ranging Trigger variant, depicted in Figure 9-61d.x. This subfield is used both the TB and Passive TB Ranging. To reduce the number of options in the standard it would should make these the same. | Change the Trigger Dependent Common Info subfield for the Ranging Trigger variant, depicted in Figure 9-61d.x., to be the same as the Trigger Dependent Common Info subfield of the Ranging Trigger frame of subvariant Passive TB Sounding, depicted in Figure 9-61d.y. | Revised. Make Passive TB Ranging altogether more similar to TB Ranging as described in 11-20/385. [For discussion]

## Slide 3: CIDs 3289
CID | Subclause | P.L | Comment | Proposed change | Resolution
3289 | 9.6.7.49 | 97.13 | The ISTA Passive TB Ranging Measurement Report frame that is used by the ISTA to send its LMR to the RSTA in the Passive TB Ranging case, can probably be merged with the Location Measurement Report frame format. We would however in some way make the frame contain either the content in the Location Measurement Report frame format for the case of non-TB and TB Ranging, or the content in the ISTA Passive TB Ranging Measurement Report frame for the case when that is used by the ISTA to send its LMR to the RSTA in the Passive TB Ranging . However, keep in mind that an idea with the ISTA to RSTA LMR reporting in the Passive TB Ranging case is that the RSTA can copy the whole ISTA Passive TB Ranging Measurement Report element from each ISTA when it broadcasts it in the Secundus RSTA Broadcast Passive TB Ranging Measurement Report frame. Thus it makes sense in the Passive TB Ranging case to contain the report from the ISTA intact in the ISTA Passive TB Ranging Measurement Report element. | As per comment. | Revised. Make Passive TB Ranging altogether more similar to TB Ranging as described in 11-20/385. [For discussion]

## Slide 4: Protocol Choices for Passive TB Ranging
The philosophy for Passive TB Ranging has been to make it as similar to TB Ranging as possible.
Ideally, if TB Ranging is supported we want that a minimum of HW and SW changes to enable support of Passive TB Ranging.
  We especially want to avoid special HW support to be required.
To a large degree this is achieved in 802.11az D2.0, though there are some aspects that may require special support.
Two example aspects that may require special HW support are:
  Sounding Dialog Token in Trigger Dependent Common Info subfield of subvariant Passive Location Sounding
  I2R LMR feedback for Passive TB Ranging
By making Passive TB Ranging more similar to TB Ranging, we could remove the need for special HW support for these features. However, there are a few additional areas in which we can make corresponding changes.

## Slide 5: Possible Passive TB Ranging Specific HW Dependencies
Passive TB Ranging aspects that can require specific HW:
Sounding Dialog Token in Trigger Dependent Common Info subfield
I2R LMR feedback for Passive TB Ranging
RSTA SIFS Broadcast of LMRs
ISTA NDP Transmission

## Slide 6
Sounding Dialog Token in Trigger Dependent Common Info subfield

## Slide 7: Sounding Dialog Token in Trigger Dependent Common Info subfield
The Trigger Dependent Common Info field of the Ranging Trigger frame of subvariant Passive Location Sounding contains the ‘Sounding Dialog Token Number’ whereas for TB Ranging, in the Sounding subvariant, it does not.
Would be good to unify these two cases.
Options:
  Include the Sounding Dialog Token Number also for the TB Ranging case.
  Remove the Sounding Dialog Token Number for the Passive TB Ranging case.
The Sounding Dialog Token Number is included for the Passive TB Ranging case in order to aid PSTAs. It only adds a byte to the subfield. Seems a small compromise to also include it for the TB Ranging case.
Make the two formats the same!

## Slide 8
I2R LMR feedback

## Slide 9: I2R LMR feedback
An ISTA may not without special HW be able to transmit an ISTA Passive TB Ranging Measurement Report frame in response to the RSTA’s Ranging LMR Trigger Frame.
Options:
Make it optional for the ISTA to send I2R LMR feedback for Passive TB Ranging
  The I2R LMR feedback is not strictly needed for Passive TB Ranging.
Allow the ISTA to, as in a TB Ranging exchange, send its LMR to the RSTA in a Location Measurement Report frame, or
For both Passive TB Ranging and RB Ranging exchanges, use a frame that is a unification of the
  Location Measurement Report frame, and the
  ISTA Passive TB Ranging Measurement Report frame
Any of these solutions work!

## Slide 10
RSTA Broadcast of LMRs

## Slide 11: RSTA Broadcast of LMRs
Allow the Primus and Secundus RSTA Broadcast Passive TB Ranging Measurement Report frames to be sent without the SIFS spacing requirement.
  That is, allow these frames to be sent as regular frames with contention - nominally within the availability window reserved for the (Passive) TB Ranging.
However, still recommend to send these frames with SIFS spacings.
Change a ‘shall’ to a ‘should’.

## Slide 12
ISTA NDP Transmission

## Slide 13: Negotiation of ISTA NDP PPDU
Add negotiation of the ISTAs UL Ranging NDP type for Passive TB Ranging exchanges:
  Enable to ISTA to request the UL Ranging NDP type to be
    HE Ranging NDP, or
    HE TB Ranging NDP, or
    No Preference (i.e. the ISTA is OK with responding with either NDP type)
  Allow the RSTA to make the final decision on what UL Ranging NDP type the ISTA shall use.
    If the ISTA can send an HE Ranging NDP, then the RSTA should select that.

## Slide 14: Restriction on ISTAs HE TB Ranging PPDU
Allow the RSTA to announce a restriction on ISTAs Passive TB Ranging UL NDP HE TB PPDU type in the in the RSTA Availability Window element in its beacon frame.
This makes it simpler for a PSTA to receive the ISTAs HE TB Ranging NDPs as it can preprogram the parameters required for receiving the HE TB PPDU (that are not contained in the HE TB PPDU itself).
RSTA only need to restrict the number of space-time-streams, N_sts, in the HE TB PPDU.

## Slide 15
PSTA reception of restricted HE TB PPDU

## Slide 16: PSTA reception of restricted HE TB PPDU
To receive an HE TB PPDU, the Rx PHY needs to be preconfigured with some PPDU parameters that are not contained in the HE TB PPDU itself. These are normally are specified in the TXVECTOR for the preceding transmitted trigger frame.
These parameters are conveyed on the one hand to the Rx PHY of the RSTA transmitting the trigger frame and in the trigger frame itself transmitted to an ISTA.
For the PSTA to receive the HE TB PPDU, it normally need to take the parameters from the preceding trigger frame and pass those parameters on to its Rx PHY.
This is a quick turnaround from receiving a frame and using its decoded content for the reception of the next PPDU. This may require specialized HW.
When the format of the HE TB PPDU is restricted the PSTA can ahead of time pass those parameters to its Rx PHY.
For example, the parameters to receive an HE TB PPDU ranging can be passed to the PSTA’s Rx PHY when it enters the availability window for the (Passive) TB Ranging, as it here is not required to be able to receive any other HE TB PPDUs.

## Slide 17
Merging Passive and Active Ranging

## Slide 18: Merging Active and Passive Ranging
Another way to make Passive TB Ranging more similar to TB Ranging can be to make Passive TB Ranging an exchange variant within the TB Ranging protocol, rather than as in D2.0, being a separate protocol.
This has the additional advantage in that it can enable new ranging use cases.
This is completely doable. Requires a few but well defined text changes.

## Slide 19
Making Passive TB Ranging part of TB Ranging

## Slide 20: Making Passive TB Ranging part of TB Ranging – 1(2)
Passive TB Ranging, though very similar to TB Ranging, is a ranging protocol of its own.
Rather than having Passive TB Ranging be a separate ranging protocol, we could make Passive TB Ranging exchanges variant exchanges within the TB Ranging protocol.
An ISTA would request a Passive TB Ranging exchange within an RTSA’s TB Ranging exchange. (The RSTA would select which TB Ranging occurrence to place the ranging in.)
If Passive TB Ranging exchanges are present, the broadcasting of the Primus and Secundus RSTA Broadcast Passive TB Ranging Measurement Report frames would be added at the end of the TB Ranging frame sequence.

## Slide 21: Making Passive TB Ranging part of TB Ranging – 2(2)
When serving Passive TB Ranging exchanges, the RSTA includes a Passive TB Ranging Availability Window element in its beacon frame body such that stations that only listen, passive STAs or PSTAs, can get information about when the Passive TB Ranging exchanges occur.
With Passive TB Ranging exchanges being part of a regular TB Ranging exchange sequence, the ISTAs performing Passive TB Ranging exchanges would (optionally) measure and report the TOAs of the ranging NDPs from other ISTAs participating in the same TB Ranging exchange sequence and themselves performing Passive TB Ranging exchanges.

## Slide 22
Combined Active and Passive Ranging

## Slide 23: Combining active and passive ranging
By combining ‘active’ ranging and passive ranging, or Passive TB Ranging exchanges, new modes of operation and use cases can be achieved.
Examples of such use cases are:
Active Passive Ranging:
  Mobile client STA, to be located, joins RSTAs (Passive) TB Ranging opportunity as an ISTA.
  Mobile client STA is able to do ‘active’ ranging exchanges with the RSTA as well as client anchor stations participating in the Passive TB Ranging exchange.
  Enables active ranging to a set of anchor client STAs in a very compressed amount of time.
  This type of ranging service can already be provided within the Passive TB Ranging protocol.
Combined active and passive ranging:
  An RSTA could have a couple of client anchor station participating in its (Passive) TB Ranging.
  A mobile client STA to be located could then chose to
    Perform passive ranging by only listening to the exchanges between the RSTA and the ISTAs performing Passive TB Ranging exchanges
      This leaves the mobile client STA completely anonymous
    Join as an ISTA performing Passive TB Ranging exchanges with the RSTA and the other ISTAs performing Passive TB Ranging exchanges
    Join as an ISTA performing TB Ranging exchanges, possibly secure, and also perform passive ranging by listening to the exchanges between the RSTA and the ISTAs performing Passive TB Ranging exchanges.
  By enabling a couple of client anchor STAs to participate in the (Passive) TB Ranging exchange the flexibility of the ranging services can be greatly increased.
  This type of ranging service can already be provided with separate Passive TB Ranging and TB Ranging sessions, though there might be some benefits in merging the two protocols.

## Slide 24: Active Passive Ranging
Client STA to be located – mobile ISTA
Access Point - RSTA
Example Scenario
Anchor Client - ISTA
Anchor Client - ISTA
Anchor Client - ISTA

## Slide 25: (Passive) TB Ranging used for Active Passive Ranging
DL
NDP
UL
NDP
TF
Responder STA
Client Anchor InitiatorSTA 1
Mobile
Initiator
STA 2
(to be located)
UL
NDP
UL
NDP
DL
NDPA
Green arrows – Regular ranging frame exchanges
Blue arrows – Extra listening opportunities
Poll
TF
PR
PR
ISTA to RSTA
LMR
TF
RSTA to
ISTA
LMR
UL
NDP
TF
ISTA to RSTA
LMR
Frame
1
Frame
2
Frames in TB Ranging protocol
Extra frames for Passive Location Ranging Protocol
ISTA to RSTA
LMR
LMR broadcasting
(Details TBD)
Enables client station receiving the NDPs and LMR reporting to calculate its location using TDOA relations.

## Slide 26: Combined Active and Passive Ranging
Client STA to be located – mobile ISTA
Access Point - RSTA
Example Scenario
Anchor Client - ISTA
Anchor Client - ISTA
Anchor Client - ISTA
Active ranging (Possibly secure?)
Passive ranging reception
(Not all marked)

## Slide 27
Straw Polls

## Slide 28: Straw Poll 1
Do you support making Passive TB Ranging more similar and a little more flexible in order to make it easier to enable Passive TB Ranging when TB Ranging is supported?
Y: N: A:

## Slide 29: Straw Poll 2
Do you support including the Sounding Dialog Token Number in Trigger Dependent Common Info field for the Sounding subvariant?
Y: N: A:

## Slide 30: Straw Poll 3
Do you support using one of the options in slide 9 in 11-20/385r3 for ISTA LMR reporting to make it easier to support Passive TB Ranging? (To start with we can make ISTA LMR reporting optional.)
Y: N: A:

## Slide 31: Straw Poll 4
Do you support allowing the Primus and Secundus RSTA Broadcast Passive TB Ranging Measurement Report frames to be sent without the SIFS spacing requirement?
Y: N: A:

## Slide 32: Straw Poll 5
Do you support adding flexibility for the ISTA’s Ranging NDP transmission along the lines described in slides 12-16 in 11-20/385r3?
Y: N: A:

## Slide 33: Straw Poll 6
Do you support making Passive TB Ranging part of TB Ranging, i.e. simply allow Passive TB Ranging exchanges in the TB Ranging protocol?
Y: N: A:

## Slide 34
Supplemental Material

## Slide 35
HE TB PPDU Parameters

## Slide 36: Missing HE-SIG-A parameters in an HE TB PPDU as compared to an HE SU PPDU
Beamchange – Set to 0
UL/DL – Set to ‘UL’
HE-MCS – Irrelevant for NDP
DCM – Irrelevant for NDP
GI+LTF size – Conveyed in TF – However the LTF type and GI size is already restricted for HE TB Ranging NDPs in 802.11az draft 2.0.
NSTS and Midamble Periodicity – Conveyed in TF – Midamble Periodicity is irrelevant for NDP.
Coding – Irrelevant for NDP

## Slide 37: Missing HE-SIG-A parameters in an HE TB PPDU as compared to an HE SU PPDU
LDPC Extra Symbol Segment – Irrelevant for NDP
STBC – Irrelevant for NDP
Beamformed – Irrelevant for NDP
PE Disambiguity – Irrelevant for Ranging NDP reception.
Doppler – Irrelevant for NDP

## Slide 38: Parameters for HE TB PPDU reception in Trigger Frame - 1(2)
UL Length - L-SIG Length field in HE TB PPDU – This parameter also controls the packet extension used.
CS Required – Would have to preset this to zero
UL BW – Is also in the HE TB PPDU HE SIG A field
GI And LTF Type – For an HE TB Ranging NDP this is already restricted to 2x HE-LTF and 1.6 us GI in 802.11az D2.0.
MU-MIMO LTF Mode – For an HE TB Ranging NDP for Passive TB Ranging we can restrict this to HE single stream pilot HE-LTF mode.
Number Of HE-LTF Symbols And Midamble Periodicity – Allow the RSTA to restrict the number of HE-LTF symbols in the HE TB Ranging PPDUs and announce it in the beacon frame. The Midamble Periodicity is irrelevant for an HE TB Ranging NDP.

## Slide 39: Parameters for HE TB PPDU reception in Trigger Frame - 2(2)
UL STBC – Irrelevant for NDP
LDPC Extra Symbol Segment – Irrelevant for NDP
AP Tx Power – Irrelevant for PSTA reception
Pre-FEC Padding Factor – Irrelevant for NDP
PE Disambiguity – Irrelevant for reception of an HE TB Ranging NDP.
UL Spatial Reuse – Preset to all zeros = No spatial reuse for an HE TB Ranging NDP for Passive TB Ranging.
Doppler – Irrelevant for NDP

## Slide 40: PSTA Preprogramming of PPDU parameters for reception of an HE TB Ranging NDP - 1(2)
The idea is that the RSTA restricts the format of the HE TB Ranging NDP, e.g. restricts the number of spatial streams, and announces this restriction it its beacon frame.
The PSTA can then preprogram its PHY to fill in the missing Rx parameters for the HE TB PPDU to match the specific restriction. This pre-programming for reception of HE TB PPDU’s is likely to be similar to the preprogramming an AP or SAP does when it send out a trigger frame to receive an HE TB PPDU. With some luck the PSTA can with existing HW comply with this, or it may only need to make smaller changes in its HW to be able to comply with this.

## Slide 41: PSTA Preprogramming of PPDU parameters for reception of an HE TB Ranging NDP - 2(2)
HE TB PPDU Rx parameter preprogramming:
Beamchange – Set to 0. (No beamforming on a Ranging NDP.)
UL/DL –Set to ‘UL’
HE-MCS –Irrelevant for NDP
DCM –Irrelevant for NDP
GI+LTF size –Preset to a GI size of 1.6 us and LTF size matching the restriction announced by the RSTA.
NSTS (and MidamblePeriodicity) – Preset N_sts to match the restriction announced by the RSTA. The MidamblePeriodicity is irrelevant for NDP.
Coding –Irrelevant for NDP
LDP Extra Symbol Segment –Irrelevant for NDP
STBC –Irrelevant for NDP
Beamformed–Irrelevant for NDP
PE Disambiguity–Irrelevant for Ranging NDP reception.
Doppler –Irrelevant for NDP.

## Slide 42
Thank You!