## Slide 1: Multi-link Association Follow Up
Date: 2020-03-16
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Agreement on multi-link setup
802.11be defines a multi-link setup signaling exchange executed over one link initiated by a non-AP MLD with an AP MLD as follows:
  Capability for one or more links can be exchanged during the multi-link setup.
  The AP MLD serves as the interface to the DS for the non-AP MLD after successful multi-link setup
    NOTE 1 – The link identification is TBD.
    NOTE 2 – Details for non-infrastructure mode of operation TBD.
802.11be shall define a mechanism to teardown an existing multi-link setup agreement.

## Slide 3: Introduction
In this contribution, we discuss about re-association process for a MLD.

## Slide 4: Background: Re-association
In current standard, a reassociation process is defined for a single-link STA.
  The reassociation service is invoked to “move” a current association of a non-AP STA from one AP to another.
    In an Extended Service Set (ESS) with Distribution System (DS), the reassociation service informs the DS of the current mapping between AP and STA as the STA moves from Basic Service Set (BSS) to BSS within the ESS.
    Reassociation also enables changing association attributes of an established association while the non-AP STA remains associated with the same AP.
  Reassociation is always initiated by the non-AP STA.

## Slide 5: Multi-link resetup for a MLD
Similar to a single link STA, we expect that reassociation (or multi-link resetup) process is needed for a non-AP MLD:
  When the non-AP MLD moves from a multi-link setup with an AP MLD to another AP MLD.
  When the non-AP MLD changes association (multi-link setup) attributes of an established association while the non-AP MLD remains associated with the same AP MLD.

## Slide 6: Frame exchange for multi-link resetup
Assuming multi-link resetup process is similar to reassociation process for a single link STA, we can have two options:
  Use of Reassociation Request/Response frames for multi-link resetup
    Additional elements regarding multi-link attributes need to be added to conventional Reassociation Request/Response frames
  New Request/Response frames can be defined for multi-link resetup
Considering that frames for multi-link setup, teardown have not been decided yet, it’s better to discuss frames for multi-link resetup together with them.

## Slide 7: Current AP Address
During multi-link resetup process, a non-AP MLD needs to indicate current AP MLD ID to new AP MLD.
  In current Reassociation Request frame for single link STA, Current AP Address field indicates the MAC address of the AP with which the STA is currently associated.
    This address is used for a target AP to identify a source AP with which the STA is currently associated.
  For multi-link resetup case, as there are one or more APs affiliated with the source AP MLD, we believe it is reasonable to use a unique AP MLD MAC address for the Current AP Address field.

## Slide 8: Transition to single link AP
If a non-AP MLD that multi-link is setup with an AP MLD moves to a single link AP (that does not support multi-link operation):
  Conventional Reassociation Request/Response frame exchange is needed.
  Similar to multi-link resetup, the AP MLD MAC address can be used for the Current AP Address field of the Reassociation Request frame.

## Slide 9: Conclusions
We discussed the need for reassociation process corresponding to multi-link operation.

## Slide 10: SP1
Do you agree to add the following to 11be SFD:
  TGbe shall define a multi-link resetup mechanism to resetup with another AP MLD or changing configuration of existing multi-link setup with an AP MLD.
    Reassociation Request/Response frame is used for this purpose.

## Slide 11: SP2
Do you agree to add the following to 11be SFD:
  When a non-AP MLD that has multi-link setup with current AP MLD sends a Reassociation Request frame to a new AP MLD, AP MLD MAC address of the current AP MLD is used in Current AP Address field of the frame.

## Slide 12: SP3
Do you agree to add the following to 11be SFD:
  When a STA of a non-AP MLD that has multi-link setup with current AP MLD sends a Reassociation Request frame to a new AP that is not affiliated with an AP MLD, AP MLD MAC address of the current AP MLD is used in Current AP Address field of the frame.
  Note: Only the STA that sends the Reassociation Request frame can associate with the new AP.