## Slide 1: Beacon, Capability, Operating Parameters
Date: 2020-03-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Multi-band Operation
An STA MLD associates with an AP MLD through one association.
  Common capabilities (capability applying to all bands), per band capabilities.
  Common operation parameters, per band operation parameters.
  Operation Negotiation (BA, security, channel switch, BW update etc.)
    Common operation negotiation (single negotiation applying to all bands), per band operation negotiation.
  UP layer interface:
    No change to MAC data service specification,
    MLME SAP primitives may be changed for per band MLME SAP primitives.

## Slide 3: Capability and Operation Parameters of Other Link
An AP/STA MLD may have different capability in different links.
An AP MLD may announce different operating parameters for different links.
The elements without link indication are the elements announced for the link where the frame is transmitted.
An element for other link has link identifier to indicate the link.
The following is the possible other link element format example 1:
Element ID = 255
Element ID Extension present
Length
Element ID Extension
Other Link related IE
Link ID
1 octet
1 octet
1 octet
1 octet
subelements
variable
Subelement ID
Length
Subelement ID Extension
1 octet
1 octet
0 or 1 octet
Information
variable
Subelement
Other Link Related element
Subelement Id can be same as Element ID for the same Information format, e.g. EDCA Parameter Set subelement has Subelement ID 12 which is same as Element ID of EDCA Parameter Set element.
Another example is to add link ID to the respective element.
  No suitable to non-extensible element.
  Multiple elements with same element ID.

## Slide 4: Subelements in Other Link Related Element
When multiple Other Link Related elements are needed to carry the subelement, the following conditions should be satisfied:
  A subelement is not in more than one Other Link Related element, i.e. a subelement can’t be fragmented.
  If a subelement can be fit in the current Other Link Related elements, i.e. after aggregating the subelement, the Other Link Related element is not more than the maximal length indicated by Length field, the subelement can’t be put in a new Other Link Related element.
Element ID = 255
Length
Element ID Extension
Link ID
subelements
Subelement ID
Length
Information
Subelement 1
Other Link Related element 2
Element ID = 255
Length
Element ID Extension
Link ID
subelements
Other Link Related element 1
Subelement ID
Length
Information
Subelement n
255 octets
Subelement ID
Length
Information
Subelement n+1
Subelement ID
Length
Information
Subelement n+2

## Slide 5: Non-inherited Element
the capabilities, operating parameters of the first link are not transmitted by the management frame in the second link instead those capabilities, operating parameters of the first link are inherited from the second link.
An Other Link may not want to inherit an element from the link that transmit the element in a management frame even if the related element is not defined in Other Link Related element.
  To help this, a Non-inherited Element subelement, e.g. the element for multiple BSSID feature, is used.
If an Element ID and Element ID Extension, if exists, are included in Non-inherited Element subelement of a other link, the element identified by the Element ID and Element ID Extension, if exists, is not inherited by the other link.
Element ID = 255
Element ID Extension present
Length
Element ID Extension
Uninherited element indicator
Link ID
1 octet
1 octet
1 octet
1 octet
subelements
variable
Subelement ID=255
Length
Subelement ID Extension
1 octet
1 octet
1 octet
Information
variable
Subelement
Other Link Related element
Element ID
Element ID Extension
1 octet
0 or 1 octet
Element ID
Element ID Extension
1 octet
0 or 1 octet

## Slide 6: Beacons in part of links of Multi-link AP/STA Entity
If no Beacon frames are transmitted in a link, the Capabilities, Operating parameters of the link are announced in another link where Beacon frame are transmitted.
If a multi-link AP entity transmits Beacons in link1 of the multi-link AP entity and link2 of the multi-link AP entity, the following information announcement rules are applied:
  In Beacon frames of link2, the information for frame exchange of link1, e.g. the Capabilities, Operating Parameters, e.g. EDCA, MU EDCA, OFDMA random access parameters, Spatial Reuse parameters, BSS Operating Parameters etc. of link1 are not announced.
  In Beacon frames of link2, the information for receiving Beacons of link1, helping the association decision, e.g. the Primary channel, BW, TSF Difference between Two Link (or TSF Time), link1 AP and link2 AP being affiliated with an AP MLD, Check Beacon etc.
    A new element or updating the current element e.g. RNR can be defined for such announcement.

## Slide 7: Capabilities, Operating Parameters in Scanning, Association, and Other Management frame
The Probe Request/Response carry the capabilities and BSS operating parameters in other links.
  Probe Request indicates the requirement of other link’s capabilities, operating parameters explicitly or implicitly (Probe Request carries the capabilities of other link ).
The Association Request and Association Response in one link need to carry the capabilities and BSS operating parameters in other links.

## Slide 8: Straw Poll 1
Do you support to define an element transmitted in one link to carry the information of other link as the subelements in the defined element?

## Slide 9: Straw Poll 2
Do you support that an AP of the AP MLD transmits Beacons in link1 carries the partial information of another AP affiliated with the same MLD in link2?

## Slide 10: Straw Poll 3
Do you support that in Probe Request/Response, (Re)Association Request/Response frame transmitted in one link, the capabilities, operating parameters of multiple links can be carried?
  Probe Request can indicate whether it want other link’s information.
  Note: the indication can be implicit indication

## Slide 11: Straw Poll 4
Do you support to use the inheriting mechanism of 11ax such that if the capabilities, operating parameters of the first link are not transmitted by a management frame in the second link, those capabilities, operating parameters of the first link are inherited from the capabilities, operating parameters in the management frame of the second link?

## Slide 12: Straw Poll 5
Do you support to use the Non-inherited mechanism of 11ax to announce the elements that are not inherited from the link where the elements are transmitted in a management frame?