## Slide 1: MLO BSS Information Transmission and Multiple BSSID Support
Date: 2020-03-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Multiple BSSID
A single-radio AP device can own multiple virtual APs:
  Only one AP that has transmitted BSSID transmits management frame frames. The BSSIDs of the other APs are non-transmitted BSSID.
  The Multiple BSSID element defines the non-transmitted BSSID profiles for APs that have non-transmitted BSSIDs.
  The non-transmitted BSSID can be figured out through the Multiple BSSID element.
  Multiple BSSID Configuration element defines the actually number of non transmitted BSSID APs.
  The non-transmitted profile of a non-transmitted BSSID in the management frame doesn’t need to carry an element of the AP’s capabilities or operating parameters that is same as the related element of the transmitted BSSID.
    One example is that if the EDCA Parameter Set element is not in the non-transmitted BSSID profile of an AP with non-transmitted BSSID ( e.g. AP2), the EDCA Parameter Set element in the management frame will be used by the STAs associated with AP2.
  An AP with non-transmitted BSSID may announce the non-inheritance of element from the AP with transmitted BSSID.
    One example is that in non-Transmitted BSSID Profile of non-transmitted BSSID1, if the Element ID of EDCA Parameter Set is in List Of Element IDs field, the EDCA Parameter Set element in the management frame will not be used by the STAs associated with AP of BSSID1.
BSSID1,
BSSID2
BSSID3,
BSSID4
Multiple BSSID AP
Transmitted BSSID
Multiple BSSID element
Multiple BSSID Configuration element
Non-inherit element

## Slide 3: Recap: AP MLD
An AP multi-link device (MLD) includes multiple APs:
  Each AP works in different link.
  All the APs share the same security policy, BA agreement, SSID, same MAC SAP.
  The APs have different medium access procedures.
  Each AP may transmit its own management frames with different TSF time, BI, TBTT etc.
  When an AP of an AP MLD transmits a management frame in link1, the management frame doesn’t need to carry a element of another AP’s capabilities or operating parameters in link2 if the element is same as the related element in link1.
  In a management frame of link1, the information of an AP in link2 may not include an element of the specific capabilities or operating parameters, and the AP in link2 doesn’t want to inherit the related element in link1
    The non-inherit Information (identified by the Element ID, Element ID Extension) can be announced to let the STAs associated with the AP in link2 know the element that are not inherited from the AP that transmitted the management frame in link1.
  The AP MLD transmits buffered frame indication of one link in another link.
    The buffer indication of the other link takes effect right away or after the following TBTT of another link.
      No indication about whether this applied to unicast or group-addressed frames. This may not be applicable to group addressed frames.
Multi-link AP device
MAC with Addr1
MAC with Addr2
Common MAC
Link1
Link2
SAP of BSSID1 (addr1)
BSSID1’s management frame
capabilities, operation parameters of AP with BSSID1
ML element with Link ID, SAP Addr, capability, operation parameters of AP with BSSID2
RNR

## Slide 4: Number of AP MLD with Multiple BSSID in Multiple Links
It is not required that when one link implements multiple BSSID, another link also needs to implement multiple BSSID.
  5GHz legacy STAs, 6GHz HE STAs, and 5GHz + 6GHz STA MLDs
When two links implement multiple BSSID, the following are the relationship of them:
  Option 1:
    If an AP in a link that is affiliated with an AP MLD has transmitted BSSID, the AP in another link that is affiliated with the same AP MLD is the transmitted BSSID.
      Option 1.1: The Multiple BSSID elements in different links define the same number of non-transmitted BSSIDs.
      Option 1.2: The Multiple BSSID elements in different links define the different number of non-transmitted BSSIDs.
  Option 2:
    If an AP in a link that is affiliated with an AP MLD has transmitted BSSID, the AP in another link that is affiliated with the same AP MLD can be a non-transmitted BSSID.
      Option 2.1: The Multiple BSSID elements in different links define the same number of non-transmitted BSSIDs.
      Option 2.2: The Multiple BSSID elements in different links define the different number of non-transmitted BSSIDs.
We prefer option 2.2.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)

## Slide 5: BSS Parameter Transmission Method of AP MLD with Multiple BSSID
This method assume that the transmitted BSSIDs of multiple links can be affiliated with different AP MLDs.
The method to transmit BSS parameters:
  APxa’s capabilities and operating parameters
  APxa’s non-transmitted BSSID profiles of the non-transmitted BSSIDs in link_x
    each non-transmitted BSSID profile of link_x’s APxb includes the capabilities, operating parameters of link_y’s APyb where APxb and APyb are owned by same AP MLD
  the AP capabilities and BSS operating parameters of transmitted BSSID AP (APyb) in link_y.
  RNR is used for non-EHT STAs and most basic AP MLD announcement.
    The link identifier (MLD ID + Link ID) in RNR and ML element defines the match between RNR and STA Profile in ML element.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.
AP11’s Beacon
Non-transmit BSSID Profiles subelement for AP12, AP13, AP14. ML elements related to AP12, AP13, AP14
Elements for AP11’s capabilities, operating parameters
ML element with Link ID, SAP Addr, capability, operation parameters of AP 21
RNR

## Slide 6: BSS Parameter Transmission Method of AP MLD with Multiple BSSID
The method to inherit the parameters:
  APs affiliated with the same AP MLD as the non-transmitted BSSID AP inherit from the non-transmitted BSSID AP and then inherit from the AP that transmits the Beacon.
  APs affiliated with the same AP MLD as the transmit AP inherit from the AP that transmits the Beacon.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
AP11’s Beacon
Non-transmit BSSID Profiles subelement for AP12, AP13, AP14. ML elements related to AP12, AP13, AP14
Elements for AP11’s capabilities, operating parameters
ML element with SAP Addr, STR/NSTR capability per pair of links, STA Profile (Link ID, capability, operation parameters) of AP 21
RNR

## Slide 7: BSS Parameter Transmission Method of AP MLD with Multiple BSSID (Cont’d)
The AP MLD reported by RNR may not include AP in the reporting link, e.g. AP MLD with addr34 SAP address.
The reporting method of such AP MLD:
  AP’s report with the announcement of belonging to AP MLD through RNR only.
    AP MLD report without MLD common info and STA profile. The MLD ID + Link ID can be BSSID Index + Link ID.
  AP’s report with ML element.
    More than one ML elements exist in the Management frame. The MLD ID + Link ID can’t be BSSID Index + Link ID.
  The rule could be
    If an MP MLD has an AP in the link where the management frame is transmitted, the ML element with Common Info and STA profile for the AP MLD is included in the Management frame. Otherwise the RNR is used to announce the AP MLD.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (A34)
MAC with Addr24 (AP24)
Common MAC
Link3
Link2
SAP of BSSID34 (addr34)
AP11’s Beacon option 1
Non-transmit BSSID Profiles subelement for AP12, AP13, AP. ML IEs related to AP12, AP13,
Elements for AP11’s capabilities, operating parameters
ML element with Link ID, SAP Addr, capability, operation parameters of AP 21
RNR for AP21 to AP24
AP11’s Beacon option 2
Non-transmit BSSID Profiles subelement for AP12, AP13, AP. ML IEs related to AP12, AP13,
Elements for AP11’s capabilities, operating parameters
ML element with Link ID, SAP Addr, capability, operation parameters of AP 21
RNR for AP21 to AP24
ML element of AP24

## Slide 8: Straw Poll 1
Do you support that it is not required that when one link implements multiple BSSID, another link also needs to implement multiple BSSID?

## Slide 9: Straw Poll 2
Do you support that if an AP in a link that is affiliated with an AP MLD has transmitted BSSID, the AP in another link that is affiliated with the same AP MLD is not required to be the transmitted BSSID?

## Slide 10: SP 3
Do you agree that AP’s Beacon and probe response shall not include ML element for MLD with no affiliated APs operating on this link?

## Slide 11: SP 4
Do you support that the MLD ID and the Link ID of an AP carried in the TBTT information field in the RNR is used to identify to which AP MLD the reported AP is affiliated to and to match the information of the same AP in an ML element?
  The MLDID is unique in the frame on which it is carried
  For APs that are in the same AP MLD as an AP1 (transmitted or non-transmitted BSSID) in the same multiple BSSID as the reporting AP, the MLDID of the AP MLD is set to the BSSID-index of AP1
  it’s TBD if we define the way to provide information for APs that belong to other MLDs not part of any MLDs in the multiple BSSID set of the reporting AP