## Slide 1: U-SIG and SIG Contents
Date: 2020-03-13
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction and Recap
Several contributions regarding U-SIG and EHT-SIG Contents have been discussed.
The contributions can be divided into two categories:
  Unified PPDU format for SU and MU transmission
    Pro: unified Rx procedure
    Con: EHT-SIG will be more than one symbol for MCS0
      [2] proposes a semi-unified proposal, which allows a format that allows one symbol EHT-SIG, whilst we do think some important signaling is missing.
  Separate PPDU format for SU and MU transmission
    Pro: low overhead for EHT-SIG for SU transmission
    Con: separate contents for SU and MU transmissions.

## Slide 3: Proposed SIG structure
In this proposal, we will propose a specific SIG design, which allows one symbol EHT-SIG and carry enough signaling bits for EHT SU transmission.
The U-SIG and EHT-SIG for SU transmission are divided into two parts: the first part carries common SU & MU SIG contents, the second part carries the info in non-MU-MIMO user specific field.

## Slide 4: Specific Contents in U-SIG and EHT-SIG
The detailed info is shown as below:
Bit | Field | Number
B0-B2 | Version Identifier | 3
B3 | DL/UL | 1
B4-B9 | BSS Color | 6
B10-B16 | TXOP | 7
B17-B22 | Bandwidth | 4~6 (set to 6 as example)
B23-B24 | PPDU Format | 2
B25 | STBC | 1
U-SIG1 (SU&MU)
Bit | Field | Number
B0 | Spatial Reuse | 2
B1 |  | 
B2 | GI+EHT-LTF | 2
B3 |  | 
B4 | LDPC Extra Symbol Segment | 1
B5 | PE Disambiguity | 1
B6 | Pre-FEC Padding Factor | 2
B7 |  | 
B8-B12 | Number of EHT-SIG Symbols or MU-MIMO users | 5
B13-B15 | EHT-SIG MCS and DCM | 3
B16-B19 | CRC | 4
B20-B25 | Tail | 6
U-SIG2 (MU)
Bit | Field | Number
B0 | Spatial Reuse | 2
B1 |  | 
B2 | GI+EHT-LTF | 2
B3 |  | 
B4 | LDPC Extra Symbol Segment | 1
B5 | PE Disambiguity | 1
B6 | Pre-FEC Padding Factor | 2
B7 |  | 
B8-B15 | AID-Part 1 (8 bit) | 8
B16-B19 | CRC | 4
B20-B25 | Tail | 6
U-SIG2 (SU)
 | Field | Number
B0 | Number of EHT-LTF Symbols And Midamble Periodicity+Doppler | 4
B1 |  | 
B2 |  | 
B3 |  | 
 | RU allocation subfield/preamble puncture indication | 8*N
 | Center 26-tone RU | 2/0
 | AID | 11
 | … | 
 | Beamformed | 1
EHT-SIG CC1
(MU)
 | Field | Number
B0-B2 | AID-Part 2 (3bit) | 3
B3-B7 | NSTS+Doppler | 5
B8-B11 | MCS | 4
B12 | DCM | 1
B13 | Beam change | 1
B14 | Coding | 1
B15 | Beamformed | 1
B16-B19 | CRC | 4
B20-B25 | Tail | 6
EHT-SIG CC1
(SU)

## Slide 5: Specific Contents in U-SIG and EHT-SIG
The SU & MU structures are highly aligned, the only difference are some EHT-SIG symbol or MCS signaling, which leads to high overhead and not necessary for SU transmission.
  The proposed method offers 2 bit PPDU format for potential R2 features (e.g. HARQ):
    DL: 00-SU, 01-MU non-OFDMA, 10-MU OFDMA, 11 reserved;
    UL: 00-SU, 01-TB, 10 reserved, 11 reserved.
  The proposed method offers 2 bit SR field
  Number of EHT-SIG Symbols or MU-MIMO users is extended to 5 bits

## Slide 6: Summary
The proposed method is highly unified, low overhead.
The proposed method can be used for both non-punctured and punctured SU transmission if the BW signals the punctured pattern or separate preamble puncture indication is signaled. Or the proposed can be used only for non-punctured case. For punctured case, can use the format for MU transmission.

## Slide 7: Straw Poll #1
Do you agree to have at least one EHT PPDU format that has only one EHT-SIG symbol with MCS 0?
  The EHT PPDU is intended to single user only
  Y
  N
  A

## Slide 8
[1] 11-20-0049-01-00be-ppdu-types-and-u-sig-content
[2] 11-20-0285-00-00be-su-ppdu-sig-contents-considerations
[3] 11-20-0031-02-00be-considerations-on-eht-ppdu-formats
[4] 11-20-0029-03-00be-preamble-structure-and-sig-contents
[5] 11-20-0019-01-00be-11be-ppdu-format
[6] 11-20-0087-00-00be-discussions-on-u-sig-content-and-eht-sig-format
References