## Slide 1: Further Proposals for Multiple RU Aggregation
Date: 2020-03-16
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
Various combinations for multiple RU aggregation were proposed [1]-[5]
TGbe approved some of the small and large RU aggregation
  For small RU aggregation, only 26+52 and 26+106 were allowed
  For large RU aggregation, only a few combinations were allowed in each OFDMA and non-OFDMA
In this contribution, we propose further combinations
  For small RU aggregation, we propose to combine middle or center 26-tone RU with other adjacent RUs
  For large RU aggregation, we propose several combinations which can support various puncturing patterns in non-OFDMA

## Slide 3: Small RU Aggregation
Middle and center 26-tone RUs may be useless in 11ax
  They are not expandable to larger size RUs and are vulnerable to DC offset
With multiple RU aggregation, we can make them more useful
  Throughput can be enhanced
  Better frequency diversity can be expected
For simple scheduling and low signaling overhead, we propose to combine only two adjacent RUs
  Middle 26-tone RU + adjacent 52/106-tone RU in each 20MHz channel
  Center 26-tone RU + adjacent 52/106-tone RU in each 80MHz channel
    E.g.,

## Slide 4: Large RU Aggregation
We focus on the non-OFDMA case in conjunction with preamble puncturing
Only a few conditional mandatory combinations were agreed
  It is hard to expect high efficiency because there are too many possible puncturing patterns that the agreed combinations cannot support
We propose further combinations which can cover diverse puncturing patterns
  As to the size of the punctured channel, 20MHz, 40MHz, and 60MHz can be considered given incumbent bandwidths in 6GHz [2][4]
  In a wide bandwidth, we also deal with 80MHz punctured channel to reduce the number of RU combinations

## Slide 5: Large RU Aggregation in 80MHz
Determined options
  60MHz with one 20MHz punctured channel
    484+242 (4 options)
It would be better to support all puncturing patterns
  Throughput is severely affected by the supportable patterns for a narrow bandwidth in particular
  Signaling overhead does not increase too much because only four options are left
Further proposed options
  40MHz with two 20MHz punctured channels
    242+242 (4 options)
 Without these options, only 20MHz transmission is possible in some cases while we can achieve about a maximum twofold increase in throughput by allowing these options

## Slide 6: Large RU Aggregation in BW ≥ 160MHz (1/4)
Determined options
  140MHz with one 20MHz punctured channel
    (242+484)+(996) (8 options)
  120MHz with one 40MHz punctured channel
    (484)+(996) (4 options)
  200MHz with one 40MHz punctured channel
    (484)+(996)+(996) (6 options)
  160MHz with one 80MHz punctured channel
    (996)+(996) (3 options)
  280MHz with one 40MHz punctured channel
    (484)+(996)+(996)+(996) (8 options)
  240MHz with one 80MHz punctured channel
    (996)+(996)+(996) (4 options)
160MHz
240MHz
320MHz
Note that () means the RU combination used in each 80MHz channel

## Slide 7: Large RU Aggregation in BW ≥ 160MHz (2/4)
We assume that an incumbent channel is located across two 80MHz channels
  Given the main incumbent bandwidths [2][4], 40MHz / 60MHz channel should be punctured in the boundary between two 80MHz channels
    E.g., 160MHz bandwidth
  Determined options in the previous slide cannot support these puncturing patterns, and thus, we cannot expect high throughput and efficiency
    In the examples above, only 40MHz or 60MHz channel can be utilized for transmission at the best
  Hence, we propose further options which can cover these various cases, as a result, a better gain can be achieved

## Slide 8: Large RU Aggregation in BW ≥ 160MHz (3/4)
There are too many cases for one 40MHz / 60MHz punctured channel in the boundary between two 80MHz channels
  One 40MHz punctured channel
    1, 2 and 3 cases for 160MHz, 240MHz and 320MHz, respectively
  One 60MHz punctured channel
    2, 4 and 6 cases for 160MHz, 240MHz and 320MHz, respectively
  Details are shown in Appendix
In order to reduce signaling overhead, we propose RU combinations which have one 80MHz punctured channel in the boundary of two 80MHz channels
  These options can be used instead of the cases above with slight throughput degradation
  The number of RU combinations can be considerably reduced
  Although the gain is small compared to allowing all the cases above, the implication for average throughput may not be severe in a large bandwidth

## Slide 9: Large RU Aggregation in BW ≥ 160MHz (4/4)
Further proposed cases
  160MHz
    (484)+(484) (1 option)
  240MHz
    (484)+(484)+(996) (2 options)
  320MHz
    (484)+(484)+(996)+(996) (3 options)

## Slide 10: Conclusion
We have proposed various combinations for multiple RU aggregation
For small RU aggregation, we have proposed combinations utilizing middle and center 26-tone RUs to make them more useful
For large RU aggregation, we have proposed combinations being able to support various puncturing patterns for a better throughput and efficiency in non-OFDMA

## Slide 11: Straw Poll #1
Do you agree to add the following text to the TGbe SFD?
  For the OFDMA transmission in the bandwidth larger than or equal to 80MHz, combinations of middle 26-tone RU and one of its adjacent 106-tone RUs are allowed within 20MHz boundary
Y/N/A: //

## Slide 12: Straw Poll #2
Do you agree to add the following text to the TGbe SFD?
  For the OFDMA transmission in the bandwidth larger than or equal to 80MHz, combinations of center 26-tone RU and one of its adjacent 106-tone RUs are allowed
Y/N/A: //

## Slide 13: Straw Poll #3
Do you agree to add the following text to the TGbe SFD?
  For the OFDMA transmission in the bandwidth larger than or equal to 80MHz, combinations of center 26-tone RU and one of its adjacent 52-tone RUs are allowed
Y/N/A: //

## Slide 14: Straw Poll #4
Do you agree to add the following text to the TGbe SFD?
  For the 80MHz non-OFDMA transmission, the following RU combinations are allowed
    242+242, 4 options
Y/N/A: //

## Slide 15: Straw Poll #5
Do you agree to add the following text to the TGbe SFD?
  For the 160MHz non-OFDMA transmission, the following RU combination is allowed
    (484)+(484), 1 option
    Note that () means the RU used in each 80MHz channel
Y/N/A: //

## Slide 16: Straw Poll #6
Do you agree to add the following text to the TGbe SFD?
  For the 240MHz non-OFDMA transmission, the following RU combinations are allowed
    (484)+(484)+(996), 2 options
    Note that () means the RU used in each 80MHz channel
Y/N/A: //

## Slide 17: Straw Poll #7
Do you agree to add the following text to the TGbe SFD?
  For the 320MHz non-OFDMA transmission, the following RU combinations are allowed
    (484)+(484)+(996)+(996), 3 options
    Note that () means the RU used in each 80MHz channel
Y/N/A: //

## Slide 18: References
[1] 802.11-19/1907r2 Multiple RU Combinations for EHT
[2] 802.11-19/1908r4 Multi-RU Support
[3] 802.11-20/0024r2 Multiple RU Aggregation
[4] 802.11-20/0048r0 RU aggregation for 240MHz and 320MHz
[5] 802.11-20/0108r0 Multi-RU Support for OFDMA

## Slide 19: Appendix
Various patterns with one 40MHz punctured channel in the boundary between two 80MHz channels
  160MHz
  240MHz
  320MHz

## Slide 20: Appendix
Various patterns with one 60MHz punctured channel in the boundary between two 80MHz channels
  160MHz
  240MHz
  320MHz