## Slide 1: Phase Rotation Proposal
Date: 2020-03-16
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In our previous contributions [1][2], we proposed several options for the phase rotation in 320MHz
  The proposed options were designed from repeating a 80MHz phase rotation sequence and applying an additional coefficient to each 80MHz segment
  We considered all kinds of 20MHz based preamble punctured cases as well as non-preamble punctured one
  We showed that even the optimized sequence has a quite high PAPR in preamble punctured cases
Meanwhile, TGbe agreed only a few preamble punctured cases in the last meeting
  One 40MHz / 80MHz hole was adopted in 320MHz
Considering those agreed cases as well as non-preamble punctured one, we propose a unified phase rotation sequence in 320MHz and show its PAPR

## Slide 3: Assumptions
Non-punctured and punctured cases are considered
  [oooo oooo oooo oooo]
  [xxoo oooo oooo oooo], [ooxx oooo oooo oooo], [oooo xxoo oooo oooo], [oooo ooxx oooo oooo], [oooo oooo xxoo oooo], [oooo oooo ooxx oooo], [oooo oooo oooo xxoo], [oooo oooo oooo ooxx], [xxxx oooo oooo oooo], [oooo xxxx oooo oooo], [oooo oooo xxxx oooo], [oooo oooo oooo xxxx]
The 11ax 80MHz phase rotation is repeated and an additional coefficient applied to each 80MHz segment is optimized to reduce PAPR
  Candidates for the additional coefficient: 1, -1, j, -j
  Additional coefficients are obtained by minimizing the worst PAPR among all cases above in L-LTF
  In each case above, we consider PAPR for 320MHz and each 160MHz as well to accommodate both contiguous 320MHz and non-contiguous 160+160MHz
O: non-punctured 20MHz
X: punctured 20MHz

## Slide 4: Optimized Phase Rotation
We propose the following phase rotation sequence
  [1 -1 -1 -1 1 -1 -1 -1 -1 1 1 1 -1 1 1 1]
PAPR
  We show the maximum PAPR for L-STF and L-LTF
    Reference: [1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1]
    Option 2A : [1 -1 -1 -1 j -j -j -j j -j -j -j 1 -1 -1 -1] (Best option under non-preamble puncturing)
    Option 2B : [1 -1 -1 -1 j -j -j -j 1 -1 -1 -1 j -j -j -j] (One of the best options under all kinds of 20MHz based preamble puncturing)
    4x IFFT is applied to calculate PAPR
  In Appendix, CDF is plotted considering all the PAPR values in each L-STF, L-LTF and L-SIG as well
 | L-STF [dB] | L-LTF [dB]
Proposal | 8.4251 | 9.0694
Reference | 8.6899 | 9.7663
Option 2A in [2] | 8.8281 | 9.6502
Option 2B in [2] | 8.4281 | 9.4274
Worst case for the proposal:
320MHz PAPR with
[oooo xxoo oooo oooo]
Worst case for the reference:
320MHz PAPR with
[xxoo oooo oooo oooo] [oooo xxoo oooo oooo] [oooo oooo xxoo oooo] [oooo oooo oooo xxoo]
Worst case for Option 2A:
320MHz PAPR with
[oooo xxxx oooo oooo]
[oooo oooo xxxx oooo]
Worst case for Option 2B:
320MHz PAPR with
[oooo xxoo oooo oooo]
Higher 160MHz part is multiplied by -1

## Slide 5: Discussion
The proposed sequence has a better PAPR than the reference sequence in the legacy part
The proposed sequence also has a low PAPR in L-STF and L-LTF compared to the PAPR for the Data part which is shown in Appendix
Whereas, in L-SIG, the proposed sequence has about a 1dB higher PAPR than the Data part at the median point of the distribution, but, the performance degradation due to this can be overcome by a combining gain attainable at a receiver
  The property of L-SIG which is random and repeated every 20MHz channel causes a high PAPR
  However, when a receiver decodes L-SIG, it can combine some of the L-SIG parts which are repeated in the time domain as well as the frequency domain which results in a performance enhancement

## Slide 6: Conclusion
We have proposed the phase rotation for 320MHz and have evaluated its PAPR
We have verified that
  The proposed sequence is better than the reference sequence
  Comparing with the Data part, the proposed sequence has a good PAPR in L-STF and L-LTF but a bit high PAPR in L-SIG which can be overcome by a combining gain

## Slide 7: Straw Poll #1
Do you agree to add the following text to the TGbe SFD?
  Phase rotation for 320MHz is defined as follows
    [1 -1 -1 -1 1 -1 -1 -1 -1 1 1 1 -1 1 1 1]
Y/N/A: //

## Slide 8: References
[1] IEEE 802.11-19/1493r1 Phase Rotation for 320MHz
[2] IEEE 802.11-19/1890r2 Phase Rotation Follow-up
[3] IEEE 802.11-20/0404r0 Further Proposals for Multiple RU Aggregation

## Slide 9: Appendix
PAPR for L-STF / L-LTF
All PAPR values of 320MHz and each 160MHz are considered for all non-punctured and punctured cases
L-STF
L-LTF

## Slide 10: Appendix
PAPR for the L-SIG part
All PAPR values of 320MHz and each 160MHz are considered for all non-punctured and punctured cases in all possible L-SIG contents

## Slide 11: Appendix
PAPR for the Data part
All PAPR values of 320MHz and each 160MHz are considered for all non-punctured and punctured cases in various random data (500 generation)