## Slide 1: RTS/CTS for multi-link
Date: 2020-03-16
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Sungjin Park |  |  |  | allean.park@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Namyeong Kim |  |  |  | namyeong.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Overview
RTS/CTS protection issue has been dealt with some contributions [1,2]
On the other hand, TGbe shall support a MLD that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links [3]
In this contribution, we address a potential problem when RTS/CTS protection is used for MLDs which do not support simultaneous tx/rx and introduce some options to deal with the problem

## Slide 3: Background: Multi-link framework
EHT device that has more than one affiliated STA is defined as multi-link device (MLD) [3]
Links of MLD can be categorized into two types: STR link set and non-STR link set
  STR link set:
    Downlink and uplink frames can be transmitted simultaneously over the links in the STR link set
  Non-STR link set:
    Transmission on a link in the non-STR link set causes in-device interference on reception of other links in the non-STR link set
MLDs that are constrained to simultaneously transmit and receive on a pair of links should be able to operate over this link pair

## Slide 4: Background: Spatial multiplexing power save
SM power saving allows a non-AP STA to operate with only one active receive chain and thus average power consumption can be reduced
SM power saving are of two types
  Static SM power saving:
    A STA enables its multiple receive chains only when it receives SM Power Save action frame from AP
  Dynamic SM power saving:
    A STA enables its multiple receive chains only when it receives stard of sequence frames
    Although it is up to vendors which frame should be used for dynamic SM power saving, exchanging RTS/CTS frames or MU-RTS/CTS frames is commonly used for this purpose
RTS
CTS
DATA
DATA
CTS
STA
AP
RTS
ACK
ACK
Dynamic SM power saving assuming number of STA’s radio is 4
Active chain = 1
Active chain = 4
Active chain = 1

## Slide 5: Problem on RTS/CTS for non-STR MLD
According to legacy .11 standard, a non-AP STA shall commence the transmission of a CTS frame response if the non-AP STA receives an (MU-)RTS Trigger frame
However, the response will cause internal interference to non-STR non-AP STAs, as shown in the figure below
This can cause a collision of a receiving frame, DATA1, even the non-AP STA is able to receive frames, i.e, DATA1 and DATA2, at the same time
: Internal interference
RTS
CTS
DATA1
DATA1
CTS
Non-AP MLD
(Non STR link set)
AP MLD
(STR link set)
Link A
Link B
Link A
Link B
RTS
Busy
(MU-)
RTS
DATA2
CTS
CTS
DATA2
(MU-)
RTS
Busy
ACK
ACK
ACK
ACK

## Slide 6: Candidate Options
Option 1: Recommend not to transmit to non-AP MLDs where internal interference may occur on reception on other links
  In RTS case, even though the AP MLD gets to access the channel, the AP MLD have to release the channel
  In MU-RTS case, the AP MLD excludes the non-AP MLDs from following MU-RTS frame
RTS
DATA1
CTS
AP MLD
(STR link set)
Link A
Link B
Busy
ACK
RTS
DATA1
CTS
AP MLD
(STR link set)
Link A
Link B
Busy
MU-RTS
DATA2
CTS
ACK
ACK
AP MLD accessed the channel but there are no frames to send,
so the channel is released immediately.
AP MLD will indicate recipients excluding the non-AP MLDs in which internal interference may be occurred.

## Slide 7: Candidate Options
In option 1, even though the non-AP MLD can receive simultaneously on its links, the non-AP MLD cannot receive any frames initiated by (MU-)RTS frame while receiving frames on other links
Option 2-1: The AP MLD can disable RTS/CTS operation regardless of RTS threshold on demand
  It is possible because the AP MLD is aware of capabilities (i.e., whether STR is supported or not) and current status of transmission/reception of associated non-AP MLDs
  This option is applicable to both DL SU and DL MU
  Instead of RTS/CTS exchange, CTS-to-self frame can be used
  SM power saving cannot be supported in this option since (MU-)RTS frame is not transmitted in this option
RTS
DATA1
CTS
AP MLD
(STR link set)
Link A
Link B
Busy
DATA2
ACK
ACK
Based on capabilities and current status, (MU-)RTS/CTS is disabled

## Slide 8: Candidate Options
Option 2-2: Omit the corresponding STA’s information (e.g., RA in RTS, AID in MU-RTS) in the (MU-)RTS frame
  Regardless of receptions of CTS frames, an RU allocation plan of following PPDU does not vary
  Hence, unless all CTS frame transmissions fail, the AP MLD will transmit data frame regardless of CTS reception result
  SM power saving cannot be supported in this option since a Trigger frame does not include a User Info field with the AID of the corresponding STA
  DL SU case cannot be supported

## Slide 9: Diagram for Option 2-2
AP MLD A is transmitting frame to non-AP MLDs B and C
When Link B becomes idle, AP MLD A gets opportunity to access channel
AP MLD A makes up MU-RTS for recipients, non-AP MLDs C and D, with omission non-AP MLD B from the MU-RTS
Non-AP MLD B can successfully receive DATA2 as if a basic method, not RTS/CTS exchange
MU-RTS
CTS
DATA1 (RA=MLD B, MLD C)
DATA1
CTS
Non-AP MLD B
(Non-STR link set)
AP MLD A
(STR link set)
Link A
Link B
Link A
Link B
MU-RTS
Busy
MU-RTS
DATA2 (RA=MLD B, MLD C, MLD D)
CTS
DATA2
Busy
ACK
ACK
ACK
ACK
CTS
DATA1
Non-AP MLD C
(STR link set)
Link A
Link B
MU-RTS
CTS
DATA2
MU-RTS
Busy
ACK
ACK
Non-AP MLD D
(Non-STR link set)
Link A
Link B
CTS
DATA2
MU-RTS
Busy
ACK
(AIDs in User Info= MLD C, MLD D)

## Slide 10: Candidate Options
Option 2-3: Indicate whether the CTS response is required or not to the corresponding STAs
  Each STA determines whether to response with CTS frame within SIFS duration or not by means of information in its corresponding User Info field
  For example, RU Allocation subfield or other reserved field can be used
  In this option, the MU-RTS behaves like CTS-to-self for non-AP MLDs which may occur internal interferences
  SM power saving works well in this option
  This option is applicable to DL MU
    Since the corresponding STA cannot respond with CTS frame, the transmitter of RTS frame cannot distinguish between transmission failure of RTS frame and intentional disregard

## Slide 11: Diagram for Option 2-3
AP MLD A is transmitting frame to non-AP MLDs B and C
When Link B becomes idle, AP MLD A gets opportunity to access channel
AP MLD A makes up MU-RTS for recipients, non-AP MLDs B, C and D, with indication of responding CTS frame
As non-AP MLD B is notified by MU-RTS, it does not response, but it expect transmission from AP MLD A
MU-RTS
CTS
DATA1 (RA=MLD B, MLD C)
DATA1
CTS
Non-AP MLD B
(Non-STR link set)
AP MLD A
(STR link set)
Link A
Link B
Link A
Link B
MU-RTS
Busy
MU-RTS
DATA2 (RA=MLD B, MLD C, MLD D)
CTS
DATA2
Busy
ACK
ACK
ACK
ACK
CTS
DATA1
Non-AP MLD C
(STR link set)
Link A
Link B
MU-RTS
CTS
DATA2
MU-RTS
Busy
ACK
ACK
Non-AP MLD D
(Non-STR link set)
Link A
Link B
CTS
DATA2
MU-RTS
Busy
ACK
MU-RTS
(AIDs in User Info=MLD B w/ indication, MLD C, MLD D)

## Slide 12: Summary
 | Option 1: Restrict transmission | Option 2-1: Transmit without RTS frame | Option 2-2: Omit the corresponding STA’s information | Option 2-3: Indicate to the corresponding STAs
Bandwidth efficiency | Low | High | High | High
SU/MU support | None | Either SU/MU support | MU support | MU support
Protection | None | Cannot be protected at both tx and rx sides | Can be protected at tx side | Can be protected at tx side
SM power saving | None | Not supported | Not supported | Supported

## Slide 13: Conclusion
We have discussed several candidates to avoid internal interference for non-STR STA MLDs when RTS/CTS protection is used
  Restrict transmission
  Transmit without RTS frame
  Omit the corresponding STA’s AID
  Inform the corresponding STAs
Indicating to the corresponding STAs whether the CTS response is required or not can be a good option to deal with the problem since the option can support SM power saving that the other options can’t
Especially in case of DL SU, disabling RTS/CTS operation is a good solution

## Slide 14: References
[1] 19/2125r0, “EHT RTS and CTS Procedure”
[2] 20/0026r0, “MLA: Support for Constrained Devices”
[3] 19/1262r8, “Specification Framework for TGbe”

## Slide 15: Straw Poll 1
Do you agree to add the following text to the TGbe SFD?
  A STA may indicate whether each recipient STA commences the transmission of a CTS frame response or not via MU-RTS frame.
    A detailed method is TBD.