## Slide 1: Bug Fix for Acknowledgement rule in Multi-link
Date: 2020-03-15
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Yifan Zhou |  |  |  | 
Guogang Huang |  |  |  | 
Yiqing Li |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Motivation
Below motion is passed in Jan 2020 IEEE meeting
  Motion 63: The receive status of QoS Data frames of a TID received on a link shall be signaled on the same link and may be signaled on other available link(s)
The QoS Data with Ack Policy of No Ack doesn’t need to be acknowledged, and should be excluded from the rules;
Current rule is too strict in some case when the Ack Policy is Block Ack; (examples showed in next slides)
Modification is proposed to fix above issues.

## Slide 3: Example 1
An example shown in below figure
  BA1 contains the acknowledgement of MSDU with sequence number 1-20, and all corresponding bits are set to 1;
  BAR2 set SSN=21 to move the WinStartB to 21;
In this example, the MSDUs with SN 11-20 already be acknowledged in link 1, and can not be acknowledged in link 2 where they are transmitted because of the shift of WinStartB;
The example is reasonable, but doesn’t follow the rule that data and acknowledgement shall be transmitted on the same link.
A-MPDU1
BAR1
A-MPDU3
BA1
A-MPDU2
A-MPDU4
BAR2
BA2
SN:1-10
SN:11-20
SN:21-30
SN:31-40
SSN=1
SSN=21
Link 1
Link 2

## Slide 4: Example 2
Another example shown in below figure
  BA1 contains the acknowledgement of MSDU with sequence number 1-10, and all corresponding bits are set to 1;
  BAR2 set SSN=11 to move the WinStartB to 11;
In this example, the MSDUs with SN 1-10 already be acknowledged in link 1, so it doesn’t need to be acknowledged in link2 once more;
The acknowledgement of MSDU 1-10 can not be transmitted in link2 anymore because BAR2 shift the WinStartB to 11;
The example is reasonable, but doesn’t follow the rule that data and acknowledgement shall be transmitted on the same link.
A-MPDU1
BAR1
A-MPDU3
BA1
A-MPDU2
A-MPDU4
BAR2
BA2
SN:1-10
SN:1-10
SN:11-20
SN:11-20
SSN=1
SSN=11
Link 1
Link 2

## Slide 5: Proposed Modification
The receive status of a MSDU or A-MSDU in a QoS Data frames of a TID received on a link shall be signaled on the same link unless at least one of following conditions is true:
  The receive status of the MSDU or A-MSDU has already be signaled in other available link(s) with corresponding bit in the BA be set to 1;
  The corresponding Ack Policy of the MSDU or A-MSDU is set to No Ack.
The receive status of a MSDU or A-MSDU in a QoS Data frames of a TID received on a link may be signaled on other available link(s) if the Ack Policy is not set to No Ack.

## Slide 6: Straw Poll 1
Do you agree to modify acknowledgement rule in multi-link as below:
  The receive status of a MSDU or A-MSDU in a QoS Data frames of a TID received on a link shall be signaled on the same link if a BA response is needed, and the SN of the MSDU or A-MSDU is larger or equal to SSN in BA frame.
  Yes
  No
  Abstain

## Slide 7: Straw Poll 2
Do you agree to modify acknowledgement rule in multi-link as below:
  The receive status of a MSDU or A-MSDU in a QoS Data frames of a TID received on a link may be signaled on other available link(s) if the Ack Policy is not set to No Ack.
  Yes
  No
  Abstain

## Slide 8: Straw Poll 1 （backup）
Do you agree to modify acknowledgement rule in multi-link as below:
  The receive status of a MSDU or A-MSDU in a QoS Data frames of a TID received on a link shall be signaled on the same link unless at least one of following conditions is true:
    The receive status of the MSDU or A-MSDU has already be signaled in other available link(s) with corresponding bit in the BA be set to 1;
    The corresponding Ack Policy of the MSDU or A-MSDU is set to No Ack.
  Yes
  No
  Abstain