## Slide 1: MLA: SSID Considerations
Date: 2020-02-14
Authors:

## Slide 2: Motivation
Currently an AP broadcasts an SSID on a link so a client looking for the same SSID value can discover this AP for association
In MLO, there are multiple APs (and beacons). How should the SSID be conveyed to an MLO client?
How to ensure the legacy clients are not impacted?

## Slide 3: Observations
Today a client looks for a specific SSID to associate with
  An SSID for which the client possesses security credentials
  Only connected to one SSID at any given time
The client discovers the specific SSID by active and passive scanning (beacon and Probe Requests)
If the client finds multiple BSSs in multiple bands/channels that serve the same SSID, the client will select one channel to perform Association
  The SSID is specified in the Association Request
  The user cannot specify which BSS a client should associate with
  The selection is client implementation-specific

## Slide 4: Observations
In fact, most latest mesh-type home Wi-Fi networks only allow the user to configure a single SSID per each network the user wants to set up (e.g., home network, guest network, etc). The APs will then bcast this SSID in all its beacons
Some users prefer to set up different SSIDs on different bands and manually separate the clients on different SSIDs. For example:
  SSID on 2.4GHz = ssid_2.4
  SSID on 5GHz = ssid_5
  All the IoT devices can then be connected to bssid_2.4 only
  This kind of setting does not make sense for MLO clients because the user should not be required to enter the corresponding credentials for EACH link of the MLO client

## Slide 5: Proposal
The current SSID carried in the beacon remains there to serve the legacy (pre-11be) clients
To serve MLO clients, an SSID is configured for an AP MLD (i.e., SSID is per-AP MLD and per network the user wants to instantiate)
  This preserves the current user experience where the user selects one SSID to connect to (and not one SSID per each link)
The MLO SSID will be carried in the “MLO info” part of the beacon/Probe Response
The above supports the manual SSID partitioning user case (in this slide) and does not require the user to reconfigure the legacy devices (to the new SSID)

## Slide 6: Comparison to Another Scheme (Option 1)
Option 1: same SSID for all APs on the same AP MLD
  Does not support the use case described on this slide 4
Option 2: add MLO SSID to legacy SSID
  Supports the split-SSID use case described on this slide
  This also allows same SSID for all APs on the same AP MLD (i.e., superset of Option 1)

## Slide 10: Tx Beacons vs Non-Tx Beacons
The previous diagrams assume all APs tx a beacon. However, it’s possible to save OTA resources to tx only a subset of beacons
Imagine the blue and green “C” shapes are stacked on top of each other as two layers
  For each channel vertically, we can pick one or more layer to tx beacons. Then, the rest of the other layers will become non-Tx beacons, which will be carried as non-Tx info in the tx beacon(s)

## Slide 11: Summary of What’s Needed for the Spec
Define the concept of MLO SSID
  Carried in management frames by the AP (same as legacy SSID advertisement)
  Its value can be the same as or different than the per-AP SSID
Client discovers all SSIDs
  Pre-11be clients can only discover the legacy SSID(s)
  MLO clients can discover (and display to the user) the legacy SSIDs and the MLO SSID

## Slide 12: Old SP1
Do you agree to the following?
  An AP MLD shall have only one SSID, that is transmitted by the APs that are affiliated to the AP MLD.
    Note 1: It is TBD whether the APs that are affiliated to the AP MLD can also have a separate SSID
    Note 2: Signaling of the SSID is TBD

## Slide 13: SP1
Do you agree to the following for 11be R1?
  The 11be spec shall support the following:
    An AP MLD configures a single SSID value that is transmitted by the APs that are affiliated to the AP MLD
    Note 1: It is TBD whether the APs that are affiliated to the AP MLD can also have a separate SSID
    Note 2: Signaling of the SSID is TBD