## Slide 1: Multi-link BA Clarification
Date: 2020-05-04
Authors:

## Slide 2: Recap: Multi-link BA consensus in TGbe SFD
A single block ack agreement is negotiated between two MLDs for a TID that may be transmitted over one or more links.
The established block ack agreement allows the QoS Data frames of the TID, aggregated within the A-MPDUs, to be exchanged between the two MLDs on any available link.
Sequence numbers are assigned from a common sequence number space shared across multiple links of a MLD, for a TID that may be transmitted to a peer MLD over one or more links.

## Slide 3: Clarification- 1
After the BA agreement is established, a set of enabled links/disabled links can be changed by updating the TID-to-link mapping.
But, after an update of the TID-to-link mapping, it is not clear that the BA re-establishment is needed or not.
  Especially, for single TID-to-single link mapping case and all TIDs-to-single link mapping case.

## Slide 4: Clarification- 1
Single TID-to-single link mapping case (i.e., flow-level aggregation MLD) :
  A non-AP MLD sets up with an AP MLD the multi-link operation on the link 1 and link 2.
    TID1-4 are mapped to the link 1 and TID5-8 are mapped to the link 2.
    The non-AP MLD establishes a Block Ack agreement for all TIDs.
  Later, the non-AP MLD changes the link mapping for TID3-4 from the link 1 to the link 2.
  At that time, for TID3-4, does the non-AP MLD reuse the existing BA agreement or re-establish the BA agreement?

## Slide 5: Clarification- 1
All TIDs-to-single link mapping case (i.e., single link MLD) :
  A non-AP MLD sets up with an AP MLD the multi-link operation on the link 1 and link 2.
    All TIDs are mapped to the link 1, and the link 2 is disabled.
    The non-AP MLD establishes a Block Ack agreement for all TIDs.
  Later, the non-AP MLD changes the link mapping for all TIDs from the link 1 to the link 2.
  At that time, for all TIDs, does the non-AP MLD reuse the existing BA agreement or re-establish the BA agreement?

## Slide 6: Clarification- 1
Our interpretation is that a BA agreement in the MLO is a per-MLD basis (not a per-link basis) and the non-AP MLD reuses the existing BA agreement regardless any update on the TID-to-link mapping.
It means that, after the BA agreement, the common sequence number space and the common reordering buffer are applied on all setup links, not only for the enabled links at the BA setup time.

## Slide 7: SP 1
Do you support that, after the BA agreement of a TID between two MLDs, the common sequence number space and the common reordering buffer of the TID are applied on all setup links?

## Slide 8: Clarification- 2
In TGbe SFD,
  A single block ack agreement is negotiated between two MLDs for a TID that may be transmitted over one or more links
But, the BA agreement is not always necessary to transmit frames over one or more links.
When the BA agreement for a TID does not exist, a MLD can only one outstanding frame belonging to that TID. But, frames for that TID can be transmitted one or more links.

## Slide 9: SP 2
Do you support to be able to send individually addressed data frames of a TID between two MLDs without a BA agreement of the TID?