## Slide 1: 11be BA Indication
Date: 2020-02-06
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang |  |  |  | 
Alexander Danny |  |  |  | 
Dan Bravo |  |  |  | 
Laurent Cariou |  |  |  | 
Arik Klein |  |  |  | 
Danny Ben-ari |  |  |  | 
Ofer Schreiber |  |  |  | 
Ghosh Chittabrata |  |  |  | 
Notes: September 2012

## Slide 2: Background
We expect that 11be will have capability to negotiate up to 1024 buffer size in R1 [1], and larger negotiated buffer size implies requirement of larger BA bitmap size and a wide range of BA bitmap size that can be used
  Currently, the recipient can respond with any BA bitmap that covers the reception range. In 11ax, most of the implementation just respond with 256 BA
  The originator of a BA agreement does not know how recipient will respond and efficiency is likely to degrade due to this reason
We propose direction to improve the efficiency for larger number of negotiated buffer size

## Slide 3: Overhead Analysis due to Wide Range of Responding BA Bitmap Size
Compressed BA size is 32/56/88/152 bytes for 64/256/512/1024 BA.
Compared with 64 BA, 256/512/1024 BA corresponds to 1.75/2.75/4.75 times increase of BA transmission time
  Note that the recipient can choose to always use the largest BA bitmap under all cases even when only a few MPDUs are sent
  Note that this is true for any data rate
  Note that the overhead is even higher for 4096 BA for sure
64 BA
256 BA (1.75x)
512 BA (2.75x)
1024 BA (4.75x)

## Slide 4: BA transmission overhead
BA overhead is 32/152 bytes for 64/1024 BA
Transmission time (us) for HE TB case
  There is a increase of 100 us to 1200 us for MCS0
Transmission time (us) for non-HT case with mandatory rate
Transmission time (us) for ER SU PPDU 106 tone is 73/347 us
Roughly multiple the above number under Multi-TID case
X Tone | MCS 0 | MCS 1 | MCS 2 | MCS 3 | MCS 4 | MCS 5
26 | 320/1520 | 150/715 | 102/486 | 77/368 | 51/243 | 38/181
52 | 150/715 | 77/368 | 51/243 | 38/181 | 25/121 | 19/91
106 | 73/347 | 36/171 | 24/114 | 18/85 | 12/57 | 9/42.9
242 | 31/150 | 15/74 | 10/50 | 7.8/37 | 5/24.9 | 4/18.7
6 Mbps | 12 Mbps | 24 Mbps
42/202 | 21/101 | 10/50

## Slide 5: Example 1:
Consider the following example for single protection
AP
Non-AP
A-MPDU with SN 2, 3
Allocated NAV for 1024 BA
64 BA
AP MLD
AP 1
AP 2
non-AP MLD
Non-AP 1
Non-AP 2
Transmission in link 1
Transmission in link 2
512 BA link2
64 BA for link1
Allocated 1024 BA for link 1 and link 2
Allocated 1024 BA for link 1 and link 2

## Slide 6: Example 2
HE TB Allocation
AP
STA 1
64 BA
Allocated HE TB for 1024 BA under low MCS
A-MPDU to STA 1
A-MPDU to STA N
STA N
64 BA
AP
STA 1
64 BA
Allocated HE TB for 1024 BA under low MCS
A-MPDU to STA 1
A-MPDU to STA N
STA N
64 BA
MU-BAR

## Slide 7: Proposal
Proposal:
  Design a mechanism for the originator of a BlockAck negotiation of a TID to indicate to the recipient the range of reported received status of a solicited BA
Explicit indication:
  Enhance BAR to solicit BA in a reported range of received status of a TID, and the solicited BA only reports received status of the TID within the reported range
Implicit indication:
  Under implicit BAR policy, for a PSDU that solicits immediate Block Ack with received status of a TID, the solicited BA only reports received status of the TID within the reported range determined implicitly

## Slide 8: Conclusion
We discuss the BA overhead under 1024 BA
  Currently, recipient determines the BA size and the originator has to allocate unnecessary medium resource under single protection or for HE TB response, and the resource is wasted
Propose to design a mechanism for the originator of a BA negotiation of a TID to indicate to the recipient the range of reported received status of a solicited BA
  Better medium resource allocation by the Originator
  Useful for the recipient to comply to save medium resource allocation or allow more transmission from the originator in a TXOP

## Slide 9: Straw Poll
Do you support to design a mechanism for the originator of a BlockAck negotiation of a TID to indicate to the recipient the range of reported received status of a solicited BA in R2?
  if supported by the recipient, it is supported for all negotiated buffer sizes

## Slide 10: Reference
[1] 11-20-0053r2 Multi-link BA