## Slide 1
Authors:
Channel Access Category
Date: 2020-03-16
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Nan Li | ZTE |  |  | 
Dan Yang | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses the channel access in Multi-Link communication to support low latency applications and high priority services.

## Slide 3: Introduction
Re-cap of support low latency requirements (1)
  802.11be PAR and CSD [1][2] indicate that
    This amendment defines at least one mode of operation capable of improved worst case latency and jitter.
    This amendment aims to build on the current and emerging WLAN technologies by providing further improvement of aggregate throughput and latency to ensure competitiveness of IEEE Std. 802.11 in coming years.
    This project will improve the latency and jitter of WLAN.

## Slide 4: Introduction
  Re-cap of support low latency requirements (2)
  In the SFD of 802.11be [3], it indicates that
    The 802.11be amendment shall define mechanism(s) in support of priority access to a non-AP STA for national security (NS)/emergency preparedness (EP) priority service

## Slide 5: Issues for Priority Service
  User Priority and Access Category
  802.11md defines a set of User Priority (UP) to allow an application to specify the traffic priority in traffic class during a stream establishment. The UP can be mapped to Access Category (AC) which is used by MAC for channel access.
  However, there are issues to support priority services and low latency applications.
    The highest AC is the AC_VO (i.e. A_VO), which is used by voice traffic or other user data traffic and management frames. This causes a difficulty to distinguish a NS/EP or a low latency traffic from others within the same AC_VO.
    There is no UP for NS/EP.

## Slide 6: Proposal for a new Access Category
  Option 1 - Revise an existing UP to map to any AC
  Update the UP to AC mapping table for support of the high priority service.
    NOTE: A traffic of high priority/low latency (e.g. NS/EP) may preempt a current on-going traffic with any AC.
Priority | UP (Same as IEEE802.1D Priority) | IEEE802.1D | AC | Transmit queue (dot11Alternate- EDCAActivated false or not present) | Transmit queue (dot11Alternate EDCAActivated true) | Designation
 | 1 | BK | AC_BK | BK | BK | Background
 | 2 | - | AC_BK | BK | BK | Background
 | 0 | BE | AC_BE | BE | BE | Best Effort
 | 3 | EE | AC_BE | BE | BE | Best Effort
 | 4 | CL | AC_VI | VI | A_VI | Video (alternate)
 | 5 | VI | AC_VI | VI | VI | Video (primary)
 | 6 | VO | AC_VO | VO | VO | Voice (primary)
 | 7 | NC | AC_VO | VO | A_VO | Voice (alternate)
 | 3 |  | AC_ANY | ANY | ANY | high priority/low latency
Lowest
Highest

## Slide 7: Proposal for a new User Priority
  Option 2 – Add a new UP for a High Priority Service
  Define a new UP (UP-12) for the high priority/low latency (HP/LL) service in Table 9-163 of 802.11md.
    UP-12 provides the highest priority amongst user priorities.
    A user traffic with UP-12 (e.g. NS/EP service) may preempt a current on-going user traffic.
User Priority | Meaning
0-7 | Use Priority of an MSDU
8 | The AC value of an MPDU is AC-VO (voice)
9 | The AC value of an MPDU is AC-VI (video)
10 | The AC value of an MPDU is AC-BE (best effort)
11 | The AC value of an MPDU is AC-BG (background)
12 | User Priority value of an MSDU which can be mapped to any AC value of an MPDU for high priority/low latency (HP/LL) service, i.e., it allows to use the channel access with any AC which comes earliest for HP/LL transmission.
123-254 | Reserved
255 | The User Priority field is not used for comparison

## Slide 8: Proposal for a new Access Category
  Option 2 – Add a new UP for a High Priority Service
  Map UP-12 to ANY AC for the high priority service.
    NOTE: A traffic of high priority/low latency (e.g. NS/EP) may preempt a current on-going traffic with any AC.
Priority | UP (Same as IEEE802.1D Priority) | IEEE802.1D | AC | Transmit queue (dot11Alternate- EDCAActivated false or not present) | Transmit queue (dot11Alternate EDCAActivated true) | Designation
 | 1 | BK | AC_BK | BK | BK | Background
 | 2 | - | AC_BK | BK | BK | Background
 | 0 | BE | AC_BE | BE | BE | Best Effort
 | 3 | EE | AC_BE | BE | BE | Best Effort
 | 4 | CL | AC_VI | VI | A_VI | Video (alternate)
 | 5 | VI | AC_VI | VI | VI | Video (primary)
 | 6 | VO | AC_VO | VO | VO | Voice (primary)
 | 7 | NC | AC_VO | VO | A_VO | Voice (alternate)
 | 12 (not same as IEEE802.1D Priority) |  | AC_ANY | ANY | ANY | (high priority and low latency)
Lowest
Highest

## Slide 9: Proposal for a new Access Category
  Comparison
  Common:
    Pros: No additional AC is added, and can reuse existing CW parameters. No extra overhead of CW over the air is introduced by support of HP/LL.
    Cons: MLD has to clean up the queued HP/LL MPDU in other ACs’ buffers if the HP/LL MPDU has been sent out.
  Option 1
    Cons: Revised existing UP value and the mapped AC may impact on the existing implementation.
  Option 2
    Pros: The new UP value does not impact the existing UP and existing UP-AC mapping.
    Cons: Needs to add new UP-AC mapping

## Slide 10: Straw Poll
Do you support to include the following in SFD ?
  802.11be shall define a user priority (e.g. HP/LL) for high priority and low latency service
    NOTE 1: HP/LL is the highest user priority.
    NOTE 2: A user traffic with HP/LL (e.g. NS/EP service) may preempt a current user traffic with any AC.
YES/NO/ABS

## Slide 11: References
[1] 11-18-1231-06-0eht-eht-draft-proposed-par
[2] 11-18-1233-07-0eht-eht-draft-proposed-csd
[2] 11-19-1262-08-00be-specification-framework-for-tgbe

## Slide 12
Thank you!