## Slide 1: HCFA Example
Date: 2020-03-31
Authors:

## Slide 2: Abstract
This presentation is a supplemental information for HCFA (11-20/0040r3).

## Slide 3: Feedback 1 for 11-20/0040r3
HCFA is faster but it is not clear if it would be able to handle stream with high number of frames going out continuously. In addition, the concept of using hash value from a frame that will be transmitted at a later time can be a problem. In most implementations, all high throughput encryption is performed in hardware which works in-line with the actual transmission of a frame. Such implementations won't work if they have to rely on receiving a future frame. In addition, it will add a significant burden on the memory requirement (esp. true for high thruput cases).
It would be good to have a presentation that estimates how high a throughput (number of frames/second) this scheme is expected to handle. This will help the group determine how realistic it would be to implement the part that generates eBCS Data frames in hardware.

## Slide 4: HCFA Procedure
Transmitter
With Instant Authentication
  Transmitter requires to buffers at least 1 frame depending on how many instant authenticators in a frame.
Without Instant Authentication
  Transmitter does not require to buffer frames
Receiver
Receiver requires to buffer the frames in 2 * TK
TK
TK
TESLA Authentication (KMAC128)
Instant Authentication
TESLA key for
SHAKE128

## Slide 5: Buffer Size Estimation
Assumptions
  Payload size: 1,400B
  Frame size: Payload (1,400) + .11 header (24) + HCFA overhead (128) + IP/UDP header (28) = 1,580B
  TK: 100ms
Full HD Video (1920 * 1080 30fps)
  Transmitter side
    >= 1,580B
  Receiver side
    12Mbps (AV1 level 4.0) = 1.5MB/s = 1,072frames/s
    Required buffer size: 1,580B * 1,072 * 0.2 = 339kB
4K Video (3840 * 2160 30fps)
  Transmitter side
    >= 1,580B
  Receiver side
    30Mbps (AV1 level 5.0) = 3.75MB/s = 2,679frames/s
    Required buffer size: 1,580B * 2,679 * 0.2 = 847kB

## Slide 6: Feedback 2 for 11-20/0040r3
PKFA
  Section 12.15.1 indicates that the certificate should be pre-installed in the receivers. However, in 12.15.2 it appears that the eBCS info frame carries the certificate, which is cached in case the eBCS info is successfully authenticated. If the assumption is that the certificate is pre-installed why we have the eBCS info frame deliver the certificate?
    The pre-installed certificate is the certificeate of the CA. The certificate in the eBCS Info frame is the certificate of the AP.
  12.15.2.1 " The eBCS transmitter generates an eBCS Info frame when it receives data to be transmitted”: Is it truly required that eBCS info frame is always sent? I realize it is written w/ DL Case in mind, but even there, is it required to always have eBCS info frame even when PKFA is used?
    Yes. The eBCS Info frame is required to be sent every time. PKFA is expected to be used for occasional non-streaming DL case, such as emergency alert.
  Is it possible to apply the PKFA w/ data frames only without dependency on eBCS info frame? For example they can carry the certificate if needed, correct?
    No. The certificate of the AP is carried only in the eBCS Info frame. Data can be piggy-backed in the eBCS Info frame.
  12.15.2.4 “If the difference between the timestamp in the eBCS Data frame and the time of the eBCS receiver is greater than the cached allowable time difference, the eBCS Data frame shall be discarded.”: Does this mean that synchronization is required between the transmitter and the receiver?
    Yes. Loose time synchronization is required to prevent replay attack.

## Slide 7: Feedback 2 for 11-20/0040r3 (Cont.)
PKFA
  Where is the cached allowable time difference coming from? eBCS info frame? Do we expect it to change? Can it be a fixed amount? Would you elaborate why the checking of time difference is needed?
    The allowable time difference is carried in the eBCS Info frame. The value of the allowable time difference depends on the characteristics of the contents. This value is used to prevent replay attack. For example, if the contents is valid in next 1 minutes, the allowable time difference should be less than 1 minutes.
HCFA:
  Per Marc’s suggestion I shared the contribution w/ some security experts at Intel; the primary feedback I have received so far regarding HCFA is that the description is a bit too complicated and difficult to follow. Adding some examples of frame creation and the description of recovery in case of missing frames would be useful.
    Thanks, I will add / modify in the next revision.

## Slide 8: Feedback 3 for 11-20/0040r3
Comment noting that it looks unlikely for the proposed link layer security design to be able to cover the HD video streaming throughput needs using existing AP hardware.
While new special purpose hardware could potentially be designed for such use cases, that would delay deployment of this technology and it would be better to look at alternative options since most protection mechanisms can actually be performed at the data stream layer without requiring new IEEE 802.11 link layer functionality for data authenticity and integrity protection.
For example, P802.11bc could provide three optional mechanisms for the downlink use cases: no link layer protection, HCFA without instant authentication, and HCFA with instant authentication. The first one of these may end up being the most likely candidate for the HD video streaming use cases at least in the initial deployments.

## Slide 9: Straw poll
Do you prefer to add “no authentication” option for downlink eBCS?
(“Note” that describes the mandatory protection in the higher layer will be added)
Yes
No
Abstain