## Slide 1: Discussion of More Data subfield for multi-link
Date: 2020-03-15
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Yifan Zhou |  |  |  | 
Guogang Huang |  |  |  | 
Yiqing Li |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Motivation
A non-DMG STA uses the More Data subfield to indicate to a STA in PS mode that more BUs are buffered for that STA at the AP; (IEEE802.11-2016)
After multi-link is introduced in 11be, the BUs of one TID can be transmitted through multiple links, and how to buffer the BUs at AP MLD side is implementation related. So it may not accurate to claim BUs are buffered at AP;
How to set More Data subfield in multi-link scenario needs to be discussed.

## Slide 3: Potential Modification: Opt 1
Principle: More Data subfield is set based on the preschedule of data and management frames on this link;
Assume a non-AP MLD supports TID1 and TID3, TID 1 mapping to link 1, TID 3 mapping to link 1, 2 and 3;
More Data subfields in PPDU31 will be set to 0, because it is the last PPDU that carries prescheduled data and management frames on link 3;
One problem is that the receiving STA on link 3 may enter doze state after PPDU31, the BUs of TID 3 failed on link 1 and 2 can not be retransmitted on link 3 anymore.
PPDU11, TID1, More Data = 1
PPDU21, TID3, More Data = 1
Doze state
Link 1
Link 2
Link 3
PPDU12, TID3, More Data = 1
PPDU31, TID3, More Data = 0
PPDU13, TID1, More Data = 0
PPDU22, TID3, More Data = 0
X
Can not be used for TID3 transmission

## Slide 4: Potential Modification: Opt 2
Principle: More Data subfield is set based on buffered BUs of any TID or management frames on this link;
Although PPDU31 is the last PPDU carries BUs of TID3 in link3, the More Data subfield in PPDU31 will be set to 1, because there are still BUs of TID3 buffered at AP MLD, and may be scheduled to be transmitted through link3;
PPDU22 is the last PPDU carries BUs of TID3 in link2, and no more Bus of TID3 buffered at AP MLD. The More Data subfield in PPDU22 will be set to 0, non-AP STA on link 2 may switches to doze state after PPDU22.
Opt2 is more preferred;
Remaining question: how the non-AP STA on link 3 enter doze state?
PPDU11, TID1, More Data = 1
PPDU21, TID3, More Data = 1
Doze state
Link 1
Link 2
Link 3
PPDU12, TID3, More Data = 1
PPDU31, TID3, More Data = 1
PPDU13, TID1, More Data = 0
PPDU22, TID3, More Data = 0
How to enter doze state?

## Slide 5: Proposed More Data Setting
Remaining question: how the non-AP STA on link 3 enter doze state?
A QoS Null frame with More Data subfield set to 0 can be transmitted in link 3 to indicate no more BU will be transmitted through link 3;
The non-AP STA on link 3 will switches to doze state after QoS Null frame.
PPDU11, TID1, More Data = 1
PPDU21, TID3, More Data = 1
Doze state
Link 1
Link 2
Link 3
PPDU12, TID3, More Data = 1
PPDU31, TID3, More Data = 1
PPDU13, TID1, More Data = 0
PPDU22, TID3, More Data = 0
QoS Null,
More Data = 0

## Slide 6: Summary
The setting of More Data subfield is not accurate in MLD case, it is better to adjust it to fit MLD scenario;
A proposed setting is provided
  When AP MLD transmit a BU in one link to a non-AP MLD, if there is at least one more BU of any TID or management frames that mapping to this link present for the same non-AP MLD, the More Data subfield is set to 1, otherwise the More Data subfield is set to 0.
  A QoS Null frame with More Data subfield sets to 0 is transmitted in one link to indicate no more BU of any TID or management frames that mapping to this link present.

## Slide 7: Straw Poll 1
Do you support to adjust the setting of More Data subfield to fit MLD scenario?
  Yes
  No
  Abstain

## Slide 8: Straw Poll 2
Do you support below setting of More Data subfield?
  When AP MLD transmit a BU in one link to a non-AP MLD, if there is at least one additional buffered BU of any TID or management frames that mapping to this link present for the same non-AP MLD, the More Data subfield is set to 1, otherwise the More Data subfield is set to 0.
  A QoS Null frame with More Data subfield sets to 0 is transmitted in one link to indicate no more additional buffered BU of any TID or management frames that mapping to this link present.
  Yes
  No
  Abstain