## Slide 1: Impact of HARQ on Latency – System Level Simulation Analysis
Date: 2020-03-03
Authors:
Name | Affiliation | Address | Phone | Email
Shimi Shilo | Huawei |  |  | 
Avi Weitzman |  |  |  | 
Shahar Patury |  |  |  | 
Ezer Melzer |  |  |  | 
Oren Hencinski |  |  |  | 

## Slide 2: Background
Various contributions on Hybrid Automatic Repeat Request (HARQ) have been presented in previous meetings [1-8]
These contributions focused mainly on the impact of HARQ on the throughput, evaluated in various Link-Level Simulations (LLS)
Reducing the worst-case latency is within the scope of 11be [9]:
  “This amendment defines at least one mode of operation capable of improved worst case latency and jitter”
The acceptable latency depends on the application; a value of 200msec is an exemplary limit for certain applications [10]
In this contribution, we analyze the impact of HARQ on the per-packet latency, by extending LLS results using an NS-3 based System-Level Simulator (SLS)

## Slide 3: Motivation to use an SLS
So far, the majority of HARQ related contributions relied on LLS evaluations
In order to assess the impact of HARQ on latency, we wanted the analysis to consider various MAC-related aspects
An SLS takes into account various system and MAC related considerations that are not part of the LLS, such as:
  An event-based simulator – events are dependent on each other
  CSMA/CA aspects (contentions & collisions, backoff)
  MPDU aggregation & retries (including in-order transfer to upper layers)
  Practical rate adaptation
These can be used to get a more realistic evaluation of the impact of HARQ on performance, in this case on the per-packet latency

## Slide 4: Simulation Methodology
We used an off-the-shelf NS-3 SLS of 802.11 with the following attributes:
  Plain-vanilla NS-3 version 3.28
  Minstrel rate-selection algorithm
  DL UDP traffic
The channel model module in the NS-3 SLS was replaced with a pre-defined SNR, for which the average PER was computed in an LLS
  LLS results (PER for various SNR values, for all MCS values, with and without HARQ) were generated and then used within the SLS
    Without HARQ, the same average PER was assumed for all transmissions
    With HARQ, distinction was made between average PER for first transmission and retransmissions
  For HARQ, we assumed Chase Combining (all coded bits are retransmitted)
This can be viewed as an extension of the LLS which includes MAC aspects
Since we assumed a single AP in all simulations, there is no interference from an OBSS and the SNR corresponds to STAs at a pre-defined distance from the AP

## Slide 5: What are we Measuring?
The per-packet latency is measured as the over-the-air trip delay
We compute the latency from arrival of the packet (at transmitter side) until it is acknowledged, as shown in the figure on the right
Transmitter may use TxOP for retransmissions or CSMA/CA
Processing & Access time corresponds to waiting in Tx queue and backoff
Transmission
Retransmission
Wi-Fi ACK
SDU enters AP
Processing & Access Time
Measured Packet Latency
IP Cloud
AP
STA
Time
Time

## Slide 6: Results – 1 AP, 1 STA
For the case of a single AP and a single STA, with 80Mbps data rate and at SNR=16dB, we get the following CCDF for the per-packet latency
With ARQ, 1% of the packets experience latency above 850msec
With HARQ, this number drops to 403msec
These are huge differences which have a major impact on the performance
In the HARQ case, 42712 packets were successfully transmitted over 5sec, as opposed to 27812 in the ARQ case (~53% improvement)
447msec
1% cases above 403msec
1% cases above 850msec

## Slide 7: Results – 1 AP, 1 STA – cont.
Why is this scenario (Point-to-Point) relevant for our analysis?
We wanted to analyze the impact of HARQ on all MAC mechanisms, while eliminating the impact of access aspects (e.g. round-robin between STAs, collisions, etc.)
This gives us an insight into the impact of HARQ on rate control, aggregation and contention window (including the round-robin between STAs) when it’s least needed
  In a Point-to-Point scenario, there are no collisions, fewer retransmissions, no interference and hence most packets experience very short delay (in the figure on the previous slide, 90% of packets experience delay lower than 75msec), hence there is relatively little to gain
In the next slide, we account for a larger number of STAs and therefore incorporate round-robin (between STAs) and contentions

## Slide 8: Results – 1 AP, 4 STAs
For the case of a single AP and 4 STAs, with 35Mbps data rate (per STA) and at SNR=16dB, we get the following CCDF for the per-packet latency
With ARQ, 1% of the packets experience latency above 1457msec
With HARQ, this number drops to 1050msec
In the HARQ case, 12128 packets were successfully transmitted over 5sec, as opposed to 6420 in the ARQ case (88% improvement)
407msec
1% cases above 1050msec
1% cases above 1457msec

## Slide 9: Results – 1 AP, 4 STAs - cont.
As expected, in such a (more complicated) scenario – with more STAs – the per-packet latency with both ARQ and HARQ is higher
Whereas for the PtP scenario 1% of packets experienced latency higher than 403msec and 850msec for the HARQ and ARQ cases, respectively, in this scenario of 4 STAs (PtMP) the numbers increase to 1050msec and 1457msec, respectively
When there are multiple STAs, a packet failure isn’t necessarily followed by a retransmission (TXOP); instead, the packet waits in the queue until it is rescheduled for a transmission

## Slide 10: Results – 1 AP, 10 STAs – 8Mbps (per STA)
For the case of a single AP and a 10 STAs, with 8Mbps data rate (per STA) and at SNR=18dB, we get the following CCDF for the per-packet latency
With ARQ, 1% of the packets experience latency above 1100msec
With HARQ, this number drops to 690msec
In the HARQ case, 15701 packets were successfully transmitted over 5sec, as opposed to 12069 in the ARQ case (30% improvement)
410msec
1% cases above 690msec
1% cases above 1100msec

## Slide 11: Conclusions
Most evaluations so far focused on the impact of HARQ on the (link-level based) throughput/goodput, ignoring MAC-level aspects
We’ve shown via a combination of system-level & link-level simulations what a significant impact HARQ has on the per-packet latency
These tests were carried out assuming UDP traffic, which means the latency has no impact on the data (packet) rate
  TCP – which determines its data rate based on the estimated round trip delay – will decrease its packet rate dramatically as the latency increases

## Slide 12: References
11-18-1587: HARQ for EHT, Sep. 2018
11-18-1955: HARQ for EHT – Further Information, Nov. 2018
11-18-1963: Discussion on HARQ for EHT, Nov. 2018
11-19-1992: HARQ Feasibility, Jan. 2019
11-19-2029: HARQ in EHT, Jan. 2019
11-19-1979: HARQ performance analysis, Jan. 2019
11-19-780: Consideration on HARQ, May 2019
11-19-1578: An HARQ Transmission Scheme for 11be, Nov. 2019
11-18-1231r6: 802.11 EHT Proposed PAR
11-19-1938r2: Discussion on low latency capability for 802.11be, Jan. 2020