## Slide 1
Authors:
Latency Measurement for Low Latency Applications
Date: 2020-03-12
Name | Affiliation | Address | Phone | Email
Liuming Lu | ZTE Corporation | No.889 Bibo Road, Shanghai, P.R.China |  | lu.liuming@zte.com.cn
Liquan Yuan | ZTE Corporation | No.889 Bibo Road, Shanghai, P.R.China |  | yuan.liquan@zte.com.cn
Bo Sun | ZTE Corporation |  |  | 
Zhiqiang Han | ZTE Corporation |  |  | 
Yonggang Fang | ZTE (TX) |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Introduction (1/2)
TGbe aims to build on the current and emerging WLAN technologies by providing further improvement of aggregate throughput and latency. And At least one mode of operation capable of improved worst case latency and jitter will be defined.[1][2]
Because Wi-Fi uses the unlicensed spectrum the interference from OBSS and other sources would usually exist, how to avoid or reduce the impact of the inference on guaranteed latency for scheduled transmission is of vital importance.

## Slide 3: Introduction (2/2)
Sufficient Latency Measurement can not only evaluate whether the current communication environment is suitable for the transmission of low latency applications, but also distinguish the different types of latency, caused by the varying interference sources.
This contribution proposes to further specify the latency measurement in TGbe including the addition of latency statistics, which would help to distinguish the different types of latency.

## Slide 4: Background (1/2)
Recently for the low-latency topics of TGbe several papers mention time-aware scheduling, multi-link aggregation, latency statistics, etc.
Contribution[3] has shown that time-aware scheduling operates on managed STAs, and interfering transmissions may impact the capability to guarantee bounded latency, further unmanaged STAs/OBSSs are seen as interference.
Contribution[4] has presented latency gains with multi-link aggregation, showing that adding an auxiliary link significantly improves the worst-case latency. But the latency gains seem to be not enough to support the RTA, such as virtual reality or augmented reality.
Contribution[5] proposes to add more latency statistics in EHT for MLO including average transmit delay and TBD percentile transmit delay statistics of each link.

## Slide 5: Background (2/2)
Time-aware scheduling theoretically seems to be a good method for low-latency, but encounters some difficulties in the Wi-Fi environment, such as the interference from unmanaged STAs/OBSSs, etc.
MLO helps to improve the latency, and how to adjust the transmission on different links for low-latency applications should be based on the current load and environment on the current links, which needs the real-time measurement of their corresponding quantitative parameters.
The current latency statistics seems to be not enough for latency measurement, especially to support the low-latency applications. The required additional latency statistics need further study.

## Slide 6: Latency Analyses
AP
Non-AP STA
the time the MSDU is passed to the MAC
Frame loss
T1
the time the frame is ready for transmission
the virtual demarcation point between intra-BSS waiting time and inter-BSS waiting time
the actual frame transmission start time
The time ACK for the initial transmission is received
the actual retransmission start time
The time ACK for the retransmission is received
The time the frame for the initial transmission is received
the actual ACK transmission start time
The time retransmission frame is received
The time ACK for the retransmission is transmitted
T2
T3
T4
T5
BSS Access delay
the time the MPDU is ready for transmission
the actual frame transmission start time
Waiting time interval for the transmission of the intra-BSS PPDUs
Waiting time interval for the transmission of the inter-BSS PPDUs
time interval of waiting time for inter-BSS transmission
time interval of waiting time for intra-BSS transmission

## Slide 7: Latency Classification
Latency | Description | Caused by | Classification
T1 | time interval from the time the MSDU is passed to the MAC to the time the frame is ready for transmission | packet congestion | BSS-Controllable
T2(intra-BSS access delay) | time interval of waiting time for intra-BSS transmission between the time the frame is ready for transmission and the actual frame transmission start time | Intra-BSS transmission contention | BSS-Controllable
T3(inter-BSS access delay) | time interval of waiting time for inter-BSS transmission between the time the frame is ready for transmission and the actual frame transmission start time | Inter-BSS transmission contention | BSS-Uncontrollable
T4 | time interval between the actual frame transmission start time and The time ACK for the initial transmission is received | Frame size and the performance of AP and non-AP STAs | BSS-Controllable
T5 | time interval between the actual frame transmission start time and The time ACK for the retransmission is received | Outside interference | BSS-Uncontrollable
Different segments of the latency for the transmission are caused by different factors.
According to the factors the segments of the latency can be divided into two categories, BSS-controllable and BSS-uncontrollable.
This contribution focuses on the intra-BSS access delay and inter-BSS access delay

## Slide 8: Current Specification of BSS Access Delay
The related definitions of access delay in current 802.11 standard ( 802.11 – 2016 ), showed in the following, don’t differentiate the intra-BSS and inter-BSS access delay:
Access delay is measured by the AP’s or PCP’s MAC layer being the average medium access delay for transmitted frames measured from the time the MPDU is ready for transmission (i.e., begins CSMA/CA access or SP access, as appropriate) until the actual frame transmission start time. Access delay measurement results are included in the BSS Average Delay element and in the BSS AC Access Delay element.
BSS Average Access Delay element contains the AP Average Access Delay, which is a measure of load in the BSS and is available in both QoS APs and non-QoS APs.
BSS AC Access Delay element: The BSS AC Access Delay element contains an Access Category Access Delay field

## Slide 9: Differentiation of the intra-BSS and inter-BSS access delay
The statistics of the intra-BSS and inter-BSS access delay helps to analyze the communication environment of interior BSS and overlap BSS and distinguish the principal factors which lead to the relatively large latency. AP and non-AP STAs can use the different types of latency statistics to adjust the transmission strategy, especially for MLO.
The intra-BSS access delay reflects the BSS-controllable communication environment, which means it can be improved through admission control and optimization of transmission scheduling in the BSS.
the inter-BSS access delay reflects the BSS-uncontrollable communication environment, which means it can be improved by the avoidance from the communication frequency of current BSS, such as multi-AP mechanism.
Generally the usage of the intra-BSS and inter-BSS access delay is not only advantageous to estimate whether it is feasible to transmit the low-latency service in the communication environment, but also provide the basis on the optimization of transmission strategies.

## Slide 10: Proposal
This contribution proposes to add the following latency statistics in 802.11be, which helps to distinguish the principal factors which lead to the relatively large latency.
BSS Access Delay for intra-BSS transmission: measured by the AP or non-AP STA’s MAC layer being the statistics for time interval of waiting time for intra-BSS transmission from the time the MPDUs are ready for transmission until the actual frame transmission start time.
BSS Access Delay for inter-BSS transmission: measured by the AP or non-AP STA’s MAC layer being the statistics for time interval of waiting time for inter-BSS transmission from the time the MPDUs are ready for transmission until the actual frame transmission start time.

## Slide 11: Conclusions
The classification of latency helps to analyze the current communication environment and distinguishes the principal factors which lead to the relatively large latency.
This contribution proposes to add the latency statistics including BSS Access Delay for intra-BSS transmission and BSS Access Delay for inter-BSS transmission.

## Slide 12: Straw Poll 1
Do you support that the statistical parameters of BSS Access Delay for intra-BSS transmission and BSS Access Delay for inter-BSS transmission are added in 802.11be?
BSS Access Delay for intra-BSS transmission: measured by the AP or non-AP STA’s MAC layer being the statistics for time interval of waiting time for intra-BSS transmission from the time the MPDUs are ready for transmission until the actual frame transmission start time.
BSS Access Delay for inter-BSS transmission: measured by the AP or non-AP STA’s MAC layer being the statistics for time interval of waiting time for inter-BSS transmission from the time the MPDUs are ready for transmission until the actual frame transmission start time.
Note: the detailed specification of the statistical parameters is TBD.

## Slide 13: References
11-18-1231-06-0eht-eht-draft-proposed-par, 802.11 EHT Proposed PAR
11-18-1233-07-0eht-eht-draft-proposed-csd, IEEE 802.11 EHT draft Proposed CSD
11-19-1933-01-00be-capabilities-to-support-time-aware-scheduling-in-802-11be
11-19-1081-01-00be-multi-link-aggregation-gain-analysis-latency,Multi-Link Aggregation: Latency Gains
11-20-0105-03-00be-link-latency-statistics-of-multi-band-operations-in-eht

## Slide 14
Thank you!