## Slide 1: Multiple Link Operation Follow Up
Date: 2020-03-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Multi Link Operation
Multiple presentations discussed the multi link operation:
  AP MLD has the capability of transmitting while receiving at the same time (T&R)
    AP MLD with the capability of receiving in multiple links where the receptions can start at the different time
  STA MLD has T&R capability or no-T&R capability.
  Different mechanisms were proposed for STA MLD with no-T&R capability:
    1), Synchronized transmission by STA MLD (transmission of multiple links with same start time)
      One link includes the primary channel and other links are treated as secondary channel.
      Several variants to this were proposed.
    2), Each link does independent backoff.
    3), synchronized transmission through AP MLD’s help.

## Slide 3: Independent Transmission by STA MLD
STA MLD with capability no-T&R does backoff independently in each link:
  When the backoff procedure in one link, one PPDU is transmitted in the link.
The throughput is not as good as combined transmission.
When one link is used for PPDU transmission, the STA MLD loses the information of another link’s activity.
Link1
Link2
MAC/PHY in link1
MAC/PHY in link2
AP MLD1
MAC/PHY in link1
MAC/PHY in link2
AP MLD2
MAC/PHY in link1
MAC/PHY in link2
STA MLD2
STA MLD2’s backoff
TXOP with STA MLD2’s UL PPDU to AP MLD1
STA MLD2’s backoff
AP MLD2’s DL PPDU
STA MLD2’s backoff
TXOP with STA MLD2’s UL PPDU to AP MLD1
Option1: address the issue.
  Treat as ProbeDelay or NAVSyncDelay (simple and in line with baseline).
  AP MLD’s help, notification of another link’s activity in one link (e.g. notify the link1’s activity in link2 in the figure, whether there is transmission during the TXOP or the remaining NAV timer value of AP’s link1).
Option 2: ignore the issue.

## Slide 4: Synchronized Transmission by STA/AP MLD
It is difficult to get the same length PPDUs of with the responding frames, e.g. BAs, in multiple links based on the current responding rules (MCS/rate selection rules).
  This makes synchronized transmission complicated.
Solution:
  The TXOP responder can select MCS/rate by itself.
  The TXOP initiator announce the same PPDU length of the responding PPDUs.
  The IFS can longer than SIFS, but no more than PIFS (simple solution).
  The BA bitmap can be longer than the official BA Bitmap size per the negotiated BA buffer size.
  The dummy Per AID TID Info fields can be added to Multi-STA BA.
Link1
Link2
DL A-MPDU3
to STA MLD1
DL A-MPDU4
to STA MLD1
QoS Null
Ack
STA MLD’s backoff
STA MLD’s backoff
UL A-MPDU2
UL A-MPDU1
DL BA2
DL BA1
Defer
UL BA2
UL BA1
DL A-MPDU5
to STA MLD1
DL A-MPDU6
to STA MLD1

## Slide 5: Synchronized Transmission by STA MLD
When two links are in same band, simultaneous transmission in two links through backoff in one link and PIFS idle/busy check in another link is allowed.
When STA MLD (simplified text of link1 STA affiliated with STA MLD) finishes backoff in one link, the STA MLD optionally reserves the TXOP and transmits in two links at the same time once its another link’s backoff counter becomes 0:
  Same issue may need to be addressed as in slide 3.
  If no protection is done in in the link where the backoff counter becomes 0 earlier, the link needs to be kept idle before another link’s backoff counter becomes 0.
Link1
Link2
UL A-MPDU3
UL A-MPDU4
QoS Null
TXOP owned by STA MLD
Ack
STA MLD’s backoff
STA MLD’s backoff
UL A-MPDU2
UL A-MPDU1
DL BA2
DL BA1
Defer
TXOP owned by STA MLD

## Slide 6: Best-effort Synchronized Transmission
When STA MLD (simplified text of link1 STA affiliated with STA MLD) finishes backoff in one link, the STA MLD starts the normal frame exchanges and ask AP MLD help of synchronized transmission if possible:
Link1
Link2
UL A-MPDU3
UL A-MPDU4
TXOP owned by STA MLD
STA MLD1’s backoff
AP MLD’s backoff
DL Trigger
STAMLD1’s UL A-MPDU2
DL A-MPDU to
STA MLD2
DL BA2
DL BA1
TXOP owned by AP MLD (AP may schedule other STA)
Trigger
Synchronized TX Indication + next UL PPDU Length
Link1
Link2
UL A-MPDU3
UL A-MPDU4
TXOP owned by STA MLD1
STA MLD1’s backoff
AP MLD’s backoff
DL Trigger
STAMLD1’s UL A-MPDU2
DL A-MPDU to
STA MLD2
DL BA2 +Trigger
DL BA1
TXOP owned by AP MLD
Trigger
Synchronized TX Indication + next UL PPDU Length
TXOP owned by AP MLD

## Slide 7: Synchronized Transmission by AP MLD’s Help
When STA MLD (simplified text of link1 STA affiliated with STA MLD) finishes backoff in one link, the STA MLD solicits AP MLD to transmit Trigger frames in multiple links:
  Once the AP accepts the solicitation, the TXOP owner is transferred to P MLD.
  The AP can reject the solicitation within the responding frame.
    STA can continue its TXOP without another backoff.
Link1
Link2
UL A-MPDU3
UL A-MPDU4
RTT
TXOP owned by AP MLD
Ack
STA MLD’s backoff
AP MLD’s backoff
DL Trigger
DL Trigger
UL A-MPDU2
UL A-MPDU1
DL BA2+Trigger
DL BA1+Trigger
Defer gap
TXOP owned by AP MLD
TXOP owned by STA MLD

## Slide 8: Wrong Responding from Multiple Links
The AP MLD needs to do one of the following when the frame exchange with wrong response (or no response) from the STA MLD in multiple links is not the first one in the TXOP:
  1), PIFS recovery for multiple links if the AP MLD still wants to transmit simultaneous multiple PPDUs to one STA MLD with no-T&R capability.
Link1
Link2
Primary 20MHz
channel
Primary
20MHz channel
DL A-MPDU2
to STA MLD2
DL A-MPDU1 To STA MLD1
UL BA1
UL BA2
BA buffer size of TID 2 is 256.
Trigger to
STA MLD1
Trigger to
STA MLD1
UL A-MPDU3
from STA MLD1
DL BA3
UL A-MPDU4
From STA MLD1
DL BA4
Trigger to
STA MLD1
Trigger to
STA MLD1
PIFS
Link1
Link2
Primary 20MHz
channel
Primary
20MHz channel
DL A-MPDU2
to STA MLD2
DL A-MPDU1 To STA MLD1
UL BA1
UL BA2
BA buffer size of TID 2 is 256.
DL A-MPDU3
to STA MLD1
UL BA3
DL A-MPDU4
to STA MLD1
UL BA4
PIFS
DL A-MPDU3
to STA MLD1
DL A-MPDU4
to STA MLD1

## Slide 9: Wrong Responding from Multiple Links
The AP MLD needs to do one of the following when the frame exchange with wrong response from the STA MLD in multiple links is not the first one in the TXOP:
  2), either PIFS recovery or backoff recovery in any link if AP MLD wants to transmits the PPDUs to one STA MLD with T&R capability in multiple link.
    An variant to this is that PIFS recovery is used for both links if AP MLD wants to transmits the PPDUs to one STA MLD with T&R capability in multiple link
  3), either PIFS recovery or backoff recovery in any link if AP MLD wants to transmits the PPDUs to different STA MLDs in different links.
    A variant to this is that PIFS recovery is used for both links if AP MLD wants to transmits the PPDUs to different STA MLDs in different links.
Link1
Link2
Primary 20MHz
channel
Primary
20MHz channel
DL A-MPDU2
to STA MLD2
DL A-MPDU1 To STA MLD1
UL BA1
UL BA2
BA buffer size of TID 2 is 256.
Trigger to
STA MLD1
Trigger to
STA MLD1
UL A-MPDU3
from STA MLD1
DL BA3
UL A-MPDU4
From STA MLD2
DL BA4
Trigger to
STA MLD1
Trigger to
STA MLD2
PIFS
Link1
Link2
Primary 20MHz
channel
Primary
20MHz channel
DL A-MPDU2
to STA MLD2
DL A-MPDU1 To STA MLD1
UL BA1
UL BA2
BA buffer size of TID 2 is 256.
DL A-MPDU3
to STA MLD1
UL BA3
DL A-MPDU4
to STA MLD1
UL BA4
PIFS
DL A-MPDU3
to STA MLD2
DL A-MPDU4
to STA MLD2
STA MID1 has no T&R capability.
STA MLD2 has T&R capability.

## Slide 10: Wrong Responding from One Link
The AP MLD needs to do one of the following when the frame exchange with wrong response (no response) from the STA MLD in one link is not the first one in the TXOP:
  1), scheduling the UL transmission or doing the DL transmission with another STA MLD after PIFS or backoff recovery.
Link1
Link2
Primary 20MHz
channel
Primary
20MHz channel
DL A-MPDU2
to STA MLD2
DL A-MPDU1 To STA MLD1
UL BA1
UL BA2
BA buffer size of TID 2 is 256.
Trigger to
STA MLD1
Trigger to
STA MLD1
UL A-MPDU3
from STA MLD1
DL BA3
UL A-MPDU4
From STA MLD3
DL BA4
Trigger to
STA MLD3
PIFS
Link1
Link2
Primary 20MHz
channel
Primary
20MHz channel
DL A-MPDU2
to STA MLD2
DL A-MPDU1 To STA MLD1
UL BA1
UL BA2
BA buffer size of TID 2 is 256.
DL A-MPDU3
to STA MLD1
UL BA3
DL A-MPDU4
to STA MLD1
UL BA4
DL A-MPDU5
to STA MLD1
DL A-MPDU4
to STA MLD3
UL BA5

## Slide 11: Wrong Responding from One Link
The AP MLD needs to do one of the following when the frame exchange with wrong response from the STA MLD in one link only is not the first one in the TXOP:
  2), no transmission in this round and scheduling the UL transmission with the same STA MLD in the following frame exchange.
    During the no transmission period, the medium needs to be idle in the link for the following frame exchange.
Link1
Link2
Primary 20MHz
channel
Primary
20MHz channel
DL A-MPDU2
to STA MLD2
DL A-MPDU1 To STA MLD1
UL BA1
UL BA2
BA buffer size of TID 2 is 256.
Trigger to
STA MLD1
Trigger to
STA MLD1
UL A-MPDU3
from STA MLD1
DL BA3
UL A-MPDU5
from STA MLD1
DL BA5
UL A-MPDU4
From STA MLD1
DL BA4
Trigger to
STA MLD1
Trigger to
STA MLD1
Link1
Link2
Primary 20MHz
channel
Primary
20MHz channel
DL A-MPDU2
to STA MLD2
DL A-MPDU1 To STA MLD1
UL BA1
UL BA2
BA buffer size of TID 2 is 256.
DL A-MPDU3
to STA MLD1
UL BA3
DL A-MPDU4
to STA MLD1
UL BA4
DL A-MPDU5
to STA MLD1
DL A-MPDU4
to STA MLD3
UL BA5
Medium idle period for the
following Trigger Tx
Medium idle period for the
following DL Tx

## Slide 12: Straw Poll 1
Do you support that an AP MLD needs to do one of the following when the frame exchange with wrong response (or no response) from the STA MLD in multiple links is not the first one in the TXOP:
  PIFS recovery for multiple links if the AP MLD still wants to transmit simultaneous PPDUs to one STA MLD with no T&R capability.
  either PIFS recovery or backoff recovery in any link if AP MLD wants to transmits the PPDUs to one STA MLD with T&R capability.
  either PIFS recovery or backoff recovery in any link if AP MLD wants to transmits the PPDUs to different STA MLDs in different links.

## Slide 13: Straw Poll 2
Do you support that an AP MLD needs to do one of the following when the frame exchange with wrong response (no response) from the STA MLD in one link is not the first one in the TXOP:
  scheduling the UL transmission or doing the DL transmission with another STA MLD after PIFS or backoff recovery.
  no transmission in this round and scheduling the UL transmission with the same STA MLD in the following frame exchange.
    During the no transmission period, the medium needs to be idle in the link for the following frame exchange.

## Slide 14: Straw Poll 3
Do you support that when two links are in same band, simultaneous transmission in two links through backoff in one link and PIFS idle/busy check in another link is allowed?

## Slide 15: Straw Poll 4
Do you support that when a STA MLD finishes backoff in one link, the STA MLD optionally reserves the TXOP and transmits in two links at the same time once its another link’s backoff counter becomes 0:
  If no protection is done in in the link where the backoff counter becomes 0 earlier, the link needs to be kept idle before another link’s backoff counter becomes 0.