## Slide 1: Multi-link Group Addressed Data Delivery
Date: 2020-03-15
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Daniel F Bravo |  |  |  | 
Arik Klein |  |  |  | 
Laurent Cariou |  |  |  | 
Notes: September 2012

## Slide 2: Background
Individual addressed data delivery for a TID is basically agreed
group addressed data delivery needs to be discussed
Currently, group addressed data delivery uses DTIM

## Slide 3: SN Space and operation of Current Group Addressed Frame
Based on Table 10-5—Transmitter sequence number spaces, group addressed data shares the same sequence number space of non-QoS Data
Based on Table 10-6—Receiver caches, STA maintains most recent <Address2, sequence number, fragment number> and drops a receive group addressed or non-QoS if receives frame has retry bit set and matches this record
A group addressed frame is never transmitted twice under non-GCR mechanism
Group addressed data frame and non-QoS data frame are transmitted in order

## Slide 4: Shared SN Space or Different SN Space for Group Addressed Frame across links
Shared SN space for group addressed frame across links
  Unlike individual addressed frame consideration, there is no need for reordering
  Complicate the SN assignment with non-QoS frame and different multicast stream across links
  Maintain in order transmission will be difficult while transmit together with non-QoS frame or switch links to transmit multicast stream
  May help on duplicate detection
Different SN space for group addressed frame across links
  Avoid all the problem of above
  We have already agreed to have different key anyway
  Need handling of duplicate avoidance, which we will talk about later
We propose different SN space for group addressed frame across links

## Slide 5: Non-AP MLD operation
To avoid duplicate, non-AP MLD shall select one link to receive group addressed data and discard group addressed data from other links
  Follow DTIM operation like today
Non-AP MLD can change the link to receive group addressed data frame
While changing links, there can be duplicate or missing group addressed
  we think we do not need 100% prevention, and some AP guidance will be enough

## Slide 6: Duplicate and Miss Group Addressed Frame
Duplicate detection:
  There is no need for duplicate detection today because group addressed frame is not retry anyway.
  Duplicate group addressed may happen while roaming, and there is no specific mechanism to 100% avoid this
Miss detection
  More data bit signal existence of additional group address for the non-AP STA to avoid missing
  Miss may happen due to reception error, and there is no specific mechanism to guarantee reception
Duplicate detection and Miss detection for multi-link should be for avoiding aggravating existing situation rather than 100 % prevention

## Slide 7: Duplicate and Miss Group Addressed Frame
Use DMS
  The last measure if duplicate and miss needs to be resolved definitely
AP guidance
  Without AP guidance, no way for non-AP MLD to figure out what is duplicate due to independent SN space
  Without AP guidance, no way for non-AP MLD to figure out what is missed regardless of shared or not shared SN space
To utilize AP guidance,
  Non-AP MLD may indicate the selected link for receiving group addressed data frame to AP MLD
  While AP MLD notices link changing for receiving group addressed frame, AP MLD indicates the time to start receiving group addressed frame in the selected link to avoid duplicate
  Non-AP MLD may request for guidance to change the selected link for receiving group addressed frame, and AP MLD can provide guidance to stop receiving group addressed frame in the current selected link to avoid missing

## Slide 8: Additional Benefits of AP MLD to know the selected link to receive group addressed frame
There are proposals to avoid triggering UL operation while one link is receiving group addressed frame
If AP does not know which link non-AP MLD selects to receive group addressed frame, then a lot of time that can be used for triggering UL operation is wasted
DTIM period
DTIM period
Total period of no triggering UL operation

## Slide 9: Additional Benefits of AP MLD to know the selected link to receive group addressed frame
There are two types of group addressed data
  Broadcast addressed
  Multicast addressed (used this to mean group addressed except broadcast addressed in this presentation)
Broadcast addressed data is likely to be transmitted on all the links of an AP MLD due to existence of legacy STAs
For multicast addressed data, this may not be the case.
  Currently, AP knows which STA subscribes to a multicast group through layer 3 method. As a result, a multicast addressed stream may not be sent by the AP if no non-AP STA subscribes to the group
  For an AP MLD, AP MLD knows which non-AP MLD subscribes to a multicast group. However, AP MLD does not know which link non-AP MLD camps to receive group addressed data frame
Without knowing which link a non-AP MLD is used to receive group addressed data frame, the group addressed data frame is forced to transmit on all the links and overload the system

## Slide 10: Example
For simplicity, assume only non-AP MLD subscribes a multicast group (a specific multicast group address)
AP MLD does not know which link a non-AP MLD is used to receive this multicast stream and send the stream on all the links
AP MLD and non-AP MLD configures a link, say link 2 to receive this multicast stream

## Slide 11: Conclusion
We discuss multi-link group addressed data delivery
We propose the following:
  Different SN space for group addressed frame across links
  non-AP MLD may indicate the selected link to receive group addressed data frame to AP MLD
  AP provides guidance on changing the selected link to receive group addressed data frame

## Slide 12: Straw Poll
Do you support that different SN space for group addressed data frame are used in different links?

## Slide 13: Straw Poll
Do you support that non-AP MLD may indicate the selected link to receive group addressed data frame to AP MLD?

## Slide 14: Straw Poll
Do you support that 11be defines a mechanism for AP MLD to provide guidance and help non-AP MLD to change the selected link to receive group addressed data frame and avoid duplicate and missing group addressed data frame?