## Slide 1
Multi-AP Sounding Discussion Follow Up
Date: 2020-03-18
Authors:
Name | Affiliation | Address | Email
Qichen Jia | ZTE Corporation | No.9 Wu Xing Section Xi Feng Road Xi’an, Shaanxi Province P.R.China | 
Ning Wei |  |  | 
Bo Sun |  |  | sun.bo1@zte.com.cn
Yonggang Fang |  |  | 
Sang Sun |  |  | 

## Slide 2: Introduction
A code based method for multi-AP joint sounding was investigated in contribution[1].
More analysis and simulations are provided to show the performance of code based method in the contribution.

## Slide 3: Code based method:Recap[1]
The new multi-AP code based joint sounding procedure
  An AP transmits a frame (e.g. Trigger) to other APs to initiate the multi-AP joint sounding procedure.
  All sounding APs send an MAP-NDPA + MAP-NDP simultaneously.
          A MAP-NDP sounding frame consists of a EHT-LTF sequence generated by the orthogonal sequence.
EHT-LTF sequence generation
  The EHT-LTF sequence is carried in a MAP-NDP sounding frame.
  An orthogonal sequence from P matrix is assigned to an AP in the multi-AP joint sounding to generate its EHT-LTF.
    The dimension of orthogonal matrix should be larger than or equal to the number of APs in the joint sounding.
    An example of orthogonal matrix is [1 -1 1 1, 1 1 -1 1, 1 1 1 -1, -1 1 1 1], the orthogonal sequences assigned to APs: AP1 = [1 -1 1 1 ], AP2 = [1 1 -1 1], AP3 = [1 1 1 -1] and AP4 = [-1 1 1 1].
  An AP creates its EHT-LTF sequence via multiplying the LTF sequence by its assigned orthogonal sequence.
    For example, EHT-LTF is generated by LTF (e.g. used in 11ax) multiplied by an orthogonal sequence.
LTF (e.g. 11ax)
Orthogonal sequence
EHT-LTF sequence

## Slide 4: Simulation Setup
Objectives
  This additional simulation intends to compare the performance of the Code-Based(CB) multi-AP joint sounding method to Tone-Selection(TS) multi-AP sounding method.
Simulation setting
  2 APs / 4APs : each AP has 4 Tx antennas; 1 STA: the STA has 4 Rx antennas
  LTF Type : 4x LTF
  Channel bandwidth: 20MHz
  Channel mode: Channel mode D with Gaussian noise
  Residual CFO: 0Hz,50Hz, 100Hz, 200Hz.
  Perfect synchronization / Residual STO:[-a,a], a= 5% , 10% , 20% sample.
  Orthogonal matrix P:

## Slide 5: Performance Analysis
Diagram of Tone-Selection(TS) sounding method and Code-based(CB) sounding method in receiver are at same SNR.
  Based on the contribution[2], cross leakage is contained in CB method.
  The main effect on the estimated value of TS method and CB method is noise and noise + leakage.
······
······
leakage
tone-selection method
code-based method

## Slide 6: Performance Analysis
  For leakage, the leakage should be very little if the flat channel.
    a channel can be considered as flat in coherence bandwith.
      In channel D, the coherence bandwith approach to 2MHz, which coherence bandwith include 6 subcarriers approximately in 20BW and 1x type.
    the effect of leakage can be ignored if the channel is flat.
  For noise, TS method is more affected by noise than CB method in low SNR.
    the noise effect of TS method and CB method is in the two subcarriers as follow.
  So, the CB method should be better than TS method in low SNR, but slightly worse in High SNR.

## Slide 7: Simulation Results (1)
Channel Estimation Performance
  the multi-AP code-based joint sounding and the multi-AP tone-selection joint sounding in 2AP case.
It is a performance intersection between code-based and tone-selection method, Assume the part less than the intersection is low SNR and much than the intersection is high SNR.
code-based channel estimation performance is about 2dB better than tone-selsetion in low SNR.
The intersection moves left with residual CFO incerase.

## Slide 8: Simulation Results (2)
Channel Estimation Performance
  the multi-AP code-based joint sounding and the multi-AP tone-selection joint sounding in 4AP case
The performance trend of 4AP case is same as 2AP case, but the gap which between the code-based and tone-selection method in 4AP case is larger than it in 2 AP case.

## Slide 9: Simulation Results (3)
Channel Estimation Performance
  the Residual STO effect for the performance
The performance have a huge attenuation with residual STO and residual STO have similar effect on code-based and tone-selection method.

## Slide 10: Conclusion
In this contribution, we provided some simulated to show the performance of code-based joint sounding method and tone-selection joint sounding method.
Code-based method should be better than Tone-selection method in Low SNR, but slightly worse in high SNR.
Synchronous error have the similar effect on code-based joint sounding method and tone-selection joint sounding method.

## Slide 11: Reference
[1] 11-20-0052-00-00be-multi-ap-sounding-discussion
[2] 11-19-1867-00-00be-performance-comparisons-for-ltf-designs-for-eht