## Slide 1: Sync transmission for non-STR MLD
Date: 2020-04-01
Authors:

## Slide 2: Background
Non-STR
  An MLD that is not capable of simultaneous Tx/Rx on multiple links for the given set of links (i.e., it can only do Tx/Tx or Rx/Rx on all links)
STR
  An MLD that is capable of simultaneous Tx/Rx on multiple links for the given set of links (i.e., it can do Tx/Rx on all links)
  Lots of contributions [1-6] touched the transmission scheme for the non-STR STA MLD
  Assume that the AP MLD is STR
  Some of them are fancy, such as self-injurious behaviors, some of them may disobey regulatory
  In this contribution, we try to pick out some simply schemes
  The application scenario: the AP MLD is STR, the STA MLD is non-STR

## Slide 3: Recap
There are two types of Sync PPDU transmission
  Type 1： Both the starting time of two PPDUs and the ending time of two PPDUs are aligned
  May violate the regulation and result in unfairness
  Type 2：Only the ending time of two PPDUs is aligned
  Independent back-off on each link
  Both two options could achieve better throughput again compared with backoff suspending. And Type 2 is more feasible than Type 1.
  In the following slides, we focus on type 2 Sync PPDU transmission
PPDU 1
PPDU 2
Link 1
Link 2
PIFS check
Type 1
PPDU 1
PPDU 2
Link 1
Link 2
Type 2

## Slide 4: Sync PPDU transmission initialized by AP MLD (DL transmission)
Case 1: each AP in the AP MLD transmits the PPDU independently on each link
  The ending time of the two PPDUs requires to be aligned
  PPDU also could be trigger frame or contain a triggering frame
  The response frames of these two PPDUs have the same transmission time
AP 1
STA 1
AP 2
STA 2
STR
AP MLD
Non-STR
STA MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
PPDU2
BA
BA
PPDU 1
A-MPDU
A-MPDU
BA
BA

## Slide 5: Sync PPDU transmission initialized by AP MLD (UL transmission)
Case 2: one AP sends a trigger frame to a STA in the non-AP MLD on one link and another AP in the same AP MLD does not send any frame on the second link
  The STA 2 in the same STA MLD could access the link 2 after the end of Trigger frame in the link 1, but the staring time of PPDU 2 shall be not later than PPDU 1
  The ending time of two PPDUs sent by the STA MLD shall be aligned
  Case 2 extension: the staring time of PPDU 2 could be later than PPDU 1, but a conservative ED level is used in this case (see case 4)
AP 1
STA 1
AP 2
STA 2
STR
AP MLD
Non-STR
STA MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
Trigger frame
PPDU 1
PPDU 2
BA
BA

## Slide 6: Sync PPDU transmission initialized by STA MLD (UL transmission)
Case 3: one STA sends a PPDU to an AP MLD on one link while another STA in the same MLD does nothing
  An AP in a AP MLD sends PPDU 2a to respond the received PPDU 1
  If the AP MLD wants to send another PPDU in link 2 to the same STA MLD, then shall align the end time of the 2 transmitted PPDUs, same as case 1
AP 1
STA 1
AP 2
STA 2
STR
AP MLD
Non-STR
STA MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
PPDU 1
PPDU 2a
PPDU 2b
BA
BA

## Slide 7: Sync PPDU transmission initialized by STA MLD (UL transmission)
Case 4: one STA sends a PPDU to an AP MLD on one link while another STA in the same MLD tries to access the second link by lowering ED level
  Do self-interference leakage estimate (X dBm) at the beginning, and check it periodically
  Use a conservative ED level, such as （-62-X ）dBm for 20 MHz
AP 1
STA 1
AP 2
STA 2
AP MLD
STA MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
PPDU 1
BA
BA
PPDU 2
Use a conservative ED level

## Slide 8: Async PPDU transmission
For the four cases mentioned before, if the two PPDUs have either different TA addresses or different RA addresses, no specific requirement is needed
  It is straightforward to use async PPDU transmission
AP 1
STA 1
AP 2
STA 2
AP MLD
STA MLD
Link 1
STA1
AP1
Other STA
AP2
Link 2
Trigger frame
PPDU 1
PPDU 2
BA
BA
STA2
AP2
Link 2
Example

## Slide 9: Summary
We propose four Sync PPDU transmission modes and all of them require that the ending time of two PPDUs is aligned
  Case 1 Case 2 and Case 3 are simply schemes
  Case 2 extension and Case 4 could also be implemented to enhance the throughput performance.

## Slide 10: References
[1] IEEE 802.11-20/1916r0 MLO-Asynch-Qsynch-Synch
[2] IEEE 802.11-20/0455r0 Async multi-link operation for non-STR STA
[3] IEEE 802.11-20/0291r1 MLO a-synchronize and synchronize operation discussions
[4] IEEE 802.11-20/0444r0 MLA: Non-STR STA EDCA rules after self-interference
[5] IEEE 802.11-20/0414r0 Method for Handling Constrained MLD,
[6] IEEE 802.11-20/26r3 MLO: Sync PPDUs, Duncan Ho

## Slide 11: SP 1
Do you agree that an AP MLD shall align the end of DL PPDUs that are sent simultaneously on multiple links to the same non-STR non-AP MLD, in such a way that the response to any of the PPDUs will not overlap with any of the DL PPDUs