## Slide 1: MLO: Reachability Problem
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-03-15

## Slide 2: Problem Statement
RF propagation characteristics are different on for each band
  2.4 GHz has a longer range compared to 5 or 6 GHz.
Further APs of an MLD may operating at different TxPower on their respective links
  An AP may operate with a lower TxPower than the max allowed TxPower (as a deployment choice or other reasons)
During discovery, a non-AP MLD should not be required to enable all radios to scan each support link of an AP MLD to determine if it can hear all the APs of an AP MLD.
In associated state, a non-AP MLD can save power by turning certain radios off if it determines that it can’t close the link with the AP MLD on certain links
MLO framework needs to provide a mechanism to help a non-AP MLD determine if it can reach the AP MLD on all links
AP-MLD
Non-AP-MLD
AP MLD reachable on 2.4 link
AP MLD unreachable on 5/6 GHz links

## Slide 3: Solution Summary
An AP of an MLD provides TxPower information of all the APs affiliated with that MLD.
Based on TxPower numbers, the non-AP can compute a rough (first order) estimate of its reachability on different links.

## Slide 4: Estimation of Reachability
A STA can compute the path-loss to an AP if it knows the transmit power of a received frame from the AP.
  PLL1 = TxPL1 – RxPL1
Further, a STA can make a rough estimation of the whether an AP on another link is reachable based on path-loss on the current link and TxPower for the other link
  RxPL2 = TxPL2 – f(PLL1)
AP-MLD
Non-AP-MLD
TxP (L1)
RxP (L1)
PL (L1)
TxP (L2)
TxP (L3)
PL (L2) = F(PL (L1))
PL (L3) = F(PL (L1))
RxP (L2)*
RxP (L3)*
* Estimated value

## Slide 5: Indication of per-link TxPower
In order to facilitate reachability estimation, the Beacon and Probe Response frames transmitted by an AP of an MLD must indicate:
  The TxPower with which the frame was transmitted
  TxPower information of the Beacon frame for the other links supported by the AP MLD
Alternatively, the AP MLD can provide an indication of the TxPower difference with respect to the transmitting link
  The STA knows the RSSI of the beacon frame received on the current link and based on the power difference, it can compute the estimated RSSI for the beacon on the other link(s)
  Provide the power difference w.r.t. Beacon frame
    E.g., is a signed value and unit of dBm.

## Slide 6: Benefits
During discovery, aids in selecting an AP MLD with which the non-AP MLD has determined to have strong reachability on multiple links
  Without requiring to scan multiple links (saves power)
During regular operation, helps non-AP MLD save power by entering power-save state on links that are unreachable
Can influence roaming decisions at the non-AP MLD.

## Slide 7: Summary
This contribution explains the need for advertising transmit power information for all the links so that a non-AP MLD can estimate the reachability on all links
  Helps client save power

## Slide 8: SP #1
Do you agree that for R1 an AP of an AP MLD shall provide in its ML Probe Response frame, sent in response to an ML Probe Request frame requesting complete information, the difference between the current AP’s beacon transmit power normalized to 20 MHz and the beacon transmit power of a reported AP of the MLD normalized to 20 MHz, if the difference is non-zero?
  NOTE 1 – the TxPower Information will include positive or negative difference with respect to the reporting AP’s TxPower.
  NOTE 2: Exact element/field to carry TxPower Information is TBD
  Y:
  N:
  A: