## Slide 1: MLO: Reachability Problem
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-03-15

## Slide 2: Problem Statement
RF propagation characteristics are different on for each band
  2.4 GHz has a longer range compared to 5 or 6 GHz.
Further APs of an MLD may operating at different TxPower on their respective links
  An AP may operate with a lower TxPower than the max allowed TxPower (as a deployment choice or other reasons)
During discovery, a non-AP MLD should not be required to enable all radios to scan each support link of an AP MLD to determine if it can hear all the APs of an AP MLD.
MLO framework needs to provide a mechanism to help a non-AP MLD determine if it can reach the AP MLD on all links
AP MLD
Non-AP MLD
AP MLD reachable on 2.4 link
AP MLD unreachable on 5/6 GHz links

## Slide 3: Solution Summary
An AP of an MLD provides TxPower information of all the APs affiliated with that MLD.
Using the TxPower information, the non-AP can compute a rough (first order) estimate of its reachability on different links.

## Slide 4: Estimation of Reachability
A non-AP MLD can compute the path-loss in link 1 as follows
  PLL1 = TxPL1 – RxPL1
    where
      PLL1 = Path Loss on link 1,
      TxPL1 = Transmit power of AP on link 1
      RxPL1 = Received power at the non-AP STA 1
The non-AP MLD can roughly estimate whether an AP on another link is reachable
  RxPL2 = TxPL2 – ƒ(PLL1)
    where
      ƒ(PLL1) = estimated path-loss at link 2 based on known path loss value for link 1
      RxPL2 = Received power at the non-AP STA 2
      TxPL2 = Transmit power of AP on link 2
AP MLD
Non AP-MLD
TxPL1
RxPL1
PLL1
TxPL2
TxPL3
PLL2 = ƒ(PLL1)
PLL3 = ƒ(PLL1)
RxPL2*
RxPL3*
* Estimated value

## Slide 5: Indication of TxPower
In order to facilitate reachability estimation, the AP of an MLD indicates:
  TxPower of the Beacon on the transmitting link
  TxPower of the Beacon transmitted on other links of the AP MLD
TxPower expressed in EIRP to account for antenna gain
  Normalized to 20 MHz (if Beacon is sent with BW > 20 MHz)
TxPower info. may also be included in ML Probe Response frames that carry complete profile
  Expectation is that providing the complete profile will be typical during discovery phase

## Slide 6: Indication of TxPower (contd)
Based on offline feedback, several members indicated a preference towards not advertising the absolute TxPower
  Simplifies signaling, reduces information being delivered over the air, etc.
Alternative approach: Delta Tx Power
  AP MLD provides the TxPower difference (Delta Tx Power) with respect to the transmitting link
    The STA knows the RSSI of the Beacon frame it receives on the current link
    Based on the Tx power difference, it can estimate RSSI for the beacon on the other link(s)
  TBD field would carry the Delta Tx Power (as a signed value)
    Delta TX Power is defined as the difference between the absolute TX powers (see previous slides)
∆Rx[L1 – L2] = ∆Tx[L1 – L2] – ƒ(∆PL[L1 – L2])
  Where:
    ∆Rx[L1 – L2] = difference in receive power between the reporting and reported links
      Non-AP MLD would know the Rx power on the scanning link (based on beacon Rx). This value tells if the RxPower on the other link is better or worst than the scanning link
    ∆Tx[L1 – L2] = difference in transmit power between the reporting and reported links
      Provided in the ML Probe Response and/or Beacons frames
    ƒ(∆PL[L1 – L2]) = estimated difference in pathloss between the two links
      Internal to each implementation

## Slide 7: Summary
This contribution motivates the need for advertising transmit power information for all the APs of the AP MLD.
  Aids a scanning non-AP MLD estimate the reachability on all links without requiring it to power on all the radios

## Slide 8: Additional Discussion
This contribution addresses the topic of downlink reachability with an AP operating on another link.
Although uplink is not the focus of this contribution, there can be other contributions complementary to this one to investigate/address that topic
  If the STA has difficulty closing the uplink, it has various tools at its disposal (such as ER SU PPDU, TB PPDU etc)
We understand that each AP may have different antenna gains
  The TxPower information is expressed in EIRP to account for antenna gain on the respective link

## Slide 9: SP #1
Do you agree that for R1:
  An AP of an AP MLD shall provide in its ML Probe Response frame, sent in response to an ML Probe Request frame requesting complete information, the difference between the current AP’s beacon transmit power normalized to 20 MHz (in EIRP) and the beacon transmit power of a reported AP of the MLD normalized to 20 MHz (in EIRP), if the difference is non-zero?
    NOTE 1 – the TxPower Information will include positive or negative difference with respect to the reporting AP’s TxPower.
    NOTE 2: Exact element/field to carry TxPower Information is TBD
  Y:
  N:
  A: