## Slide 1: Discussion on Channels for Multi-link Operation
Authors:
Date: 2020-04-05

## Slide 2: Introduction
11be defined a multi-link device (MLD) [1].
  An MLD includes multiple affiliated STAs.
11be has not defined a constraint on channels that each link of an MLD occupies.
This contribution states problems with overlapped channels of a multi-link operation and proposes potential solutions.

## Slide 3: Multi-link channel configurations
Non-overlapped multi-link channels
  An MLD can have peak throughput gain by multi-link aggregations.
  Independent channel access on multiple links may provide channel access gain.
Overlapped multi-link channels
  It is difficult to have peak throughput gain by multi-link aggregations.
  It is also difficult to have channel access gain.
    When there is a transmission on one link, the other link would be sensed as busy.
  A STA on one link may interfere with transmissions on the other link.
Channel on which Link 2 operates
Channel on which Link 1 operates
Frequency
Frequency

## Slide 4: Overlapped channels example (1)
Channel environment example
  Assume that two radios of an MLD can operate up to 160 MHz band.
  However, only one 160 MHz channel is available due to incumbent devices.
  To utilize 160 MHz operation capabilties of both radios, a multi-link is configured in one 160 MHz channel using overlapped channels.
160 MHz
5170 MHz
5330 MHz
5250 MHz
5490 MHz
Weather radar
Link 1
Link 2
Multi-link setup
P20
P20

## Slide 5: Overlapped channels example (2)
320 MHz channelization example
  According to the SFD, 320 MHz channel can be consist of any two adjacent 160 MHz channels [1].
    “802.11be supports defining 320 MHz channels as any two adjacent 160 MHz channels.”
  A multi-link can be configured using two 320 MHz channels that are overlapped.
Link 1
Link 2
320 MHz
320 MHz

## Slide 6: Problems with overlapped channels (1/3)
PIFS backoff
  During a transmission on Link 1, a STA on Link 2 may check channel status of non-primary 20 MHz channels.
  With a CCA threshold for non-primary 20 MHz channels, there is a probability for the STA on Link 2 to interfere with the transmission on Link 1.
Link 1 of multi-link
Link 2 of multi-link
PPDU on Link 1
PIFS
PPDU on Link 2
3 | 2 | 1 | 0
Collision
Frequency
P20
P20
Link 2
Link 1

## Slide 7: Problems with overlapped channels (2/3)
Spatial reuse operation
  A STA on one link would receive a PPDU on the other link.
  If APs of an MLD select BSS color values independently, the STA on one link would receive a different BSS color value from the PPDU.
  Then the STA may perform a spatial reuse operation on the PPDU from the other link.
Link 1
(BSS color A)
Link 2
(BSS color B)
PPDU from AP on Link 1
Preamble detection
 Different BSS color
 Spatial reuse
PPDU from STA on Link 2
Collision

## Slide 8: Problems with overlapped channels (3/3)
Unnecessary decoding
  Even when there is an appropriate coordination on BSS color selection, there may be a lot of unnecessary decoding.
    A STA on one link cannot filter out a PPDU on the other link using BSS color.
  It may increase power consumption of an MLD.

## Slide 9: Potential solutions
1) An AP MLD configures a multi-link using non-overlapped channels.
2) It is allowed for an MLD to use overlapped channels with operations defined for this case.
  Example 1) Multiple links of an MLD use the same BSS color.
  Example 2) A STA recognizes multiple BSS color values as a corresponding value.

## Slide 10: Conclusion
This contribution presented possible problems when a multi-link is configured using overlapped channels.
11be specification needs to define a solution for the problems.

## Slide 11: References
[1] 11-19/1262r12 Specification Framework for TGbe

## Slide 12: Straw poll #1
Which option do you prefer to prevent problems of overlapped multi-link channels?
  Option 1) Restrict channel configurations established by an AP MLD
    e.g. Channels of a multi-link are not overlapped.
  Option 2) Define MLD operations when using overlapped channels
    e.g. BSS color selection rule between overlapped links

## Slide 13: Straw poll #2
Do you support that an AP MLD shall configure a multi-link using channels that are not overlapped each other?
  Y
  N
  A