## Slide 1: Discussion On Coordinated UL MU-MIMO
Date: 23-03-2020
Authors:
Name | Affiliation | Address | Phone | Email
Genadiy Tsodik | Huawei Technologies |  |  | 
Shimi Shilo |  |  |  | 
Yunbo Li |  |  |  | 
Jason Yuchen Guo |  |  |  | 

## Slide 2: Introduction
Various cooperation schemes are discussed as candidates for DL and UL coordinated transmissions
All the proposed schemes have advantages in certain scenarios, whereas in other scenarios - other schemes may be preferable
In [1] we introduced a Coordinated UL MU-MIMO transmission scheme and studied its properties and performance
In this contribution we want to review the scenarios where the proposed scheme has advantages and suggest it as a candidate scheme for UL Coordination

## Slide 3: Short Recap
The main idea [1] is to allow parallel UL transmissions of multiple BSSs by extending UL MU-MIMO defined in 11ax (not possible today with existing Trigger Frame type and formats)
Orthogonal LTF signals allow each AP to estimate channel of each STA independently and apply MIMO detection or interference mitigation
The suggested scheme doesn’t require phase synchronization, but requires a solution for triggering multiple STAs from different OBSS
We compared the performance of different interference mitigation schemes and showed an advantage of the proposed method
UL Coordination Negotiation Procedure
Coordinated UL Trigger
Data Frame
Master AP
Slave AP
STA1
STA2
Data Frame
MU-MIMO HE-LTF
MU-MIMO HE-LTF
Full Alignment
Time

## Slide 4: Discussed Coordination Schemes
Currently four main schemes were proposed for AP Coordination: Co-OFDMA, Co-SR, JT and CBF, where two last schemes are proposed for DL coordination
Co-SR and Co-OFDMA require minimal synchronization (or none) and allow multiple transmissions (DL and/or UL) during the coordination period
We want to focus on cases where the AP needs to trigger an UL transmission (with no preceding DL data packet)
  Co-OFDMA requires negotiation and agreement between APs preceding the coordinated transmission
  In case of Co-OFDMA the throughput will be reduced to 1/N per OBSS where N is the number of OBSSs participating in Co-OFDMA (assuming symmetric BF division)
  Co-SR introduces a trade-off between robustness and efficiency, and requires additional overhead in more complex schemes (like OBSS RSSI indication for PSR or channel sounding for PSR with Null Steering)
So we would like to have an additional solution that allows less throughput reduction and requires less (or similar) overhead for triggered UL data transmissions

## Slide 5: Triggered UL Data
We showed in [1] that Coordinated UL MU-MIMO can yield good performance compared with non-synchronized parallel transmissions with very small required overhead
  UL MU-MIMO requires only special trigger frame solution – it requires less overhead compared with channel sounding or RSSI monitoring
  No channel knowledge is required in advance – orthogonal LTF signals allow accurate channel estimation of all participants of MU-MIMO transmission
  UL MU-MIMO throughput increase will be in range of 50% to 200%, where it depends on channel properties and MIMO detection capabilities of AP – in worst case the throughput of UL MU-MIMO will be similar to Co-OFDMA
  Mitigation of synchronized interference requires less degrees of freedom (1 Rx antenna per interferer instead of 1 Rx antenna per interference path) – see [1]

## Slide 6: Procedure
The main flow should include three stages: negotiation (similar to Co-OFDMA), trigger, UL transmission (see diagram below)
The main question is how to trigger STAs from different BSSs
Today we can not transmit parallel TFs because each AP has different data to transmit and there is no solution for consecutive trigger frames
Thus to allow coordinated UL MU-MIMO we need to make all the TFs identical (in this case all the APs may transmit the same TF simultaneously)
UL Coordination Negotiation Procedure
Coordinated UL Trigger
Data Frame
Master AP
Slave AP
STA1
STA2
Data Frame
MU-MIMO HE-LTF
MU-MIMO HE-LTF
Full Alignment
Time
Coordinated UL Trigger

## Slide 7: Trigger Frame Design
We want to suggest a TF for Coordinated UL MU-MIMO with minimal modifications to the existing TF format
Two main aspects need to be addressed: BSS color and AID
BSS Color issue only existing in HE or EHT PPDU format
  BSS color set to 0, so that scheduled STA in each BSS will continue decode the payload;
AID solution:
  Option1: Divide AID range between APs – in this case every STA has unique ID and all the STAs can be triggered by using common BSS and their AIDs, thus no change to TF format is required
  Option2: Some indication is introduced to distinguish AID from different BSS. Need to modify the Trigger frame format, or define a new trigger type in this option.

## Slide 8: UL Coordination Schemes
Here we want to summarize the reviewed schemes and give their main properties
We can see in the table below that each scheme has its own advantages, requirements and overhead – thus Sharing AP may select a specific method that is preferable for a specific scenario
Scheme | Throughput Impact (Avg) | Required #Rx Ant | Synchronization (Time/Freq/Phase) | Channel Knowledge | Preprocessing Overhead
Co-OFDMA | Lower | Any # | Loose | Not Required | Trigger Frame
Co-SR | Medium | Any # | Time only | Not Required | OBSS RSSI Indication
Co-SR + Null Steering | Medium-High | >>1 | Time and Freq | Required | OBSS RSSI Indication + Sounding
Co-UL MU-MIMO | Medium-High | >>1 | Time and Freq | Not Required | Trigger Frame

## Slide 9: Standardization Aspects
802.11be agreed on two releases where only Low-complexity AP Coordination schemes will be developed for Release1
Coordinated UL MU-MIMO
  Doesn’t require any PHY change at STA side
  Doesn’t require tight synchronization (similar to other coordination schemes)
  Main modification is coordination and Trigger frame format, which are mainly MAC change.
Thus based on the details of this contribution we propose the following:
  Consider Coordinated UL MU-MIMO as an optional coordination scheme for triggered UL transmissions for Release1 of 802.11be

## Slide 10: Conclusion
We reviewed several scenarios with respect to UL Coordination
In case of triggered UL transmission (not following DL data) UL MU-MIMO schemes may have advantages in terms of overhead and performance (depending on the scenario)
Coordinated UL MU-MIMO may be considered as a candidate for UL coordination
Multiple UL Coordination schemes may be adopted to allow APs to adjust a selected scheme for a specific scenario
In main DL coordination scenarios UL MU-MIMO can be a candidate for UL response

## Slide 11: References
[1] 11-19-1979-01-00be-ul-coordination-for-throughput-improvement-and-interference-reduction

## Slide 12: SP1
Do you support that 802.11be will adopt Coordinated UL MU-MIMO as an optional coordination scheme for triggered UL transmissions?