## Slide 1: Power Efficient Broadcasting
Date: 2020-03-15
Authors:

## Slide 2
Abstract
In this contribution, we discuss proposals to address the power efficiency requirements for TGbc.

## Slide 3: Introduction
802.11bc has a requirement for power efficiency [1]
  TGbc R3.4.2: 802.11bc amendment shall have a mechanism to facilitate power-efficient broadcasting.
Potential source of wasted energy in E-BCS:
  APs keep on broadcasting when there are no longer consumers of the broadcast information
Broadcasting APs need to have the capabilities to ensure that there are consumers
  AP should stop broadcasting when it has detected that there is no STAs consuming the broadcast service
The exact method may depend on the characteristics of the DL traffic

## Slide 4: Ways to Prevent Energy Waste (1/4)
In some TGbc use cases, traffic may be constantly broadcast and rapidly changing, but due to heavy medium load, it should only be turned on when needed and turned off when no longer needed:
  Stadium live video/VR eSport Distribution
  Broadcast Services for Event Production
  Multi-lingual broadcast
For this class of use cases, there may be a number of ways to determine when to end broadcasting service in order to prevent energy waste
  Method 1: Negotiate broadcast service for a reasonable duration
  Method 2: Termination notice for broadcast services
  Broadcast service should be terminated once it is detected that there is no STA consuming the broadcast data
In some other use cases, traffic may be of small size, non-changing or slowly changing, but the information is broadcast periodically
  Intelligent Transportation Broadcast: train arrival
  Train schedule broadcasting at train stations
For this class of use cases, including a scheduling of broadcast may help STAs power save as well as announce the duration of the broadcast service
  Method 3: Advertisement of a schedule for a broadcast service(s)

## Slide 5: Ways to Prevent Energy Waste (2/4)
For use cases with traffic may be constant and rapidly changing, but due to heavy medium load, it should only be turned on when needed and turned off when no longer needed:
  Method 1: Negotiate broadcast service for a reasonable duration
  Method 2: Termination notice for broadcast services
Method 1: Negotiate broadcast service for a reasonable duration
  Unassociated and associated STAs may negotiate with an AP for particular broadcast services
    May be conducted through ANQP or e-BCS request/response exchanges
  An optional duration indication may be added to the negotiation to indicate the broadcast service may be provided for a reasonable amount of time
    In terms of time units, or for the entire duration of the broadcast service (e.g., a football match video)
  STAs needs to re-negotiate if they still desire the service at the end of the duration
    Security: In order to prevent a rogue device from continuously requesting extension of broadcast, the ultimate decision on whether to extend the broadcast lies with the AP.
  However, this option alone may not be sufficient:
    STAs are mobile and may move away before duration expires
    STAs that cannot transmit may also request e-BCS services

## Slide 6: Ways to Prevent Energy Waste (3/4)
Method 2 may be needed to address these cases
Method 2: AP sends Termination Notice before ending a e-BCS service
  Termination Notice should be sent out well before the termination of e-BCS service to ensure that STAs consuming the service have time to act
  Termination Notice likely needs to include the following information:
    E-BCS service identifier
    Time to termination
    Negotiation method: e-BCS request/response frame (for associated STAs), ANQP/GAS (for unassociated STAs), out of band IP (for Rx only STA, the negotiation method is similar to RX only STA’s request for eBCS services)
  Need to ensure that there won’t be a response storm by many of the STAs that are consuming a certain e-BCS service
    GAS already has some mechanisms to avoid signaling storms
    May need to design other mechanisms in a similar fashion

## Slide 7: Ways to Prevent Energy Waste (4/4)
For use cases with traffic which may be of small size, non-changing or slowly changing, but the information is broadcast periodically
  Method 3: Advertisement of a schedule for a broadcast service(s)
Method 3: AP advertises a schedule for broadcast service
  AP schedules broadcast for certain duration of time at periodic intervals.
    For example, every 2 mins for a duration of 30 sec, the AP would provide the broadcast service (i.e., broadcast the stream).
    This schedule information is broadcasted advertised by an eBCS capable AP
      E.g., broadcast Probe Response frame, FILS Discovery frame or a new frame
        Exact frame/container details TBD
        Beacons may include some indicators on where schedule information can be found
    Interested STA(s) would know when to expect the broadcast and for how long.
      STAs can tuned to the channel or wake-up during that time to receive the service
  Such a scheme will address the security and Rx-only scenarios described in option 1.

## Slide 8: Conclusions
We proposed three ideas to address the power efficiency requirement for e-BCS; all can help determine whether there are STAs consuming one or more eBCS service:
For use cases with traffic may be constant and rapidly changing, but due to heavy medium load, it should only be turned on when needed and turned off when no longer needed:
  Method 1: Negotiate broadcast service for a reasonable duration
  Method 2: Termination notice for broadcast services
For use cases with traffic which may be of small size, non-changing or slowly changing, but the information is broadcast periodically
  Method 3: Advertisement of a schedule for a broadcast service(s)

## Slide 9
References
[1] IEEE 11-19/151r5, 802.11bc Functional Requirements Document, September 2019
[2] IEEE 11-19/1001r1, Functional Requirements Document Proposed Update, July 2019

## Slide 10: Straw Poll 1
Do you agree to add to the TGbc SFD in Section 9.6.31 (eBCS Service Request Frame):
  TGbc shall define a mechanism for STAs to negotiate durations of services when negotiating for one or more eBCS services.
  Note: the transmitter of a e-BCS service is expected to have authority on the duration of the eBCS service and can respond with an eBCS Response frame (9.6.32).

## Slide 11: Straw Poll 2
Do you agree to add to the TGbc SFD:
  9.6.34 eBCS Termination Notice Frame
  This frame is transmitted by a transmitter of an eBCS service to announce the termination the eBCS service.

## Slide 12: Straw Poll 3
Do you agree to add to the TGbc SFD in Section 9.6.33 (eBCS Service Advertisement Frame):
  A transmitter of an eBCS service can advertise a schedule (periodicity and duration) of one or more eBCS services.