## Slide 1: Enhanced Multi-Link Single Radio Operation
Date: 2020-4-21
Authors:

## Slide 2: Introduction
11be non-AP MLDs are expected to have different capabilities for multi-link operation and many non-AP MLDs are expected to operate with a single radio
It is important to enable a multi-link operation for a single radio non-AP MLD that can provide throughput enhancement and latency reduction close to a concurrent dual radio non-AP MLD
In this presentation, we propose an enhanced multi-link single radio operation that can achieve this goal

## Slide 3: Problem: Multi-link operation using concurrent dual-radio in a busy network environment
In a busy network environment, concurrent dual-radio doesn’t provide full benefit of STR
Radio 1
Channel 1
Channel 2
Radio 2
AP
(Concurrent dual radio)
STA
(Concurrent dual radio)
Radio 1
Radio 2
Max peak throughput gain of concurrent dual radio can be achieved when two channels are idle
Radio 1
Channel 1
Channel 2
Radio 2
AP
(Concurrent dual radio)
STA
(Concurrent dual radio)
Radio 1
Radio 2
Low latency
Ideal case: Channel 1 and Channel 2 idle
(no overlapping networks)
Reality: Channel 1 and Channel 2 busy
(due to overlapping networks)
data packet
As network gets busier, there is less chance to have two (or multiple) idle channels at the same time
In this case, most of time just one of the two channels will be used for data transfer
This is effectively a single channel operation but switching between the two channels
In a busy network, concurrent dual radio can still provide low latency benefit compared to single radio since AP can transmit a packet on any channel when the medium is idle
busy
busy
Long delay if single radio

## Slide 4: Proposal: Enhanced Multi-link Single Radio (MLSR) Operation
We propose an enhanced mode of operation for a single radio non-AP MLD where
  Single-radio non-AP MLD listens to two (or more) pre-configured channels simultaneously
    2x2 Tx/Rx module may be configured to 1x1 on each channel/band (e.g. 5GHz and 6GHz) to listen to incoming packets on each channel
    1x1 STA on one channel may add an extra 1x1 Rx on the other channel and listen to two channels for incoming packets
  AP MLD transmits a control frame (e.g. RTS or MU-RTS) on any idle channel of the pre-configured channels before a data frame transmission
    The control frame indicates to non-AP MLD which channel will be used for data transmission
  Upon reception of the control frame, non-AP MLD responds with a control frame (e.g. CTS)
  Data transmission follows the response from the non-AP MLD
  Non-AP MLD and AP MLD exchange frames on one link at a time
Radio 1
Channel 1
Channel 2
Radio 2
AP
(Concurrent dual radio)
STA
(single radio)
1x1 Radio 1
Low latency
Channel switch signal (RTS)
D
busy
D
D
D
Radio 1
Channel 1
Channel 2
Radio 2
AP
(Concurrent dual radio)
STA
(Concurrent dual radio)
Radio 1
Radio 2
Low latency
D
busy
D
busy
D
D
Long delay if single radio
Concurrent Dual Radio
Proposal: Enhanced Multi-link Single radio
R
C
A
R
C
1x1 on ch1
1x1 on ch2
1x1 Radio 1
for data reception
2x2
on ch2

## Slide 5: Network Simulation Setup
Configuration
  Target BSS:
    1 AP, 1 STA, 2 bands/channels
    2x2, 80MHz, MCS0/4/7, max TXOP = 5msec
  4 OBSSs:
    1 AP, 2 STAs each
    One STA on each band/channel
    1x1, 80MHz, MCS0
  OBSS traffic load on each band:
    10-90% of 1x1, 80MHz, MCS0 PHY rate (36Mbps) on each band
    This is an example configuration that models channel occupancy due to OBSS (e.g. 10% load generates 3.6 Mbps traffic load and occupies approximately 10% of airtime)
  RTS/CTS enabled
Comparisons:
  SLSR: Single-link, single-radio
  MLMR: Multi-link, multi-radio (concurrent)
  MLSR: Enhanced multi-link, single-radio (use RTS for channel switch signal)
Throughput evaluation:
  Backlogged traffic on the target BSS (DL), simulation time: 10 sec, 6 times
End-to-end latency evaluation:
  512 byte packet every 20 msec, simulation time: 20 sec, 1 time

## Slide 6: Throughput results – 80MHz, 2x2, MCS4
Enhanced multi-link single-radio achieves 60-70% throughput enhancement in a busy network (OBSS load : 40-70%)
Enhanced multi-link single-radio reaches 70-80% of the multi-link multi-radio throughput in a busy network (OBSS load >30%)

## Slide 7: Throughput results for lower MCS – 80MHz, 2x2, MCS0
Results follow similar trend as the MCS4 case
Enhanced multi-link single-radio achieves 60-70% throughput enhancement in a busy network (OBSS load : 40-70%)
Enhanced multi-link single-radio reaches 70-80% of the multi-link multi-radio throughput in a busy network (OBSS load >30%)

## Slide 8: Throughput results for higher MCS – 80MHz, 2x2, MCS7
Results follow similar trend as the MCS0 and MCS4 cases
Enhanced multi-link single-radio achieves 60-70% throughput enhancement in a busy network (OBSS load : 40-70%)
Enhanced multi-link single-radio reaches 70-80% of the multi-link multi-radio throughput in a busy network (OBSS load >30%)

## Slide 9: Latency results
In a very busy network, the proposed enhanced multi-link single radio approach reduces the end-to-end latency by half compared to single-link single radio – worst case latency improvement
The latency performance of the proposed method is similar to the multi-link multi-radio case
OBSS load | 80% | 90%
SLSR | 73ms | 84ms
MLMR | 32ms | 38ms
MLSR | 32ms | 39ms
90%tile e2e latency measurement
~half

## Slide 10: Enabling the proposed MLSR operation with minimal changes in 802.11be
Non-AP MLD’s behavior
  Indicates that it is “Single-Radio” non-AP MLD to its intended transmitter or receiver (i.e. AP MLD)
    Single-Radio non-AP MLD is unable to transmit or receive frames on more than one link simultaneously
  Enable two or more links
    Initial power states: one link is in the awake state and the rest are in the doze state
  Enable the dynamic SM power save for the two or more enabled link
    HE dynamic SM power save may need to be extended to EHT dynamic SM power save with additional constraints (e.g. supported MCS, bandwidth, frame types (e.g. RTS, MU-RTS, Trigger, etc.))
  To enable the MLSR operation, the non-AP MLD indicates two or more enabled links are in the awake state
AP MLD’s behavior
  When a non-AP MLD indicates the above information to the AP MLD, the AP MLD starts a frame exchange sequence by following the dynamic SM power save procedure on any one enabled link that is in the awake state

## Slide 11: Conclusion
When a single-radio non-AP MLD is operating in a busy network environment, having an additional capability to listen to two (or more) pre-configured channels simultaneously and an AP MLD able to deliver the non-AP MLD’s queued data on the next pre-configured channel to become idle can provide most of benefits that can be provided by the multi-link operation of a concurrent dual-radio non-AP MLD

## Slide 12: Straw Poll
Do you support the concept of the multi-link operation for a single-radio non-AP MLD proposed in this presentation?