## Slide 1: Consideration of interworking between 3GPP 5G core and IEEE 802.11
Date: 2020-04-06
Authors:

## Slide 2: Abstract
The presentation introduces potential standardization demand in IEEE 802.11 regarding interworking with 5G QoS model and 5G QoS signalling and proposes to consider trusted WLAN interworking scenario in addition to the commonly assumed untrusted scenario.

## Slide 3: Motivation
Rationales for AANI SC 5G WLAN Interworking report
  IEEE 802.11 is widely used for early introduction of 5G-like services demanding high throughput and high capacity
  5G provides not only higher capacity and throughput but also new kind of services (URLLC, eMTC) that haven’t considered yet for interworking with IEEE 802.11
  P802.11be considers enhancements to QoS that would allow for 5G services beyond prioritized best effort communication, e.g. low latency communications. Design decisions in P802.11be could benefit from insights into interworking issues with 5G core.
The slides provide thoughts in addition to the content already covered in “Draft technical report on interworking between 3GPP 5G network & WLAN”
  May trigger discussions leading to further revisions of the draft report

## Slide 4: 5G Qos Model
5G QoS characteristics is defined through:
1 Resource Type (GBR, Delay critical GBR or Non-GBR);
2 Priority Level;
3 Packet Delay Budget;
4 Packet Error Rate;
5 Averaging window (for GBR and Delay-critical GBR resource type only);
6 Maximum Data Burst Volume (for Delay-critical GBR resource type only).
3GPP TS 23.501 Figure 5.7.1.5-1: The principle for classification and User Plane marking for QoS Flows and mapping to AN Resources

## Slide 5: 5G QoS Signaling
QoS signaling (establishment, maintenance, and teardown of service flows) is part of NAS (Non-Access-Stratum) protocol
In 5G NAS procedures are used for:
  5GS mobility management (5GMM) protocol for the control of mobility within NG radio access network (NG-RAN) and/or non-3GPP access network.
    Also provides control of security for the NAS protocols.
  5GS session management (5GSM) protocol for the handling of 5GS PDU sessions.
    Control of user-plane resources together with the bearer control provided by the access stratum
A 5GS session management (5GSM) message is piggybacked in specific 5GS mobility management (5GMM) transport messages.
The UE can only initiate the 5GSM procedure when there is a 5GMM context established at the UE.

## Slide 6: Potential IEEE 802.11 standardization topics for 5G QoS support
Current IEEE 802.11 does not provide full support of 5G QoS model
  How to realize and handle QoS flows over IEEE 802.11?
  Which 5G QoS classes could be supported by IEEE 802.11ax? Which by P802.11be?
There is no equivalent to the 5GSM in IEEE 802.11
  Currently realized OTT through 5G-EAP/IKEv2/IPsec
  How to interface into the IEEE 802.11 ‘access stratum’?

## Slide 7: 3GPP 5G Untrusted WLAN Interworking Scenario
Untrusted scenario is most commonly assumed for WLAN interworking with N1 carrying NAS protocol, and NWu representing 5G EAP/IKEv2/IPsec
3GPP TS 23.501 Figure 4.2.8.2.1-1: Non-roaming architecture for 5G Core Network with untrusted non-3GPP access

## Slide 8: 3GPP 5G Trusted WLAN Interworking Scenario
Trusted model could be deployed by mobile operators owning their WLAN access, but also for private 5G deployments e.g industrial use cases.
3GPP TS 23.501 Figure 4.2.8.2.1-2: Non-roaming architecture for 5G Core Network with trusted non-3GPP access

## Slide 9: Conclusion
It makes sense to create a report on interworking between 3GPP 5G core and IEEE 802.11 to facilitate better integration of Wi-Fi with 5G.
Identified missing functionalities could be addressed in P802.11be or also in new IEEE 802.11 standardization projects.
Further investigations and documentation required on adaptation of IEEE 802.11 to 3GPP 5G QoS model and QoS signalling.
Trusted interworking model should be considered in addition to untrusted model, in particular when enabling industrial use cases.