## Slide 1: Consideration on EHT-STF
Date: 2020-04-16
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
11ax supports 1x and 2x HE-STF
  1x HE-STF is used for HE PPDUs that are not HE TB PPDU
  2x HE-STF is used for HE TB PPDU
Meanwhile, in 11be, various PPDU types are being considered including EHT TB PPDU [1][2], and thus, 1x and 2x STF modes may be necessary
In this contribution, we propose to support 1x and 2x EHT-STF in 11be and reuse 1x and 2x HE-STF sequences in 20/40/80/160/80+80 MHz
  PAPRs are investigated for 1x and 2x HE-STF sequences in 20/40/80/160/80+80 MHz for verification
In addition, we briefly deal with how to design 1x and 2x EHT-STF sequences in 240/160+80/320/160+160 MHz

## Slide 3: 1x and 2x EHT-STF
In [3], for 11ax, HE-STF was discussed in detail in terms of AGC
  HE-STF needs 5 periods at least for AGC processing
  HE-STF with 5 periods can also allow leveraging the 11ac AGC design
  HE-STF of 0.8us periodicity with 5 periods (1x HE-STF) provides low overhead and enough performance for HE PPDUs that are not HE TB PPDU
  HE-STF of 1.6us periodicity with 5 periods (2x HE-STF) provides additional performance improvement and reliability for HE TB PPDU
Based on the conclusion of [1], we propose to support 1x EHT-STF for EHT SU/MU PPDU and 2x EHT-STF for EHT TB PPDU
  EHT-STF is positioned immediately after EHT-SIG in EHT PPDU
    If EHT PPDU doesn’t have EHT-SIG, EHT-STF is positioned immediately after U-SIG
  For 20/40/80/160/80+80 MHz, 1x HE-STF and 2x HE-STF can be reused but we need to further check on the validity in terms of PAPR
  For 240/160+80/320/160+160 MHz, 1x and 2x EHT-STF sequences need to be designed

## Slide 4: EHT-STF Sequence for BW ≤ 160MHz
In [4], for 11ax, M sequence with length 15 was used for building up 1x and 2x HE-STF sequences for 20/40/80 MHz
  1x HE-STF design
In [5], for 11ax, HE-STF sequence for 160/80+80 MHz was designed by repeating 80MHz HE-STF sequence and applying additional phase rotation to the lower 40MHz portion in higher 80MHz
For 11be, we can reuse HE-STF sequences for 20/40/80/160/80+80 MHz, but we need to verify whether they have reasonable PAPRs because of the newly adopted features such as preamble puncturing and multiple RU aggregation

## Slide 5: 1x EHT-STF Sequence for BW ≤ 160MHz (1/2)
For 1x EHT-STF design, we need to consider non-preamble punctured and preamble punctured cases as well
  Only 80/160 MHz HE-STF sequence needs to be looked into since there is no preamble punctured case defined in 20/40 MHz
    20/40 MHz 1x HE-STF sequence can be definitely reused
  The following preamble punctured cases are considered for PAPR investigation
    80MHz: [oooo], [xooo], [oxoo], [ooxo], [ooox]
    160MHz: [oooo oooo], [xooo oooo], [oxoo oooo], [ooxo oooo], [ooox oooo],
    [oooo xooo], [oooo oxoo], [oooo ooxo], [oooo ooox],
    [xxoo oooo], [ooxx oooo], [oooo xxoo], [oooo ooxx]
1x HE-STF sequences are given as follows
  20MHz: HES-112,112(-112:16:112) = M *(1+j)*sqrt(1/2), HES-112,112(0) = 0
  40MHz: HES-240,240(-240:16:240) = {M, 0, -M} *(1+j)*sqrt(1/2)
  80MHz: HES-496,496(-496:16:496) = {M, 1, -M, 0, -M, 1, -M} *(1+j)*sqrt(1/2)
  160 MHz: HES-1008,1008(-1008:16:1008) = {M, 1, -M, 0, -M, 1, -M, 0, -M, -1, M, 0, -M, 1, -M} *(1+j)*sqrt(1/2)
  M = {-1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1}
O: non-punctured 20MHz
X: punctured 20MHz

## Slide 6: 1x EHT-STF Sequence for BW ≤ 160MHz (2/2)
PAPR [dB]
  80MHz: 4.5287, 6.3527, 5.7658, 7.1182, 4.8194
  160MHz: 5.9283, 7.3646, 5.8974, 8.1153, 6.8627, 7.3646, 7.1456, 8.1153, 6.1031, 6.0309, 6.7871, 6.0654, 6.7871
  CDF comparison with the data part
    PAPRs for non-punctured and punctured cases are merged in both HE-STF and data part
Even in 80/160/80+80 MHz, it seems feasible to reuse 1x HE-STF sequence
<80MHz>
<160MHz>

## Slide 7: 2x EHT-STF Sequence for BW ≤ 160MHz (1/3)
For 2x EHT-STF design, we need to consider various multiple RU combinations as well as the existing RUs on top of non-preamble punctured and preamble punctured cases
  All 2x HE-STF sequences need to be validated
2x HE-STF sequences are given as follows
  20MHz: HES-120,120(-120:8:120) = {M, 0 , -M} *(1+j)*sqrt(1/2)
  40MHz: HES-248,248(-248:8:248) = {M, -1, -M, 0, M, -1, M} *(1+j)*sqrt(1/2), HES-248,248(±248) = 0
  80MHz: HES-504,504 (-504:8:504) = {M, -1, M, -1, -M, -1, M, 0, -M, 1, M, 1, -M, 1, -M} *(1+j)*sqrt(1/2), HES-504,504(±504) = 0
  160/80+80MHz: HES-1016,1016 (-1016:8:1016) = {M, -1, M, -1, -M, -1, M, 0, -M, 1, M, 1, -M, 1, -M, 0, -M, 1, -M, 1, M, 1, -M, 0, -M, 1, M, 1, -M, 1, -M} *(1+j)*sqrt(1/2), HES-1016,1016(±8) = 0, HES-1016,1016(±1016) = 0

## Slide 8: 2x EHT-STF Sequence for BW ≤ 160MHz (2/3)
CDF comparison with the data part in 20/40 MHz
  PAPRs for all RUs and multiple RU combinations are merged in both HE-STF and data part
  Note that there is no preamble punctured case defined in 20/40MHz
In 20/40 MHz, it seems feasible to reuse 2x HE-STF sequence
<20MHz>
<40MHz>

## Slide 9: 2x EHT-STF Sequence for BW ≤ 160MHz (3/3)
CDF comparison with the data part in 80/160 MHz
  PAPRs for all RUs and multiple RU combinations as well as non-punctured and punctured cases are incorporated in both HE-STF and data part
Even in 80/160/80+80 MHz, it seems feasible to reuse 2x HE-STF sequence
<80MHz>
<160MHz>

## Slide 10: EHT-STF Sequence for BW > 160MHz (1/2)
In 11ax, the following approach was utilized to build up 160MHz HE-STF sequences
  1x 160MHz HE-STF
For simplicity, this kind of approach can be employed for 240/320MHz EHT-STF sequence design, e.g., 80MHz HE-STF sequence (80HES) is repeated and each 80MHz segment can be multiplied by an additional coefficient
  240MHz: [80HES, a*80HES, b*80HES]
  320MHz: [80HES, a*80HES, b*80HES, c*80HES]
  Candidates of a, b, c: 1, -1
  For further PAPR improvement, 40/20 MHz can be regarded as the minimum segment unit which is multiplied by additional coefficients

## Slide 11: EHT-STF Sequence for BW > 160MHz (2/2)
It is also possible to reuse 160MHz HE-STF sequence (160HES) for the 320MHz design and an additional coefficient can be applied only to the higher 160MHz segment
  320MHz: [160HES, a*160HES]
  Candidates of a: 1, -1
  For further PAPR improvement, 80/40/20 MHz can be regarded as the minimum segment unit which is multiplied by additional coefficients
Additional coefficients can be optimized in terms of the PAPR
  For 1x EHT-STF, we need to consider non-preamble punctured and agreed preamble punctured cases as well
  For 2x EHT-STF, we need to consider all RUs and multiple RU combinations on top of non-preamble punctured and preamble punctured cases

## Slide 12: Conclusion
We have proposed to support 1x and 2x EHT-STF in 11be
  EHT-STF is positioned immediately after U-SIG/EHT-SIG in EHT PPDU
  1x EHT-STF is used for EHT SU/MU PPDU
  2x EHT-STF is used for EHT TB PPDU
For 20/40/80/160/80+80 MHz, we have verified that reusing 1x and 2x HE-STF sequences is possible
  Although preamble puncturing and multiple RU aggregation cause a further increase in PAPR, HE-STF sequences have a lower PAPR than the data part
For 240/320MHz, we have briefly introduced the EHT-STF sequence design based on the HE-STF sequences
  11ax 80/160 MHz HE-STF sequence is repeated and each segment is multiplied by an additional coefficient to reduce PAPR
  To optimize the additional coefficients, preamble puncturing and multiple RU aggregation need to be considered

## Slide 13: Straw Poll #1
Do you agree to add the following text to the TGbe SFD?
  EHT PPDU has EHT-STF immediately after EHT-SIG
    If EHT PPDU doesn’t have EHT-SIG, EHT-STF is positioned immediately after U-SIG
Y/N/A: //

## Slide 14: Straw Poll #2
Do you agree to add the following text to the TGbe SFD?
  802.11be supports 1x EHT-STF and 2x EHT-STF
    1x EHT-STF is used in EHT SU/MU PPDU
      Whether SU and MU PPDU format is the same is TBD
    2x EHT-STF is used in EHT TB PPDU
    TBD for any new EHT PPDU formats
Y/N/A: //

## Slide 15: Straw Poll #3
Do you agree to add the following text to the TGbe SFD?
  802.11be reuses 1x HE-STF and 2x HE-STF in 20/40/80/160/80+80 MHz PPDU
Y/N/A: //

## Slide 16: References
[1] 802-11-20/0019r1 11be PPDU Format
[2] 802.11-20/0049r2 PPDU Types and U-SIG Content
[3] 802.11-15/0381r1 HE-STF Proposal
[4] 802.11-15/1323r1 HE-STF Sequences
[5] 802.11-16/0335r0 HE-STF Sequences for 160/80+80 MHz