## Slide 1: STR AP Sync. PPDU Transmission
Date: 2020-03-20
Authors:
Name | Affiliations | Address | Phone | Email
Zhou Lan | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | zhou.lan@broadcom.com
Albert Bredewoud |  |  |  | 
George Kondylis |  |  |  | 
Matthew Fischer |  |  |  | 
Notes: September 2012

## Slide 2: Summary
Aync. transmissions are supported by a STA that is STR capable
  When a STR AP transmits to a non-STR STA, the ending time of the PPDUs are aligned to help non-STR STA operation
This contribution proposes to allow STR AP sync. PPDU transmission for high throughput scenario

## Slide 3: Recap-STR AP Async. Transmission
  Independent EDCA on multiple links
  Async. PPDU TX starts on the link that completes back off
  Sync. PPDU ending time alignment[1][2] to help the non STR STA avoiding concurrent TX/RX operation
  Triggered BA/MBA or relaxing SIFS requirement to align the starting time of the next Sync. PPDU

## Slide 4: Issue of STR Async. Transmission
  RTS/CTS exchanges is critical for high throughput traffic protection
  [3] has described 3 scenarios where RTS/CTS exchanges are compromised due to non-STR capabilities of the STA
  [3] has also discussed a sub optimal solution of CTS-to-self frame transmission
  This contribution describe another problematic RTS/CTS scenario that may impact the throughput dramatically
  Assuming the congestion are on the same level, back off on multiple links may not complete at the same time, but close enough so that there is overlapping between RTS/CTS exchanges across multiple links
  The CTS TX on one link may damage the RTS RX on another link and vice verse. In such case, the following data transmissions are blocked

## Slide 5: Issue of STR Async. Transmission (cont.)
  Async. PPDU transmission doesn’t provide optimized high throughput performance
    Single link provides up to 11.4Gbps capacity @320 MHz, 4SS, 4K QAM. Up to 8 M bytes can be transmitted with in one TXOP (i.e. 5.4 ms)
    8 M bytes cover 1024 MPDUs (assuming 1500 bytes MSDU, 4 MSDU per MPDU)
    Now here is the problem as shown in the following diagram
      AP1 completes back off on the first link and decides to transmit, how to decide aggregation size X on link 1?
        Option 1: Aggregate up to 1024 MPDU since the TXOP is sufficient
          Then AP2 completes back off on link 2, it can only pick up QoS Data from different TID
        Option 2: Aggregate up to X MPDUs
          AP2 may not even be able to complete back off, technically no way to decide X
          Even if AP2 completes back off and can do aggregation from X to Y, but it is already too late for AP1 to re-aggregate (L-SIG already on the air) so that the end time alignment can not be achieved
  Async. PPDU transmission may provide the most channel access opportunities but not sufficient for the high through usage case

## Slide 6: Allow STR AP Sync. PPDU Transmission
  Option 1:
  Independent EDCA on each link. Sync. PPDU TX starts once back off on either link completes and PIFS check passes on the other link
  Regulation support 160/80+80 type of operation. 11be should supports this mode anyway (maybe with some constrains?)
  Option 2: adopting the proposal in [3] for STR AP:
  Independent EDCA on each link. RTS TX starts on the link that completes back off. CTSs TX start on multiple links if NAV and CCA check passes to enable the following sync. PPDU TX on multiple links
  A low complexity feature that provides good protection for MLO. There is regulation uncertainty and unfairness issue. But the NAV check and CCA check on the second link mitigates the unfairness issue.
  Option 3:
  Independent EDCA on each link. Sync. PPDU TX starts once back off on either link completes and PIFS check passes on other links. The remaining back off counter is stored
  The next EDCA attempt adds the truncated back off of the first transmission to the new back off counter to account for the unfairness issue
  A low complexity feature as well that addresses both regulation and unfairness issues

## Slide 7: Conclusion
  Async. operation should cover some of STR AP to Non-STR STA DL data transmission scenarios
  For high throughput transmission where RTS/CTS protection is critical, we propose to allow a mode that enables STR AP to transmit data to non-STR STA and solicits acknowledgement using sync. PPDUs

## Slide 8: Straw poll 1
  Do you agree 802.11be define a mode of operation that allows STR AP transmits Sync. PPDUs to non-STR STA and solicits acknowledgement
    YES
    NO
    ABS

## Slide 9: Reference
[1] IEEE802.11-20/26r3, “MLO: Sync PPDUs”
[2] IEEE802.11-20/106r4, “Follow up on performance aspects of mlink ops with constrains”
[3] IEEE802.11-20/291r1, “MLO Async. and Sync. Operation Discussion”

## Slide 10: Annex-Issue of STR AP Async. Transmission
  RTS/CTS case 1
    Allow NO RTS/CTS exchange on the second link that finish back off late

## Slide 11: Annex-Issue of STR AP Async. Transmission
  RTS/CTS case 2
  Do RTS/CTS on the second link
  Issue: if the backoff on the second link finish during the RTS/CTS exchange of link 1, the RTS/CTS exchange on both link fail

## Slide 12: Annex-Issue of STR AP Async. Transmission
  RTS/CTS case 3
  NO RTS/CTS on the second link, instead a CTS-A is sent out when back off finished on the second link
  Issue: not as good protection as RTS/CTS exchange on the second link