## Slide 1: Signaling of RU allocation in 11be
Date: 2020-04-24
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
April 2020

## Slide 2: Introduction
We introduced the three options for signaling of RU allocation in our previous contribution[1].
  Option 1 : enhance RU allocation subfield
  Option 2 : leverage the STA-ID
  Option 3 : leverage the reserved bits of RU allocation subfield
Regarding opt.1, various signaling methods for RU allocation have been discussed in several contributions [2~4].
This contribution further discusses RU allocation signals related opt.1 in consideration of MU-MIMO.

## Slide 3: Consideration for MU-MIMO
In the 11ax, MU-MIMO is supported on the RUs larger than or equal to 106 tone as following.
  “Both DL and UL MU-MIMO transmissions are supported on portions of the PPDU bandwidth (on resource units greater than or equal to 106 tones).”
So, regardless of MRU aggregation, we can consider MU-MIMO is supported if the size of the allocated RU is equal or larger than 106 tones.
  The 26+106 RU among the small MRUs can be used for MU-MIMO transmission.
Also, based on the following motion in 11be SFD, we can consider the maximum number of users supported for DL MU-MIMO transmissions to 16 users per resource unit (RU)
  802.11be supports a maximum of 16 spatial streams (total across all the scheduled STAs) for MU-MIMO.

## Slide 4: Signaling of RU allocation
Basically, we can reuse the RU allocation subfield defined in 11ax, when single RU are allocated to each STA in OFDMA transmission.
  But, to accommodate the increased number of user for MU-MIMO, it needs to be extended by using the additional bits.
In order to support the large bandwidth, MRU aggregation, and more users for MU-MIMO, we can consider the extended RU allocation subfield which consists of 8bits and additional 2bits.
  In the additional 2bits, as described in[1], the 1 bit is used to indicate whether the RU allocation is for M-RU aggregation or not and another 1bit is used to support the increased number of users in MU-MIMO.

## Slide 5: Signaling of RU allocation
The RU allocation subfield can be composed by including extended 2bit such as following.
  RU allocation subfield = [X1 8bits X2] ( total 10bits)
  The MSB 1bit of RU allocation field is used to indicate whether RU allocation includes the allocation for MRU or not.
    If X1 is set to 0, it means that the RU allocation only includes the assessment of single RU for STA.
      And, 8bit defined in 11ax and extended 1bit (i.e., X2) are used for extending the number of MU-MIMO users.
      For example, [52 52 106]
      Where, 8bit information is equal to 11ax and by using y2y1y0w1, it can support to 16 number of entities.
    It is a simple way since we can reuse the conventional RU allocation of 11ax.
MSB (1bit) | 8bit information | LSB(1bit) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B9 | (B8 B7 B6 B5 B4 B3 B2 B1) | B0 |  |  |  |  |  |  |  |  |  | 
0 | 00010y2y1y0 | w1 | 52 |  | 52 |  | - | 106 |  |  |  | 16

## Slide 6: Signaling of RU allocation
  While if X1 is set to 1, it means that the RU allocation is for the MRU allocation.
    9-bit excluding MSB 1bit in the RU allocation subfield is used to indicate the MRU assignments.
    For example, [ 26 26+52 26 26 26 26 26] and [26 26 26 26 26+106 ]
    We can support the possible cases for MRU by using the 9bit information.
MSB (1bit) | 9bit information | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B9 | (B8 B7 B6 B5 B4 B3 B2 B1 B0) |  |  |  |  |  |  |  |  |  | 
1 | 000000000 | 26 | 26+52 |  |  | 26 | 26 | 26 | 26 | 26 | 1
··· | ··· | ··· |  |  |  |  |  |  |  |  | ···
1 | 00011x3x2x1x0 | 26 | 26 | 26 | 26 | 26+106 |  |  |  |  | 16
··· | ··· | ··· |  |  |  |  |  |  |  |  | ···

## Slide 7: Example : RU allocation subfield for single RU allocation
MSB (1bit) | 8bit information | LSB(1bit) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries | MSB (1bit) | 8bit information | LSB(1bit) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B9 | (B8 B7 B6 B5 B4 B3 B2 B1) | B0 |  |  |  |  |  |  |  |  |  |  | B9 | (B8 B7 B6 B5 B4 B3 B2 B1) | B0 |  |  |  |  |  |  |  |  |  | 
0 | 00000000 | 0 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1 | 0 | 00100y2y1y0 | w1 | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 16
0 | 00000000 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 00101y2y1y0 | w1 | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 16
0 | 00000001 | 0 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1 | 0 | 00110y2y1y0 | w1 | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 16
0 | 00000001 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 00111y2y1y0 | w1 | 52 |  | 52 |  | 26 | 106 |  |  |  | 16
0 | 00000010 | 0 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1 | 0 | 01000y2y1y0 | w1 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 16
0 | 00000010 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01001y2y1y0 | w1 | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 16
0 | 00000011 | 0 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1 | 0 | 01010y2y1y0 | w1 | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 16
0 | 00000011 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01011y2y1y0 | w1 | 106 |  |  |  | 26 | 52 |  | 52 |  | 16
0 | 00000100 | 0 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1 | 0 | 0110y1y0z1z0 | 0 | 106 |  |  |  | - | 106 |  |  |  | 16
0 | 00000100 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 0110y1y0z1z0 | 1 | Reserved |  |  |  |  |  |  |  |  | 16
0 | 00000101 | 0 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1 | 0 | 01110000 | 0 | 52 |  | 52 |  | - | 52 |  | 52 |  | 1
0 | 00000101 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01110000 | 1 | Reserved |  |  |  |  |  |  |  |  | 1
0 | 00000110 | 0 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1 | 0 | 01110001 | 0 | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
0 | 00000110 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01110001 | 1 | Reserved |  |  |  |  |  |  |  |  | 1
0 | 00000111 | 0 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1 | 0 | 01110010 | 0 | 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00000111 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01110010 | 1 | Reserved |  |  |  |  |  |  |  |  | 1
0 | 00001000 | 0 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1 | 0 | 01110011 | 0 | 996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00001000 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01110011 | 1 | Reserved |  |  |  |  |  |  |  |  | 1
0 | 00001001 | 0 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1 | 0 | 01110100 | 0 | 2x996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00001001 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01110100 | 1 | Reserved |  |  |  |  |  |  |  |  | 1
0 | 00001010 | 0 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1 | 0 | 01110101 | 0 | 3x996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00001010 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01110101 | 1 | Reserved |  |  |  |  |  |  |  |  | 1
0 | 00001011 | 0 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1 | 0 | 0111011x0 | w1 | Reserved |  |  |  |  |  |  |  |  | 4
0 | 00001011 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 01111y2y1y0 | w1 | Reserved |  |  |  |  |  |  |  |  | 16
0 | 00001100 | 0 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1 | 0 | 10y2y1y0z2z1z0 | 0 | 106 |  |  |  | 26 | 106 |  |  |  | 64
0 | 00001100 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 11000y2y1y0 | w1 | 242 |  |  |  |  |  |  |  |  | 16
0 | 00001101 | 0 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1 | 0 | 11001y2y1y0 | w1 | 484 |  |  |  |  |  |  |  |  | 16
0 | 00001101 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 11010y2y1y0 | w1 | 996 |  |  |  |  |  |  |  |  | 16
0 | 00001110 | 0 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1 | 0 | 11011y2y1y0 | w1 | 2x996 |  |  |  |  |  |  |  |  | 16
0 | 00001110 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 11100y2y1y0 | w1 | 3x996 |  |  |  |  |  |  |  |  | 16
0 | 00001111 | 0 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1 | 0 | 11101y2y1y0 | w1 | Reserved |  |  |  |  |  |  |  |  | 16
0 | 00001111 | 1 | Reserved |  |  |  |  |  |  |  |  | 1 | 0 | 11110y2y1y0 | w1 | Reserved |  |  |  |  |  |  |  |  | 16
0 | 00010y2y1y0 | w1 | 52 |  | 52 |  | - | 106 |  |  |  | 16 | 0 | 11111y2y1y0 | w1 | Reserved |  |  |  |  |  |  |  |  | 16
0 | 00011y2y1y0 | w1 | 106 |  |  |  | - | 52 |  | 52 |  | 16 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8: Example : RU allocation subfield for MRU allocation
RU Allocation subfield |  |  |  |  |  |  |  |  |  |  | 
MSB (1bit) | 9bit information | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B9 | (B8 B7 B6 B5 B4 B3 B2 B1 B0) |  |  |  |  |  |  |  |  |  | 
1 | 000000000 | 26 | 26+52 |  |  | 26 | 26 | 26 | 26 | 26 | 1
1 | 000000001 | 26 | 26+52 |  |  | 26 | 26 | 26 | 52 |  | 1
1 | 000000010 | 26 | 26+52 |  |  | 26 | 52 |  | 26 | 26 | 1
1 | 000000011 | 26 | 26+52 |  |  | 26 | 52 |  | 52 |  | 1
1 | 000000100 | 26 | 26 | 26 | 26 | 26 | 52+26 |  |  | 26 | 1
1 | 000000101 | 26 | 26 | 52 |  | 26 | 52+26 |  |  | 26 | 1
1 | 000000110 | 52 |  | 26 | 26 | 26 | 52+26 |  |  | 26 | 1
1 | 000000111 | 52 |  | 52 |  | 26 | 52+26 |  |  | 26 | 1
1 | 000001000 | 26 | 26+52 |  |  | 26 | 52+26 |  |  | 26 | 1
1 | 000001001~1111 | reserved |  |  |  |  |  |  |  |  | 7
1 | 00001x3x2x1x0 | 26 | 26+52 |  |  | 26 | 106 |  |  |  | 16
1 | 00010x3x2x1x0 | 106 |  |  |  | 26 | 52+26 |  |  | 26 | 16
1 | 00011x3x2x1x0 | 26 | 26 | 26 | 26 | 26+106 |  |  |  |  | 16
1 | 00100x3x2x1x0 | 26 | 26 | 52 |  | 26+106 |  |  |  |  | 16
1 | 00101x3x2x1x0 | 52 |  | 26 | 26 | 26+106 |  |  |  |  | 16
1 | 00110x3x2x1x0 | 52 |  | 52 |  | 26+106 |  |  |  |  | 16
1 | 00111x3x2x1x0 | 106+26 |  |  |  |  | 26 | 26 | 26 | 26 | 16
1 | 01000x3x2x1x0 | 106+26 |  |  |  |  | 26 | 26 | 52 |  | 16
1 | 01001x3x2x1x0 | 106+26 |  |  |  |  | 52 |  | 26 | 26 | 16
1 | 01010x3x2x1x0 | 106+26 |  |  |  |  | 52 |  | 52 |  | 16
1 | 01011x3x2x1x0 | 106+26 |  |  |  |  | 52+26 |  |  | 26 | 16
1 | 01100x3x2x1x0 | 26 | 26+52 |  |  | 26+106 |  |  |  |  | 16
1 | 01101x3x2x1x0 | reserved |  |  |  |  |  |  |  |  | 16
1 | 01110x3x2x1x0 | reserved |  |  |  |  |  |  |  |  | 16
1 | 01111x3x2x1x0 | reserved |  |  |  |  |  |  |  |  | 16
1 | 100y5y4y3y2y1y0 | 106 |  |  |  | 26+106 |  |  |  |  | 64
1 | 101y5y4y3y2y1y0 | 106+26 |  |  |  |  | 106 |  |  |  | 64
1 | 11000x3x2x1x0 | 242(1)+484(2), second 242 is not allocated in 80MHz |  |  |  |  |  |  |  |  | 16
1 | 11001x3x2x1x0 | 242(2)+484(2) , first 242 is not allocated in 80MHz |  |  |  |  |  |  |  |  | 16
1 | 11010x3x2x1x0 | 484(1)+242(4), third 242 is not allocated in 80MHz |  |  |  |  |  |  |  |  | 16
1 | 11011x3x2x1x0 | 484(1)+242(3), forth 242 is not allocated in 80MHz |  |  |  |  |  |  |  |  | 16
1 | 11100x3x2x1x0 | 484(1)+996(2), second 484 is not allocated in 160MHz |  |  |  |  |  |  |  |  | 16
1 | 11101x3x2x1x0 | 484(2)+996(2) , first 484 is not allocated in 160MHz |  |  |  |  |  |  |  |  | 16
1 | 11110x3x2x1x0 | 996(1)+484(4), third 484 is not allocated in 160MHz |  |  |  |  |  |  |  |  | 16
1 | 11111x3x2x1x0 | 996(1)+484(3), forth 484 is not allocated in 160MHz |  |  |  |  |  |  |  |  | 16

## Slide 9: Summary
To accommodate the MRU allocation and increased number of users in MU-MIMO, we proposed the extended RU allocation information.
  The extended RU allocation information consists of 10bits.
  The MSB 1bit of RU allocation is used to indicate whether MRU allocation is included or not.
  The LSB 1bit of RU allocation is used for extending the number of MU-MIMO users.
  We can reuse the RU allocation information when single RU is allocated to STA.

## Slide 10: Straw Poll #1
Do you agree that the RU allocation subfield in the EHT-SIG field of an EHT-PPDU sent to multiple users includes the RU allocation for Multiple RUs as well as Single RU?
  Y/N/A

## Slide 11: Straw Poll #2
Do you agree that MU-MIMO is supported on the RUs equal to or larger than 106 tones including MRU aggregation cases?
  Y/N/A

## Slide 12: Straw Poll #3
Do you agree that the RU allocation subfield of EHT-SIG field consists of 10bits ?
  Detail for construction of RU allocation is TBD.
  Y/N/A

## Slide 13: Straw Poll #4
Do you agree that the maximum number of users supported for DL MU-MIMO is 16 per resource unit(RU)?
  The number of MU-MIMO users for RU < 242 tones is TBD.
  Y/N/A

## Slide 14: Straw Poll #5
Do you agree that the MSB 1bit in the RU allocation subfield of the EHT-SIG field is used to indicate whether RU allocation information is for single RU or MRU?
  Y/N/A

## Slide 15: Straw Poll #6
Do you agree that the LSB 1bit in the RU allocation subfield of the EHT-SIG field is used for extending the number of MU-MIMO users up to 16 in single RU allocation?

## Slide 16: Reference
[1] 11-20-0403r0-signaling-of-multiple-ru-aggregation-in-ofdma (Dongguk Lim, LGE)
[2] 11-20-0578r0-on-ru-allocation-singling-in-eht-sig(Jianhan Liu, Mediatek)
[3] 11-20-0373r1-ru-allocation-subfield-design-for-multi-ru-support(Myeongjin Kim, Samsung)
[4]11-20-0400r0-multi-ru-combination-and-signaling-for-ofdma-transmission(Mengshi Hu, Huawei)

## Slide 17: Appendix

## Slide 18: Combination of small-size RUs (1/2)
Based on the passed motions in [1], we can consider the following allocation for combinations of small-size RUs.
  We assume the followings
    Bandwidth : 20MHz
    Number of allocated combination in BW : up to 2
    An Allocation subfield is configure per 20MHz.
    Multiple User transmission (i.e., OFDMA), but, MU-MIMO is not considered.
  Allocation for RU26+RU52,
Index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26
2 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 | 
3 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26
4 | 26 | 26 | 52 |  | 26 | 52 |  | 52 | 
5 | 26 | 26 | 52 |  | 26 | 106 |  |  | 
6 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26
7 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26
8 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26
9 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26
10 | 106 |  |  |  | 26 | 52 |  | 26 | 26
11 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26

## Slide 19: Combination of small-size RUs (1/2)
  Allocation for RU26+RU106
  We can also consider the allocation of two combinations configured with different small-size RUs.
    For example, RU26+RU52 and RU26+RU106 can be considered.
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 26 | 26 | 26 | 26 | 26 | 106 |  |  | 
2 | 26 | 26 | 52 |  | 26 | 106 |  |  | 
3 | 52 |  | 26 | 26 | 26 | 106 |  |  | 
4 | 52 |  | 52 |  | 26 | 106 |  |  | 
5 | 106 |  |  |  | 26 | 106 |  |  | 
6 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26
7 | 106 |  |  |  | 26 | 26 | 26 | 52 | 
8 | 106 |  |  |  | 26 | 52 |  | 26 | 26
9 | 106 |  |  |  | 26 | 52 |  | 52 | 
10 | 106 |  |  |  | 26 | 106 |  |  | 
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 106 |  |  |  | 26 | 52 |  | 26 | 26
2 | 26 | 26 | 52 |  | 26 | 106 |  |  | 

## Slide 20: Combination of Large-size RUs
We can also consider the following allocation for Combination of Large-size RUs based on 11be SFD[1].
  We assume that the multiple user transmission(i.e. OFDMA) but MU-MIMO is not considered.
  In 80MHz
  In 160MHz
  For the 240MHz and 320MHz, the above combinations for 160MHz can be used in the continuous 160MHz within this bandwidth.
index | 1 | 2 | 3 | 4
1 | 242 | 242 | 484 | 
2 | 242 | 242 | 484 | 
3 | 484 |  | 242 | 242
4 | 484 |  | 242 | 242
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | 484 |  | 484 |  | 996 |  |  | 
2 | 484 |  | 484 |  | 996 |  |  | 
3 | 996 |  |  |  | 484 |  | 484 | 
4 | 996 |  |  |  | 484 |  | 484 |