## Slide 1: Synchronous Multi-Link Operation Follow-Up
Date: 2020-07-26
Authors:

## Slide 2: Recap: Ending Times Alignment
802.11be supports the following PPDU transmission restriction for the constrained multi-link operation:
  If an AP MLD intends to align the ending time of DL PPDUs carrying a frame soliciting an immediate response simultaneously sent to the same non-STR non-AP MLD on multiple links, the AP MLD shall ensure that the difference between the ending times of transmitting DL PPDUs is less than TBD (< SIFS).
  Where the reference of the ending time of the PPDU is TBD.
  [Motion 111, #SP0611-31, [7] and [109]]

## Slide 3: Introduction
This contribution resolves the TBD requirements about the ending times alignment.

## Slide 4: Ending Times Alignment in Synchronous Multi-link Operation
If the difference between the ending times of the DL PPDUs is less than SIFS (i.e., aSIFSTime + aSignalExtension), any UL PPDUs solicited from the DL PPDUs are not overlapped with DL PPDUs.
  aSIFSTime:
    10 μs when operating in the 2.4 GHz band
    16 μs when operating in the 5 GHz bands
  aSignalExtension:
    0 μs when operating in the 5 GHz band
    6 μs when operating in the 2.4 GHz band

## Slide 5: Ending Times Alignment in Synchronous Multi-link Operation
But, if the SIFS timing accuracies of STAs within the same non-STR non-AP MLD is different, a reception time of DL PPDUs and a transmission time of UL PPDUs can be overlapped.
  In IEEE 802.11-2016, the SIFS timing accuracy is ±0.9 μs.
    An IEEE 802.11 implementation of a non-DMG STA shall not allow the space between frames that are defined to be separated by a SIFS, as measured on the medium, to vary from the nominal SIFS by more than ±10% × (aSlotTime – aAirPropagationTime) for the PHY in use.

## Slide 6: Ending Times Alignment in Synchronous Multi-link Operation
Considering the SIFS timing accuracy issue, the difference between the ending times of the DL PPDUs should be less than SIFS (i.e., aSIFSTime + aSignalExtension) – Timing Margin.
  Timing Margin shall be less than 0.9 μs (i.e., 10% × (aSlotTime – aAirPropagationTime).
The Timing Margin can be set to any value between 0.9 μs and 16 μs.

## Slide 7: Ending Times Alignment in Synchronous Multi-link Operation
As Timing Margin decreases, the ending times are more loosely aligned.
  Pros: At a transmitter side, the padding complexity can be reduced.
  Cons: At a receiver side, the cross link information is not timely available. The padding overhead can be increased.
In this contribution we propose to choose a medium value (i.e., 8 μs) to balance the pros and cons at a transmitter and a receiver.
PPDU 1
PPDU 2
BA 1
SIFS (16μs)
15μs
The PPDU2 related information may not be available on STA of Link 1 within 1 us.
In such case, the BA1 frame should be prepared for the worst condition.
In consequence, an unnecessary padding is caused.
BA1
Link 1
Link 2
Padding
Padding
SIFS (16μs)

## Slide 8: Ending Times Alignment in Synchronous Multi-link Operation
So, the following is the updated ending times alignment requirement.
  If an AP MLD intends to align the ending time of DL PPDUs carrying a frame soliciting an immediate response simultaneously sent to the same non-STR non-AP MLD on multiple links, the AP MLD shall ensure that the difference between the ending times of transmitting DL PPDUs is less than (aSIFSTime + aSignalExtension)/2.

## Slide 9: Ending Times Alignment in Synchronous Multi-link Operation
Packet
Extension
Signal
Extension
Signal
Extension
About the reference of the ending time of the PPDU, we propose to choose the end of the OFDM symbol.
  When the Packet Extension field is present in the PPDU, the ending time of the PPDU is the end of the last symbol of the Packet Extension field.
  But, the Signal Extension field is not regarded.
5GHz
6GHz
Data
MAC Padding
AP
STA
AP
STA
PHY Padding
Packet
Extension
Data
MAC Padding
PHY Padding
Packet
Extension
SIFS
Ack
MAC Padding
PHY Padding
Block Ack
Difference between the ending times of the transmissions is less than (aSIFSTime + aSignalExtension)/2
SIFS

## Slide 10: Straw Poll 1
Do you support to amend the SFD texts as the following?
  802.11be supports the following PPDU transmission restriction for the constrained multi-link operation:
    If an AP MLD intends to align the ending time of DL PPDUs carrying a frame soliciting an immediate response simultaneously sent to the same non-STR non-AP MLD on multiple links, the AP MLD shall ensure that the difference between the ending times of transmitting DL PPDUs is less than or equal to TBD (< SIFS) 8 μs ((aSIFSTime + aSignalExtension)/2).
      Where the reference of the ending time of the PPDU is TBD not including the Signal Extension field.
  Approved with unanimous consent