## Slide 1: Forward Compatible OFDMA
Date: 03/28/20
Authors | Affiliation | Email
Xiaogang Chen | Intel | Xiaogang.c.chen@intel.com
Qinghua Li |  | 
Feng Jiang |  | 
Thomas Kenney |  | 
Po-Kai Huang |  | 
Laurent Cariou |  | 
Stacey Robert |  | 

## Slide 2: Outline
Background of the forward compatible OFDMA;
Design examples;
Summary.

## Slide 3: Forward compatible OFDMA (1/2)
Concept:
  Enable the STAs of different WiFi amendments (WiFi 7/8/…STAs) be scheduled in one transmission.
    One transmission could be One PPDU or Multiple orthogonal PPDUs.
Motivations:
  A large number of legacy WiFi devices will coexist with new WiFi devices for a long time;
  A 320MHz capable AP may serve several 80MHz capable clients each of which is from the same or different WiFi amendments.
  Improves the scheduling flexibility and efficiency as WiFi evolves.

## Slide 4: Forward compatible OFDMA (2/2)
Forward compatible: enable multiplexing of EHT STA with EHT+ STA
  PHY requirements:
    Consistent tone spacing in different WiFi amendments;
    Preamble design support.
  MAC requirement:
    Enhanced Trigger/announcement frame.
How about backward compatible? I.e. Enable multiplexing of HE STA with EHT STA in one transmission.
  Both HE and EHT technologies are on the table and ready for design;
  Backward compatible can also be considered if a simple solution is feasible;
    Must be transparent to WiFi 6 STA.

## Slide 5: Example of the MAC Protocol
Downlink Announcement frame
  Move EHT and EHT+ STA to non-primary 80 for the succeeding Tx/Rx;
  HE STA stay on the P80 (Transparent to HE STA).
EHT and EHT+ STA move back to P80 after Tx/Rx.
Notes: Otherwise one PPDU will have HE preamble, EHT preamble, etc.

## Slide 6: Considerations of the PHY Protocols
HE clients always camp on P80 and fully reuse the HE processing flow;
  Transparent to HE STA.
EHT clients understand the new structure, and will process the EHT portion accordingly;
  Details will be defined in TGbe.
Future generation (e.g. 11bx) STAs understand both legacy portions and 11bx portion. They will process their own portion correctly.

## Slide 7: Considerations of the PHY Protocols (Cont’d)
All proposals below in IEEE are useful tools to support mixing WiFi amendments in one transmission:
  Per 80MHz variable U-SIG;
  Per 80MHz variable EHT-SIG;
  Per 80MHz puncturing indication;
  Symbol alignment between 80MHz segments.
    Guarantee the orthogonality of the transmissions from different WiFi amendments.
Protocol-wise, forward compatible OFDMA is well backed up by the proposals in IEEE.
  May not need to initiate new preamble related design other than the ones we already have;
  Details need to be polished and not the scope of this contribution.

## Slide 8: Summary
Enable multiple WiFi amendments in one transmission with OFDMA could be an useful feature as WiFi evolving;
Propose to support this feature in EHT.
  The current protocols TGbe developed in IEEE paved the path for this feature already. Not much new protocol are required.

## Slide 9: SP
Do you agree that 11be support the design of allowing multiplexing STAs of different amendments in one transmissions with OFDMA?
  STAs of different amendments may include HE, EHT and post-EHT STA;
    The BW allocated to different STAs that can be mixed in one transmission is TBD;
  This feature is targeted for R2.