## Slide 1: Some Thoughts on Control Response MCS Negotiation
Date: 2020-04-27
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang |  |  |  | 
Robert Stacey |  |  |  | 
Daniel F Bravo |  |  |  | 
Emily Qi |  |  |  | 
Notes: September 2012

## Slide 2: Discussion in TGmd vs. TGbe
The discussion on Control Response Rate Selection (described in 11-19-1562) is an important discussion, and need a broad review/evaluation.
We believe TGbe would be a venue to entertain the discussion because
  Consideration for the latest technology can be factor in
  Problem can be analyzed as a whole
  Avoid to have pre-be solution and be solution

## Slide 3: Recommend for Analysis
The proposal vaguely talks about solving power imbalance and assumes that
  The recipient can figure out the power imbalance between the originator and the recipient
  The recipient can then figure out the MCS difference across the board needed to accommodate that power imbalance
  The above question is considered implementation specific and ignored in the proposal
In reality,
  MCS decoding curve is different for each device and depends on
    Channel Model
    Size of the frames
    Impairments
  We expect that a STA has to guess and keep changing the negotiated value similar to a link adaptation procedure (try MCS difference 1, try MCS difference 2, and so on)
  Analysis maybe useful to understand if this additional procedure on top of existing link adaptation procedure is helpful and improves the performance

## Slide 4: Requirement of Negotiation
The current spec assumes that the originator can reject the request for whatever reason
However, the previous slide highlights that a STA may need adaptation algorithm to figure out the difference
If a originator can reject for whatever reason, then there is no way for the STA to do adaptation algorithm
We think the negotiation procedure may need to be simplified if we want the proposal to be useful

## Slide 5: Conclusion
We recommend the overhaul of control response MCS selection to be discussed in 11be
  To consider the major change introduced by 11ax and 11be and avoid having different solutions going forward
We recommend to have more analysis to describe the gain saving for non-S1G STA
  Useful to convince people to use it after this is introduced to the spec
We recommend to reconsider the need of negotiation, and the negotiation procedure may need to be revised to make the protocol useful.