## Slide 1: Some Thoughts on Control Response MCS Negotiation
Date: 2020-04-27
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | po-kai.huang@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Daniel F Bravo |  |  |  | 
Emily Qi |  |  |  | emily.h.qi@intel.com
April 2020
Notes: September 2012

## Slide 2: Recommend for Analysis
The proposal vaguely talks about solving power imbalance and assumes that
  The recipient can figure out the power imbalance between the originator and the recipient
  The recipient can then figure out the MCS difference across the board needed to accommodate that power imbalance
  The above question is considered implementation specific and ignored in the proposal
In reality,
  MCS decoding curve is different for each device and depends on
    Channel Model
    Size of the frames
    Impairments
  We expect that a STA has to guess and keep changing the negotiated value similar to a link adaptation procedure (try MCS difference 1, try MCS difference 2, and so on)
  Analysis maybe useful to understand if this additional procedure on top of existing link adaptation procedure is helpful and improves the performance
April 2020

## Slide 3: Requirement of Negotiation
The current spec assumes that the originator can reject the request for whatever reason
However, the previous slide highlights that a STA may need adaptation algorithm to figure out the difference
If a originator can reject for whatever reason, then there is no way for the STA to do adaptation algorithm
We think the negotiation procedure may need to be simplified if we want the proposal to be useful
April 2020

## Slide 4: Consideration of 11ah vs baseline
11ah is designed for a scenario for thousands of STAs due to extended coverage, which is different from the scenario of baseline.
Different scenarios requires different consideration and analysis.
Directly copying the negotiation algorithm is not the best way to go forward.

## Slide 5: Conclusion
We recommend to have more analysis to describe the gain saving for non-S1G STA
  Useful to convince people to use it after this is introduced to the spec
We recommend to reconsider the need of negotiation, and the negotiation procedure may need to be revised to make the protocol useful.
We recommend to differentiate the scenarios used in 11ah and baseline separately rather than directly copy the algorithm
April 2020

## Slide 6: Proposed Resolution for CID 4156
Proposed Resolution: Reject.
Reject reason:
  The CRC discussed this comment at length and did not come to consensus to make the change. The major concern raised during the discussion to extend and cover PHY types beyond S1G is the need to negotiate for MCS change. Specifically, 11ah is designed for a scenario with thousands of STAs due to extended coverage, which is different from the scenario of baseline. As a result, the needs of negotiation due to huge number of STAs does not hold in the baseline scenario. Further, the uplink channel condition is dynamic and depends on many factors. The STA is likely required to have implementation specific algorithm to figure out the MCS difference and may need several rounds of change independent of the decision from the AP. Negotiation puts additional complexity on the implementation specific algorithm.