## Slide 1
Operating Bandwidth Indication for EHT BSS
Date: 2020-04-23
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei | Shenzhen, China |  | huangguogang1@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com
Yunbo Li |  |  |  | liyunbo@huawei.com
Ming Gan |  |  |  | guoyuchen@huawei.com
Yifan Zhou |  |  |  | zhouyifan8@huawei.com
Yiqing Li |  |  |  | liyiqing3@huawei.com

## Slide 2
Contribution [1-2] propose a solution to use EHT operation element to indicate > 160/80+80MHz or not, and EHT CCFS.
Further, when some 20MHz channels in the BW announced by VHT/HE Operation element are punctured, contribution [1] proposes to use Operation Mode Notification combined with VHT/EHT Operation element to announce the BW for VHT/HE STA.
  Con. This solution will change the original usage of Operation Mode Notification
In this contribution, we will give another solution to indicate channel configuration for EHT STA.
Motivation

## Slide 3
The current 160 MHz configuration is based on
  5 GHz: Channel Width, CCFS0, and CCFS1 of VHT operation element or CCFS2 of HT operation element in 5 GHz
  6 GHz: Channel Width, CCFS0, CCFS1 in 6 GHz Operation Information field
Example:
  160 MHz (|CCFS0-CCFS1/CCFS2|=8)
  80+80 MHz (|CCFS0-CCFS1/CCFS2|>16)
Recap
Primary 80 MHz
Secondary 80 MHz
CCFS0
CCFS1/CCFS2
5 GHz: Channel Width in VHT op: 1
6 GHz: Channel Width in HE op: 3
Primary 80 MHz
Secondary 80 MHz
CCFS0
CCFS1/CCFS2
5 GHz: Channel Width in VHT op: 1
6 GHz: Channel Width in HE op: 3

## Slide 4
EHT is expected to support static&dynamic channel puncture
  Static channel puncture is used to indicate which 20 MHz channel cannot be used for transmission
  Dynamic channel puncture shall be based on the indication of static channel puncture indication, which is indicated in the EHT preamble of per PPDU
We propose to define an independent EHT operation element which does not need to be used in combination with VHT/HE operation element to indicate the BW for EHT STA
  EHT STA obtains the channel configuration info by parsing EHT operation element and ignoring the channel width field and CCFS field in VHT/HE operation elements
  VHT/HE operation elements are used to indicate the bandwidth of channel without puncture and center frequency for VHT/HE STAs
Bandwidth Indication for EHT BSS

## Slide 5
EHT operation element contains the following fields
Indication Scheme
Option 1. Two CCFS fields
Primary 80/160 MHz
Secondary 80/160 MHz
CCFS3
CCFS4
Primary 80/160 MHz
Secondary 80/160 MHz
CCFS3
CCFS4
Channel Width
CCFS3
CCFS4
Puncture info

## Slide 6
Option 1. Two CCFS fields (Cont.)
Channel Width
CCFS3
CCFS4
Puncture info
Conditions | Channel Configuration
Channel width=0 | 20 MHz
Channel width=1 | 40 MHz
Channel width=2 | 80 MHz
Channel width=3 CCFS3>0, CCFS4>0, ¦CCFS4-CCFS3¦=8 | 160 MHz
Channel width=3 CCFS3>0, CCFS4>0, ¦CCFS4-CCFS3¦>16 | 80+80 MHz
Channel width=4 CCFS3>0, CCFS4>0, ¦CCFS4-CCFS3¦=16 | 320 MHz
Channel width=4 CCFS3>0, CCFS4>0, ¦CCFS4-CCFS3¦>32 | 160+160 MHz
Option 1.1 Channel Width field with 3 bits

## Slide 7
Option 1.2 Channel Width field with 2 bits
Option 1. Two CCFS fields (Cont.)
Channel Width
CCFS3
CCFS4
Puncture info
Conditions | Channel Configuration
Channel width=0 | 20 MHz
Channel width=1 | 40 MHz
Channel width=2, CCFS3>0, CCFS4=0 | 80 MHz
Channel width=2 CCFS3>0, CCFS4>0, ¦CCFS4-CCFS3¦=8 | 160 MHz
Channel width=2 CCFS3>0, CCFS4>0, ¦CCFS4-CCFS3¦>16 | 80+80 MHz
Channel width=3 CCFS3>0, CCFS4>0, ¦CCFS4-CCFS3¦=16 | 320 MHz
Channel width=3 CCFS3>0, CCFS4>0, ¦CCFS4-CCFS3¦>32 | 160+160 MHz

## Slide 8
Example
  5G band: VHT Operation element (80 MHz)
    Channel width=1, CCFS0>0, CCFS1=0
    CCFS0 indicate the center frequency of P80 MHz
  6G band: HE Operation element (80 MHz)
    Channel width=2, CCFS0>0, CCFS1=0
    CCFS0 indicate the center frequency of P80 MHz
  EHT Operation element (320 MHz)
    Channel width=4, CCFS3>0, CCFS4>0, OCP=0,|CCFS4-CCFS3|=16, Puncture bitmap: 11111011 11111011, CCFS3 indicate the center frequency of P160 MHz, CCFS4 indicate the center frequency of 320 MHz
Option 1. Two CCFS fields (Cont.)
Primary 20MHz channel
80 MHz for VHT/HE STAs
320 MHz for EHT STAs

## Slide 9
EHT operation element contains the following fields
Indication Scheme
Option 2. Three CCFS fields
Primary 80 MHz
Secondary 80 MHz
CCFS3
CCFS4
Secondary 160 MHz
CCFS5
Primary 80 MHz
Secondary 80 MHz
CCFS3
CCFS4
Secondary 160 MHz
CCFS5
Channel Width
CCFS3
CCFS4
Puncture info
CCFS5

## Slide 10
Option 2. Three CCFS fields
Channel Width
CCFS3
CCFS4
Puncture info
CCFS5
Conditions | Channel Configuration
Channel width=0, CCFS3>0 | 20 MHz
Channel width=1, CCFS3>0 | 40 MHz
Channel width=2, CCFS3>0 | 80 MHz
Channel width=3, CCFS3>0, CCFS4>0, CCFS5=0 ¦CCFS4-CCFS3¦=8 | 160 MHz
Channel width=3, CCFS3>0, CCFS4>0, CCFS5=0 ¦CCFS4-CCFS3¦>16 | 80+80 MHz
Channel width=4, CCFS3>0, CCFS4>0，CCFS5>0 ¦CCFS4-CCFS3¦=8 ¦CCFS5-CCFS4¦=16 | 320 MHz
Channel width=4, CCFS3>0, CCFS4>0，CCFS5>0 ¦CCFS4-CCFS3¦=8 ¦CCFS5-CCFS4¦>32 | 160+160 MHz

## Slide 11
We propose to define an independent EHT operation element to indicate the channel configuration for EHT BSS, which does not based on the indication of CCFS0 and CCFS1 in VHT/HE operation elements
  EHT STA obtains the channel configuration info by parsing EHT operation element and ignoring the channel width field and CCFS field in VHT/HE operation elements
  VHT/HE operation elements are used to indicate the bandwidth of unpunctured channel and center frequency for VHT/HE STAs
Conclusions

## Slide 12
[1] 11-20-0398-02-00be-eht-bss-with-wider-bandwidth
[2] 11-20-0384-01-00be-320-mhz-bss-configuration
Reference

## Slide 13
Do you support to define EHT operation element to indicate the channel configuration for EHT STA, which does not need to combine with the indication of CCFS0 and CCFS1 in VHT/HE operation elements.
  Note. VHT/HE operation element are used to announce the unpunctured BW for VHT/HE STA
  Y
  N
  A
Straw Poll 1

## Slide 14
Do you support to define EHT operation element with the N number of CCFS fields to indicate channel configuration for EHT BSS?
  Option 1. N=2
  Option 2. N=3
  Option 1:
  Option 2:
  Neither:
  Abstain
Straw Poll 2

## Slide 15
Do you support to define EHT operation element with the M bits of Channel Width field to indicate channel width for EHT BSS?
  Option 1. M=2
  Option 2. M=3
  Option 1:
  Option 2:
  Neither:
  Abstain:
Straw Poll 3