## Slide 1
Scoreboard Operation for Multi-link Aggregation
Date: 2020-04-22
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei | Shenzhen, China |  | huangguogang1@huawei.com
Yuchen Guo |  |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | liyunbo@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com
Yifan Zhou |  |  |  | zhouyifan8@huawei.com
Yiqing Li |  |  |  | liyiqing3@huawei.com

## Slide 2
Multi-link aggregation is allowed MPDUs belonged to one TID to transmit simultaneously through multiple links
  Increase the throughput of this TID
  Reduce the delay of MPDUs belonged to this TID
Background

## Slide 3
When the initiator transmits a BAR to the recipient, if there are MSDUs/A-MSDUs whose Sequence Number values are less than the value in Block ACK Start Sequence Control field of the BAR, the recipien will discard these MSUDs/A-MSDUs even they are correctly decoded.
In this contribution, we will give a simple but efficient solution to solve this issue
Motivation
Link1
Link2
A-MPDU1 (Seq 1 to 31, 60, 61)
A-MPDU2 (Seq 32 to 59)
BA
BA
BA
BAR
Adjust WinStartB
The retransmission of missed frames in A-MPDU1 is not helpful. The recipient will discard the retransmitted MPDUs in A-MPDU1 because of the adjusted WinStartB.
Some frames in A-MPDU1 are not received correctly.
BA is not received correctly.

## Slide 4
Contribution [2] had been proposed
  Add one bit indication info in the BAR frame to indicate whether the initiator of BAR wants the recipient of BAR to shift the WinStartB or not.
    If the initiator transmits a BAR to the recipient, the initiator shall guarantee that all the MSDUs/A-MSDUs whose Sequence Number values are less than the value in Block ACK Start Sequence Control field of the BAR will not be transmitted after the BAR.
    In other words, the initiator shall guarantee that there is no MSDU/A-MSDU whose Sequence Number value is less than the value in Block ACK Start Sequence Control field of the BAR
Existing Solution

## Slide 5
Scoreboard operation
  Rule 1. The SSN carried in the BAR can be set to the sequence number of the next MSDU to be sent on the link or a sequence number greater than the discarded MSDU
  Rule 2. Shift rules of scoreboard window
    When the BAR is received, the recipient shifts the scoreboard to the right so that WinStart = SSN from the BAR and returns a BA frame with the contents of the scoreboard.
    For each received data frame,
      If SN is within the current scoreboard window, i.e.WinStart ≤ SN ≤WinEnd, then the scoreboard records receipt at the offset represented by SN.
      If SN is outside the current scoreboard window, but within half sequence space range, i.e. WinEnd < SN < WinStart + 2^11, then the scoreboard is shifted right to accommodate SN, i.e. set the starting serial number of the current window of the scoreboard to WinStart = SN-WinSize + 1.
      If SN is more than half the sequence space beyond the window, i.e. WinStart + 2^11 <SN < WinStart, then no change is made.
Recap

## Slide 6
Rule 1. The SSN carried in the BAR sent on each aggregated link can be set to the sequence number of the next MSDU to be sent on the link or a sequence number greater than the discarded MSDU
Rule 2. Delayed shift rules of scoreboard window.
  SSN_i is denoted as the latest SSN value of aggregated link i, which is initialized to the Starting Sequence Number subfield value carried in the ADDBA Request/Response frames. When received a BAR frame on link i, then update the SSN_i to SSN carried in the BAR frame
  When the BAR is received, the recipient shifts the scoreboard to the right so that WinStart = min(SSN_1,SSN_2,…, SSN_N) and returns a BA frame with the contents of the scoreboard.
Scoreboard Operation for MLA

## Slide 7
Rule 2. (Cont.)
  For each received data frame,
    If SN is within the current scoreboard window, i.e.WinStart ≤ SN ≤WinEnd, then the scoreboard records receipt at the offset represented by SN.
    If SN is outside the current scoreboard window, but within half sequence space range, i.e. WinEnd < SN < WinStart + 2^11, then the scoreboard is shifted right to accommodate SN, i.e. set the starting serial number of the current window of the scoreboard to WinStart = SN-WinSize + 1. If SSN_i<WinStart, then SSN_i is updated to WinStart, i=1,2,…,N
    If SN is more than half the sequence space beyond the window, i.e. WinStart + 2^11 <SN < WinStart, then no change is made.
Scoreboard Operation for MLA

## Slide 8
At the initial time t0, both SSN_1 and SSN_2 are initialized to SSN_0, where SSN_0 is the starting sequence number carried in the ADDBA request and ADDBA response frame, and SSN_1 and SSN_2 are the BAR received on Aggregate Link 1 and Aggregate Link 2, respectively The SSN value carried in the frame. Then the receiver sets WinStart to min (SSN_1, SSN_2) = min (0,0) = 0
At time t1, the receiving end receives a BAR frame on aggregation link 1, which carries SSN_1 of 20, and then the receiving end sets WinStart to min (SSN_1, SSN_2) = min (20,0) = 0
At time t2, the receiving end receives a BAR frame on aggregated link 2, which carries SSN_2 of 30, and then the receiving end sets WinStart to min (SSN_1, SSN_2) = min (20,30) = 20
At time t3, the receiving end receives a BAR frame on aggregated link 1, which carries SSN_1 of 25, and then the receiving end sets WinStart to min (SSN_1, SSN_2) = min (25,30) = 25
At time t4, the receiving end receives a BAR frame on aggregated link 1, which carries SSN_1 of 28, and then the receiving end sets WinStart to min (SSN_1, SSN_2) = min (28,30) = 28
At time t5, the receiving end receives a BAR frame on aggregated link 2, which carries SSN_2 of 40, and then the receiving end sets WinStart to min (SSN_1, SSN_2) = min (28,40) = 28
At time t6, the receiving end receives a BAR frame on aggregated link 1, which carries SSN_1 of 45, and then the receiving end sets WinStart to min (SSN_1, SSN_2) = min (45,40) = 40
And so on
Example 1-Delayed shift
For simplicity, we make the following assumption
ACK Policy field of all QoS data frames are set to Block ACK
There is no case where SN falls on WinEnd <SN <WinStart + 2 ^ 11

## Slide 9
…
Link 1: Data SN=103
103
4
WinSize=100
Sequence Number Space
…
Link 2: Data SN=105
1
1
…
103
4
Link 2: BAR SSN=20
1
SSN_1=0, SSN_2=0, WinStart=4
Since SSN_1<WinStart, SSN_2<WinStart, then SSN_1=4, SSN_2=4
SSN_2=20
WinStart=min(SSN_1,SSN_2)
=min(4,20)
…
Link 1: BAR SSN=10
1
6
105
Example 2-Delayed shift
SSN_1=4,SSN_2=20, WinStart=6, Since
SSN_1<WinStart,
SSN_2>WinStart, then
SSN_1=6
…
109
10
SSN_1=10,
WinStart=min(SSN_1,SSN_2)
=min(10,20)
Link 1: Data SN=10
…
…
…
…
…
103
6
Within the Scoreboard window, then no change is mad
1
103
105
1

## Slide 10
Advantages of proposed solution
  There is no requirement for interaction capability between aggregated links at the transmitter side, which is very useful especially for non-collocated MLA
  No need to change the existing BAR frame format and sending rules at the transmitter side, just change the shift rule of WinStart at the receiver side
Discussions

## Slide 11
In this contribution, we proposed a method of scoreboard operation for multi-link aggregation.
Summary

## Slide 12
[1] 11-20-0122-01-00be-a-bar-variant-for-multi-link-operation
[2] 11-19-1856-03-00be-a-mpdu-and-ba
Reference

## Slide 13
Do you agree that the proposed shift rules of scoreboard window for multi-link aggregation?
  Yes
  No
  Abstain
Straw Poll 1