## Slide 1: MLA: MAC Address Security
Date: 2020-06-29
Authors:

## Slide 2: Current Direction of 11be Security
Each AP of an AP MLD uses a different MAC Address
  The AP MLD address can be a value different than any of the AP MAC addresses or it can take the value of one of the AP MAC addresses
Each STA of a non-AP MLD also uses a different MAC Address
  The non-AP MLD address can be a value different than any of the STA MAC addresses or it can take the value of one of the STA MAC addresses
Single PMK per MLD
Single PMKSA per MLD
Single TK per MLD

## Slide 3: AP MLD and Non-AP MLD

## Slide 4: Current Direction of 11be Security (Cont’d)
During association, all the link MAC addresses and the MLD address of both peer MLDs are exchanged (all unprotected though)
The 4-way handshake uses the MLD address of the peer MLDs (as opposed to the MAC address of the peer STAs)
Post-authentication, the TA/RA fields in the MAC header use the MAC addresses of the link for which the frames are transmitted on

## Slide 5: Potential Security Flaw
Traditionally in the single link case, the MAC addresses of the peer STAs are used for 4-way handshake
  The same MAC addresses are then used in the TA/RA of the frame header
  Therefore, the MAC addresses are protected by the 4-way handshake
  The TA/RA fields are protected by the MIC after the 4-way handshake
In the MLO case (currently proposed),
  The MAC addresses are exchanged during Association (unprotected)
  The MLD addresses of the peer MLDs are used for the computation of the PTK in the 4-way handshake. MAC addresses are still used for the actual OTA msgs

## Slide 6: Potential Security Flaw (Cont’d)
Step 1: An attacker replaces the authentic STA MAC addresses of the links* during Association (unprotected) with some other values. *The links other than the one used for the Association
Step 2: Both peer MLDs will execute the 4-way handshake with the MLD addresses and everything will look good
Step 3: However, when the transmitter tries to send a frame with TA/RA field set to the authentic MAC addresses, the receiver will ignore this frame because the receiver only knows about the values (as the RA) injected by the attacker in Step 1 above

## Slide 7: Example
2-link AP MLD:
  MLD address = MLDa
  Link 1 AP1 MAC address = a1
  Link 2 AP2 MAC address = a2
2-link Non-AP MLD:
  MLD address = MLDm
  Link 1 STA1 MAC address = m1
  Link 2 STA2 MAC address = m2

## Slide 8: Example (Cont’d)
Association performed on Link 1 (a1, m1), unprotected
Association exchanges:
  (MLDa, a1, a2, MLDm, m1, m2’)
    Attacker replaces the original m2 by m2’ in the Association frames
4-way handshake performed on Link 1 (a1, m1) successfully
Now AP MLD sends a legit frame on Link 2 with
  <TA, RA> = <a2, m2> , which will be ignored by the STA on Link 2, which is looking for frames with RA=m2’ and not m2
  => Link 2 will appear dead to the AP MLD

## Slide 9: Proposed Solution
To include all the MAC addresses of an MLD during the 4-way handshake so they could be bound to the MLD address and MLD entity
The STA should verify these MAC addresses are the same as those exchanged during the Association Request/Response phase
E.g., add the MAC addresses of the STAs affiliated with the MLDs as new KDEs in the EAPOL-Key msg 3, and either msg 2 or msg 4. In addition, FT and FILS authentication cases would likely need to be covered as well and for those, similar payload would need to be included either in FTE subelement or a new IE in (Re)Association Request/Response frame

## Slide 10: SP1
Do you agree to the following?
  A non-AP MLD includes the following in the (re)Association Request frame:
    The non-AP MLD address
    The MAC addresses of all the STAs of the non-AP MLD
  An AP MLD includes the following in the Association Response frame:
    The AP MLD address
    The MAC addresses of all the APs of the AP MLD

## Slide 11: SP2
Do you agree to the following?
  A non-AP MLD and AP MLD use a single and same link to perform the following (i.e., all the following OTA messages will have the same <TA, RA> ):
    802.11 Authentication (e.g., the open authentication, SAE, etc)
    Association and Re-association
    4-way handshake

## Slide 12: SP3
Do you agree to the following?
  The 4-way handshake uses the MLD addresses of the peer MLDs in lieu of MAC addresses (<TA, RA> of the frames corresponding to the 4-way handshake msgs) as AA and SPA in PTK derivation
  During the 4-way handshake, the peer MLDs shall exchange the MAC addresses of the STAs corresponding to each setup link
  The MLDs shall verify that the MAC addresses corresponding to each setup link that are exchanged during the 4-way handshake and the multi-link setup are identical. If there is a mismatch, the MLD shall tear down the multi-link (re)setup with the peer MLD