## Slide 1: Identifier Privacy Service
1
Date: 2020-05-12
Authors:
Name | Affiliations | Address | Phone | email
Nehru Bhandaru | Broadcom Inc. | 250 Innovation Drive, San Jose CA 95134 | 408-391-2159 | nehru.bhandaru@Broadcom.com
Thomas Derham | Broadcom Inc. | 16340 W Bernardo Dr, San Diego CA 92127 |  | thomas.derham@Broadcom.com

## Slide 2: Problem & Background
Privacy is about protecting any identifiable information
  Avoid tracking without knowledge and permission of a tracked device/user
  802.11 protocols contain identifiers not protected by RSNA mechanisms
Increasing industry attention to privacy
TGm has had various related discussions and specific proposals
  11-20/0543r2 - Privacy of password identifiers
  11-20/0366r0 - MAC privacy and PMKSA caching
  11-19/0489r0 - Client Privacy Discussion
Some comments in TGm suggested the possibility of a general scheme
  Cover privacy of Password Identifiers, PMKIDs, extensible to potentially cover other identifiers
This submission is a summary of generic identifier protection service capability for 802.11 described in 11-20/0746r0
  Based on ECIES, a scheme also used by 3GPP (TS 133.501) and IETF RFC8492 for identifier protection
  Can be applied to password identifiers to resolve CID 4731
  Extended to support privacy of other identifiers and downgrade protection

## Slide 3: Solution Considerations
Possibility to protect identifiers in initial exchange of a first-time connection to the network, as well as subsequent connections
Protection against active attacks, including downgrade protection
Avoid changes to existing protocols/computation
Minimizing state on AP and non-AP STA
Low overhead per identifier protected
Minimal protocol complexity, e.g. new information elements
Potentially extensible to support other identifiers
  e.g. support for avoiding device/user fingerprinting

## Slide 4: Proposal Outline
Protection using ECIES [2]
ESS-wide public-private key pair
  Private key distributed across APs in the ESS (out-of-scope distribution)
  Public key idpk securely distributed to non-AP STAs using existing handshakes (e.g. 4-way)
  Key pair assumed constant for the lifetime of the network
Identifier Privacy (IDP) service – dot11IdentifierPrivacySupported
  Advertised in RSNXE, Downgrade protected by STA policy, once idpk is known
Non-AP STA chooses which identifiers it wants to protect, if any
  Protected by in-place encryption of the entire Information field of IEs that contain the identifiers, using symmetric key
  IDP MIC element included in frames that include protected IEs – e.g. authentication/association frames, containing:
    list of the protected element IDs, Ephemeral DH public key and MIC
AP protects the response if non-AP STA is requesting the service
  Includes IDP MIC element; Status fields included in AAD to prevent downgrade
Pseudonym scheme for PMKID protection in EAPOL M1 and M2

## Slide 5: Cost/Benefit
Similar in complexity to 11-20-0543r2
  Requires two ECC operations per-exchange on non-AP STA
  One ECC operation per protected frame on the AP
    Optimize to one operation per exchange by STA using same ephemeral key for all frames sent during the same exchange
    Similar complexity to 0543r2 where encrypted value is used to generate PT with an ECC Scalar Operation
  Most 802.11 devices now support ECC
If idpk is obtained a-priori, can protect the exchange of the first-time connection
  Protects against passive attacks
  If obtained in a trusted manner, protects against active attacks
Non-AP STA has control over what to protect
Minimal effect on underlying protocols
  No change to SAE to provide password identifier protection
  One MIC for all the identifiers protected
Proposal covers
  General framework, Password Identifier privacy, PMK Identifier privacy

## Slide 6: Open Issues and Next steps
Some Issues
  Bootstrapping idpk
    Should there be an unprotected initial exchange to provision idpk, for use cases where there is no secure out-of-band channel
    Trusted out-of-band bootstrapping mechanisms might include MDM-configured network profiles, attribute in QR code URI, etc.
  Update of idpk
  Enhanced denial of service protection – e.g. based on proof of work
  Padding for hiding password identifier length w/ in-place encryption
    reuse the same IE with IETF RFC 8018 padding when protected with IDP mechanism
TG member feedback

## Slide 7: References
[1] IEEE P802.11-REVmd™/D3.2, March 2020
[2] SEC1 – Elliptic Curve Cryptography - https://www.secg.org/sec1-v2.pdf
[3] 11-20/0543r2 – Protected Password Identifiers for Privacy
[4] 11-20/0366r0 – MAC Privacy and PMKSA caching
[5] ETSI TS 133 501 V15.1.0 (2018-07) – 5G Security Architecture and Procedures
[6] IETF RFC 8492 – Secured Password Ciphersuites for TLS
[7] 11-19/0489r0 – Client Privacy Discussion
[8] IETF RFC 8018 - PKCS #5: Password-Based Cryptography Specification Version 2.1