## Slide 1: Multi Link SM Power Save Mode
Date: 2020-04-29
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 

## Slide 2: Introduction
Multi-link operation will bring a lot of benefits, including higher peak throughput, lower latency, increased reliability, etc.
On the other hand, due to the use of multiple RF chains, multi-link operation will also bring higher power consumption.
In the baseline SPEC, we have the dynamic SM power save mode to control the power consumption when the traffic is light loaded.
In this contribution, we extend the dynamic SM power save mode to the multi-link scenario to decrease the power consumption of multi-link.

## Slide 3: Recap – Dynamic SM Power Save Mode
The dynamic SM power save mode allows a non-AP STA to operate with only one active receive chain for a significant portion of time.
An SM Power Save Frame shall be transmitted to enter the dynamic SM Power Save Mode.
In dynamic SM power save mode, the STA switches to the multiple receive chain mode when it receives the frame addressed to it and switches back immediately when the frame exchange sequence ends.
Such a frame exchange sequence shall start with a single-spatial stream individually addressed frame that requires an immediate response.
SM Power Save Frame
ACK
RTS/Data
CTS/BA
Data
BA
Data
BA
Multiple Receive Chains
Multiple Receive Chains
Single Receive Chain
Single Receive Chain
……
AP
STA

## Slide 4: Recap – HE Dynamic SM Power Save Mode
The non-AP HE STA may enable its multiple receive chains if it receives a Trigger frame, including
  MU-RTS Trigger frame
  BSRP Trigger frame
  BQRP Trigger frame
The STA switches to the multiple receive chain mode if it receives the Trigger frame addressed to it as defined above and switches back immediately after the frame exchange sequence ends
Trigger
response
Data
BA
Data
BA
Multiple Receive Chains
Multiple Receive Chains
Single Receive Chain
Single Receive Chain
……
SM Power Save Frame
ACK
AP
STA

## Slide 5: ML SM Power Save Mode
After multi-ink setup, the non-AP STA can use multiple links and multiple RF chains to communicate with the AP
However, when the traffic load is not so high, the non-AP STA can keep only one link active with only one RF chain, other links can be turned off, this link can be called anchor link
Once the AP has data to transmit to the non-AP STA, the first frame shall be transmitted with single link and single stream, then the non-AP STA shall switch to the multi-link multi-RF chain state
The non-AP STA can switch back to single-link and single-RF chain immediately after the frame exchange sequence ends
MU-RTS /Data/TF
CTS/BA/resp
Data
BA
Data
BA
Multi-link Multi-RF chain
Multi-link Multi-RF chain
Single-link Single-RF chain
Single-link Single-RF chain
……
Data
BA
Data
BA
……
off
off
ML SM Power Save Frame
ACK
AP1
STA1
AP2
STA2
link1
link2
Note: AP1 and AP2 belong to the same AP-MLD ; STA1 and STA2 belong to the same non-AP MLD

## Slide 6: ML SM Power Save Mode
Question 1: when the non-AP STA switches to the multi-link multi-RF chain mode, which links should the non-AP STA turn on?
Option 1: turn on all the enabled links
  Easy, but consumes more power
Option 2: turn on the links which are mapped by the TIDs of the corresponding DL data frames.
  Power efficient, the AP needs to tell the non-AP STA the TIDs of the DL data
Option 3: the AP can indicate the non-AP STA which links to turn on in the first frame
  Power efficient, the AP needs to tell the non-AP STA the links that it is going to use
  The first frame can be a MU-RTS frame (with some modification to carry the indication)
We prefer option 3. Reason:
  The AP MLD decides which links are scheduled to be used for data transmission to the non-AP MLD;
  The AP MLD knows which links it is about to win the contention based on the medium state and the backoff counter value

## Slide 7: ML SM Power Save Mode
Question 2: How to determine the frame sequences on multiple links have ended?
Option 1: Link-by-Link determination
  Each link can be switched off if one of the following happens
    It receives an individually addressed frame addressed to another STA.
    It receives a frame with a TA that differs from the TA of the frame that started the TXOP.
    The CS mechanism indicates that the medium is idle at the TxPIFS slot boundary (counting from the time that the STA starts receiving its own frames).
  Drawback: limitation on cross-link retry
Option 2: MLD level determination
  Use the “More Data” bit to serve the purpose since the meaning of the “More Data” bit has been changed for the MLD [1]
    Passed SP: When AP MLD transmit a BU in one link to a non-AP MLD, if there is at least one additional buffered BU of any TID or management frames that is mapped to this link by TID-to-link mapping or default mapping for the same non-AP MLD, the More Data subfield is set to 1, otherwise the More Data subfield is set to 0.
We are OK with either option

## Slide 8: ML SM Power Save Mode
Question 3: What if the non-AP MLD does not receive any frame addressed to it on the newly enabled links?
Solution: the newly enabled links are automatically turned off if the non-AP MLD does not receive any frame addressed to it when the TXOP on the anchor link has finished.

## Slide 9: Conclusion
  We propose a multi-link SM power save mode in this contribution
  Single link and single stream is enabled after entering the ML SM power save mode
  Multi-link and multi-stream will be activated when the DL data frames arrive.

## Slide 10: Straw Poll 1
  Do you support to define a ML (multi-link) SM power save mode in R2 as follows:
    A non-AP MLD that is in ML SM PS mode can use only one link and one active receive chain for receiving and responding to an initial control frame sent to it
    The non-AP MLD automatically becomes available on other links when it receives the start of a frame exchange sequence addressed to it
      How to determine the “other links” is TBD
    The non-AP MLD may become unavailable on any of the “other links” if one of the following is satisfied
      The TXOP on the “other link” has ended
      Other TBD condition to deal with the case when the non-AP MLD does not receive any frame addressed to it on the “other links”
    This is an optional feature for both AP and non-AP MLD

## Slide 11: Reference
[1] 11-20-0472-02-00be-discussion-of-more-data-subfield-for-multi-link