## Slide 1: Multi Link Group Addressed Frame delivery for non-STR MLD
Date: 2020-04-23
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 

## Slide 2: Introduction
Multi-link operation is a key feature in TGbe
Non-AP MLD may be non-STR on two links: not capable of transmitting on one link while receiving on the other link
On each link, the non-AP MLD always has DL frames to receive if it’s not in PS mode
  Beacon frame
  Group addressed frames
    Broadcast frames
    Multicast frames
When a non-STR non-AP MLD is receiving DL frames on a link, there should be some restrictions on the other link, e.g., The non-STR non-AP MLD should not transmit on the other link
In this contribution, we propose a scheme on group addressed frame delivery to alleviate the above restrictions

## Slide 3: Motivation
As show in the following figure, when link 1 is used for transmitting Beacon and group addressed frames, there are some restrictions on link 2, and vice versa.
  Restriction 1: The AP-MLD should not transmit a frame to the non-STR non-AP MLD on Link 2 which solicits response
  Restriction 2: The non-STR non-AP MLD should not contend channel on Link 2 to transmit frames
MLD1 - AP1
Link 1
Link 2
MLD2 - STA1
MLD1 – AP2
MLD2 – STA2
DTIM Beacon
DTIM Beacon
Group addressed frame
Group addressed frame
Restriction 1
Restriction 2
Restriction 1
Restriction 2

## Slide 4: Proposal – TXOP termination
When the non-AP MLD intends to receive Beacon frame on link 1, it may still be doing channel access on link 2, and the transmission on link 2 will impact the Beacon reception on link 1 if the TXOP is not terminated before the TBTT
When the Beacon is a DTIM Beacon, not only the Beacon reception, but also the group addressed frame reception will be impacted if the TXOP is not terminated before the TBTT
Proposed rule: if a non-STR MLD successfully contends the channel before the TBTT, then it should end its TXOP before the TBTT
MLD1 - AP1
Link 1
Link 2
MLD2 - STA1
MLD1 – AP2
MLD2 – STA2
DTIM Beacon
Group addressed frame
TXOP
backoff

## Slide 5: Conclusion
  We propose a scheme on group addressed frame delivery
  We suggest define the following operations in TGbe
    TXOP early termination of non-STR MLD to make sure the Beacon frames can be received on other links

## Slide 6: Straw Poll 1
  Do you support the following rule?
    For a NSTR link pair of a non-AP MLD, if the non-AP MLD successfully obtains a TXOP on one link before the TBTT of the other link, then it should end its TXOP before the TBTT of the other link if it intends to receive Beacon frames on the other link
      Note: the non-STR MLD may not do so if it is not aware of the TSF of the other link