## Slide 1: STA ID Indication for Constrained Multi-link Operation
Date: 2020-08-03
Authors:

## Slide 2: Recap: Constrained Multi-Link Device (MLD)
A Constrained MLD (aka non-STR MLD) is a MLD with which in-device coexistence (IDC) interference occurs when more than one STA within the MLD simultaneously transmits and receives frames on multiple links.
  When simultaneous Tx and Rx occur on 2.4 GHz band and 5 GHz links, the IDC interference is probably negligible.
  But, the IDC interference caused by simultaneous Tx and Rx on 5 GHz band and 6 GHz band links may be significantly worse depending on some implementation factors such as RF filter performance.

## Slide 3: Introduction
TGbe SFD
  Do you agree to have STA-ID related information in the EHT PPDU preamble sent to a single user and multiple users? TB PPDU is TBD.
    [20/0285r5 (SU PPDU SIG Contents Considerations, Wook Bong Lee, Samsung), SP#3, Y/N/A: 42/2/13]
The PHY ad-hoc group already decided to have the STA-ID related information in the EHT SIG in an EHT SU and MU PPDU.
  Based on the 20/0285r5 contribution, the main motivation of the STA-ID related information is to help the non-STR multi-link operation.
    For example, if STA ID info indicates a non-STR STA, AP can still transmit to other non-STR STAs.

## Slide 4: Introduction
This submission proposes how to configure the STA ID field in an EHT SU PPDU and the related MLD behavior.
  Because the STA ID field in an EHT MU PPDU is tightly coupled with other MU-MIMO/OFMDA protocol, it is not covered in this contribution.

## Slide 5: STA ID Indication in EHT SIG
For an EHT PPDU sent from an AP in an AP MLD, the STA ID field is configured as the following:
  If a receiver of the EHT PPDU is single STA, the STA ID field is set to the hash value of the AID associated with the receiver STA.
  Otherwise, the STA ID field is set to the pre-determined value (e.g., 0).
    For example, a receiver of the EHT PPDU is a group of STAs.
For an EHT PPDU sent to an AP in an AP MLD, the STA ID field is configured as the following:
  The STA ID field is set to the hash value of the AID associated with the STA in the transmitter STA.

## Slide 6: STA ID based non-AP MLD Behavior
When a STA in a constrained non-AP MLD is receiving an EHT PPDU that meets one of the following conditions, other STAs in the same constrained non-AP MLD may not transmit any PPDU or may pause the EDCA channel access.
  The UL/DL field in the EHT PPDU PHY header is equal to DL and the STA ID field in the EHT PPDU PHY header is matched with the hash value of the AID associated with the receiver STA in the constrained non-AP MLD.
  The UL/DL field in the EHT PPDU PHY header is equal to DL and the STA ID field in the EHT PPDU PHY header is equal to the pre-determined value (e.g., 0).

## Slide 7: STA ID based non-AP MLD Behavior
But, after decoding the MAC header, when the STA in the constrained non-AP MLD figures out that it is not a recipient of the EHT PPDU, other STAs in the same constrained non-AP MLD can initiate a PPDU transmission or resume the EDCA channel access.

## Slide 8: STA ID based AP MLD Behavior
While an AP in an AP MLD is receiving an EHT PPDU, other APs in the same AP MLD should not schedule any PPDU to the following STAs.
  A STA that is in the constrained non-AP MLD and whose the hash value of the AID is matched with the STA ID field in the EHT PPDU PHY header.

## Slide 9: STA ID based AP MLD Behavior
But, after decoding the MAC header is decoded, the STA in the constrained non-AP MLD that is not matched with either the RA or the TA in the MAC header in the received EHT PPDU can be scheduled by other APs in the same AP MLD.

## Slide 10: Conclusion
The STA ID field in the EHT PPDU is useful for addressing the IDC interference issue of a constrained MLD.
Also, it is helpful to reduce the power consumption of a non-AP MLD.
  Because multiple STAs are activated, the power consumption of the MLD is proportionally increased comparing with a legacy single link STA.
  So, reducing the power consumption during the reception of the intra-BSS PPDU is much important.

## Slide 11: Straw Poll 1
Do you support that the STA ID field in a downlink EHT SU PPDU sent from an EHT AP to an EHT STA identifies the recipient EHT STA?
  NOTE- The size and encoding of the STA ID field in the downlink EHT SU PPDU is TBD.
  Approved with unanimous consent

## Slide 12: Straw Poll 2
Do you support that the STA ID field in an uplink EHT SU PPDU sent from an EHT STA to an EHT AP identifies the transmitter EHT STA?
  NOTE- The size and encoding of the STA ID field in the uplink EHT SU PPDU is TBD.
  Approved with unanimous consent