## Slide 1: Trigger Consideration
Date: 2020-05-12
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Triger Frame in 11ax, 11az
Trigger frame is used to solicit UL transmission from multiple STAs.
  The UL PPDU type is fixed by Trigger Type.
    HE TB PPDU.
    Non-HT duplicated PPDU.
Trigger frames will be used for EHT and the future 802.11 generations.
Most UL multiple user transmission information are applied to various PPDU format.
Trigger frame
Common Info field
User Info field

## Slide 3: Gap Analysis
Wider BW will be supported in EHT and the future 802.11 standards.
TB PPDU format that is different from HE TB PPDU will be used, e.g. EHT TB PPDU or the future TB PPDU.
A STA can support the punctured operation where more than RU will be allocated to a single STA.
Larger Nss is needed.

## Slide 4: Trigger Design Option 1 (1)
The Trigger Type (Basic, BFRP, BQRP, MU-BAR, MU-RTS etc.) is reused (Preferred method).
  The lengths of Common Info and User Info are kept same as 11ax.
A User Info field with specific AID value (e.g. AID 2007, AID 2043) in AID12 field can announce a specific PPDU format, e.g. one of HE/EHT/future TB ( OFDMA or MU MIMO) PPDU formats and SU PPDU format.
  Other additional information can also be announced, e.g. the BW more than 160MHz, 20MHz Channel Bitmap that announce available 20MHz channel for puncture operation.
  The User Info fields follow it will use the announced specific OFDMA (MU MIMO) format until a new OFDMA(MU MIMO) format is announced.
  The HE OFDMA format can be announced explicitly or can be announced by default, e.g. the User Info fields immediately following the Common User Info field without OFDMA format announcement.
MAC header
User Info 2
Common Info
User Info 1
User Info 7
User Info 3
User Info 4
User Info 5
User Info 6
UL HE OFDMA
User Info to announce new MU format, e.g. EHT MU MIMO.
UL EHT MU MUMIMO
User Info to announce new MU format, e.g. NG_EHT OFDMA
NG_EHT OFDMA
MAC header
User Info 2
Common Info
User Info 1
User Info 7
User Info 3
User Info 4
User Info 5
User Info 6
UL HE OFDMA
User Info to announce new MU format, e.g. EHT OFDMA/MU_MIMO.
UL EHT MU MUMIMO
User Info to announce new MU format, e.g. NG_EHT OFDMA/MU_MIMO
NG_EHT OFDMA
User Info 0
User Info to announce HE OFDMA/MU-MIMO.
Optional Padding
FCS
Optional Padding
FCS

## Slide 5: Trigger Design Option 1 (2)
The User Info that announces the MU format and Common Info for specific TB type (specific User Info) has different length when it is in different Trigger Type.
  It has same length as the other User Info fields in the respective Trigger Type.
    In enhanced Basic Trigger, the specific User Info includes one octet Trigger Dependent User Info field (besides B0 to B39) which has reserved value or specific value for enhanced Basic Trigger.
    In enhanced MU-BAR, the specific User Info includes the Trigger Dependent User Info field (besides B0 to B39) that is related to single STA with BAR request from single TID.
    In enhanced BFRP Trigger, the specific User Info includes one-octet Trigger Dependent User Info field (besides B0 to B39) which has reserved value or specific value for enhanced BFRP.
    In enhanced BSRP and enhanced BQRP Trigger, the specific User Info includes B0 to B39.

## Slide 6: Trigger Design Option 2: Redefining Field in Common User
The Trigger Type (Basic, BFRP, BQRP, MU-BAR, MU-RTS etc.) is reused.
  The lengths of Common Info and User Info are kept same as 11ax.
UL HE SIG-A2 Reserved is redefined to carry the information for EHT STAs and the STAs of next generation of EHT (EHT-NG STAs).
  The UL HE SIG-A2 indicates the redesigned B54 to B52 of the Common Info field, e.g. one bit (for example B54 as Further Common Info Indication field) is always set to 0 for such purpose.
    The other fields in Common Info field are not changed.
    The Further Common Info (B55 to B62) can indicate:
      the TB PPDU type, e.g. EHT PPDU, EHT-NG TB PPDU etc.
        One exception is that MU-RTS still solicit non-HT duplicated CTS in static punctured channel, dynamic punctured channel, or non-punctured channel
      The Additional BW Indication, e.g. 320/160+160 etc.
        The 320/160+160 may be indicated by other place instead, e.g. by B63.
      Other common information.
The lengths of the other subfields in Common Info are not changed.
EHT Trigger frame
Common Info field
User Info field
Further Common Info Indication(=0) | Further Common Info
B54
B55
B62

## Slide 7: Trigger Design Option 3
The EHT TB PPDU and future are defined through new Trigger type, e.g.:
  New Trigger frame type through Trigger Dependent Common Info indicates that the AP solicits an EHT TB PPDU.
    A Trigger type indicates the EHT Trigger which includes the Trigger Depended Common Info.
  New Trigger Control frame through the new Control subtype indicates that the AP solicits an EHT TB PPDU and the future generations of TB PPDU.
Common User, TB Type Dependent Common Info, TB Type Dependent User Info can be redefined to support >160MHz BW, new TB PPDU format, punctured RUs etc.
  Common Info includes the information for all solicited TB types:
    4-bit Trigger Type (indicating the trigger extension),
    4-bit Extended Trigger Subtype (variants under trigger extension): Extended Basic Trigger, enhanced BFRP, enhanced MU-BAR, enhanced MU-RTS, enhanced BSRP, enhanced BQRP, enhanced NFRP.
    12-bit UL Length (same as 11ax),
    1-bit CS Required (same as 11ax),
    3-bit UL BW,
      One embodiment is that this field is in Common Info for Specific TB Type.
    6-bit AP Tx Power (same as 11ax),
    Other common Info fields.

## Slide 8: RU and Nss Consideration
Additional bit in User Info field may be required for RU Allocation.
Additional two bits are for >8 SS support in Basic Trigger.
  It is reasonable to assume that >8 SS only occurs in Basic Trigger case.
For Trigger design option 1 and 2, it seems we can find enough bits for these requirements.
One available bit here
One available bit in Basic Trigger

## Slide 9: Multiple RUs for Single STA Method 1
The punctured RUs for a STA is identified by one RU Allocation value (Preferred method).
  No more than one User Info field in the Trigger frame being will be addressed to a STA.
The current Trigger parsing is less changed.
The RU lookup table become bigger.

## Slide 10: Multiple RUs for Single STA Method 2
Multiple User Info fields are allocated to single STA where the multiple User Info fields have same values in their AID12 fields.
The multiple User Info fields with same AID12 field value are not separated by User Info fields for other STAs in Trigger frame.
  An option could be that one bit in User Info field indicates whether the User Info field is the only or last User Info field for a STA.
More change to the current Trigger parsing is needed.
The RU lookup table is smaller.