## Slide 1: Trigger Consideration
Date: 2020-05-12
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Triger Frame in 11ax, 11az
Trigger frame is used to solicit UL transmission from multiple STAs.
  The UL PPDU type is fixed by Trigger Type.
    HE TB PPDU.
    Non-HT duplicated PPDU.
Trigger frames will be used for EHT and the future 802.11 generations.
Most UL multiple user transmission information are applied to various PPDU format.
Trigger frame
Common Info field
User Info field

## Slide 3: Gap Analysis
Wider BW will be supported in EHT and the future 802.11 standards.
TB PPDU format that is different from HE TB PPDU will be used, e.g. EHT TB PPDU or the future TB PPDU.
A STA can support the punctured operation where more than RU will be allocated to a single STA.
Larger Nss is needed.

## Slide 4: Trigger Design Option 1 (1)
The Trigger Type (Basic, BFRP, BQRP, MU-BAR, MU-RTS etc.) is reused.
  The lengths of Common Info and User Info are kept same as 11ax.
UL HE SIG-A2 Reserved is redefined to carry the common information.
A User Info field with specific AID value (e.g. AID 2008, AID 2043) in AID12 field (Dummy User Info field) can announce the common information.
The common information can e divided into two group: TB type independent common information and TB type dependent common information:
  The TB type independent common information includes UL length, More TF, CS quired. UL BW AP Tx power, UL spatial reuse
  Other additional information can also be announced, e.g. TB type, Channel Bitmap that announce available 20MHz channel for puncture operation.
MAC header
User Info 2
Common Info
User Info 1
User Info 7
User Info 3
User Info 4
User Info 5
User Info 6
UL HE OFDMA
User Info to announce new MU format, e.g. EHT MU MIMO/OFDMA, and other common Info specific to EHT TB
UL EHT MU MUMIMO
User Info to announce new MU format, e.g. NG_EHT OFDMA, and other common Info specific to NG_EHT TB
NG_EHT OFDMA
Optional Padding
FCS
Common Info field
Further Common Info Indication(=0) | Additional Common Info
B54
B55
B62

## Slide 5: Trigger Design Option 1 (2)
In Basic Trigger the Specific User Info field include one-octet Trigger Dependent User Info field besides B0 to B39.
In MU-BAR, the Specific User Info field include the Trigger Dependent User Info field that solicit BAR from one TID besides B0 to B39.
In BFRP Trigger, the Specific User Info field include the Trigger Dependent User Info field that solicit BAR from one TID besides B0 to B39.
In enhanced BSRP and enhanced BQRP Trigger, the specific User Info includes B0 to B39.
MAC header
User Info 2
Common Info
User Info 1
User Info 7
User Info 3
User Info 4
User Info 5
User Info 6
UL HE OFDMA
User Info to announce new MU format, e.g. EHT MU MIMO/OFDMA, and other common Info specific to EHT TB
UL EHT MU MUMIMO
User Info to announce new MU format, e.g. NG_EHT OFDMA, and other common Info specific to NG_EHT TB
NG_EHT OFDMA
MAC header
User Info 2
Common Info
User Info 1
User Info 7
User Info 3
User Info 4
User Info 5
User Info 6
UL HE OFDMA
User Info to announce new MU format, e.g. EHT OFDMA/MU_MIMO. and other common Info specific to EHT TB
UL EHT MU MUMIMO
User Info to announce new MU format, e.g. NG_EHT OFDMA/MU_MIMO and other common Info specific to EHT TB
NG_EHT OFDMA
User Info 0
User Info to announce HE OFDMA/MU-MIMO.
Optional Padding
FCS
Optional Padding
FCS
Slide 5

## Slide 6: RU and Nss Consideration
Additional bit in User Info field may be required for RU Allocation.
  One User Info field in the Trigger frame being will be addressed to a STA even for punctured RUs for a STA.
Additional two bits are for >8 SS support in Basic Trigger.
  It is reasonable to assume that >8 SS only occurs in Basic Trigger case.
One available bit here
One available bit in Basic Trigger

## Slide 7: Trigger Design Option 2
The EHT TB PPDU and future are defined through new Trigger types, e.g.:
  The enhanced trigger type (one new value of Triger Type) + 4-bit Extended Trigger Subtype (Extended Basic Trigger, enhanced BFRP, enhanced MU-BAR, enhanced MU-RTS, enhanced BSRP, enhanced BQRP, enhanced NFRP).
Common User, User Info can be redefined to support >160MHz BW, new TB PPDU format, punctured RUs etc.
  The method similar to Option 1 can be used for supporting different TB PPDU types.
    TB independent common information for all TB types, TB dependent common information for specific TB type, User Info fields for specific TB type.
  The Common Info, User Info can be flexibly defined.

## Slide 8: Conclusion
The Trigger design for 11be and the future generation of 802.11 is discussed:
  Option 1:
    Reuse Trigger types in 11ax for 11be and beyond.
  Option 2:
    Define the new Trigger types for 11be and beyond
We prefer option 1 for 11be Trigger design.

## Slide 9: Straw Poll 1
Do you support to reuse the Trigger Type of 11ax in 11be
  All the Per User Info fields in a Trigger frame other than MU-BAR Trigger shall have the same size.

## Slide 10: Straw Poll 2
Do you support that UL HE SIG-A2 Reserved field is used to carry the information of the Trigger frame for soliciting EHT TB PPDU?
  The field name can be revised in Trigger frame for soliciting EHT TB PPDU.

## Slide 11: Straw Poll 3
Do you support that a User Info field with specific value in AID12 field is used to carry the common information of the Trigger frame?