## Slide 1: MLO: AID Allocation
Date: 2020-04-28
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Background
Current consensus includes:
  A bit in a partial virtual bitmap of a TIM element that corresponds to a non-AP MLD is set to 1 if any individually addressed BUs for the non-AP MLD are buffered by the AP MLD.
This implies that an AID is allocated to each non-AP MLD regardless of the number of links the non-AP MLD has set up.
In this contribution, we study if there are any further restrictions needed on the AID allocation for non-AP MLDs.

## Slide 3: Background
Baseline AID allocation rule:
  AID 0 is used to indicate group addressed traffic.
  When a multi-BSSID is supported,
    AIDs from 1 to (2^n -1) are not allocated to a STA, where the maximum possible number of BSSIDs is an integer power of 2, n = log2 (maximum possible number of BSSIDs)
      The bits 1 to (2^n – 1) of the bitmap are used to indicate that one or more group addressed frames are buffered for each AP corresponding to a nontransmitted BSSID and are called NonTxBSS identifiers.
      The NonTxBSS ID equals the value carried in the BSSID Index field of the Multiple BSSID-Index element carried in its nontransmitted BSSID profile.
    AIDs from 2^n to 2007 are allocated to STAs within any BSS corresponding to a transmitted or nontransmitted BSSID.

## Slide 4: Issues
Let us assume that AP1 and AP2 are affiliated with an AP MLD:
  AP1 supports multiple BSSID such that the maximum possible number of BSSIDs for AP1 is 2^n.
    AP1 can assign STAs AID chosen from 2^n to 2007.
  AP2 does not operate with a multiple BSSID set.
    AP2 can assign STAs AIDs chosen from 1 to 2007.
    If AIDs 1 to (2^n-1) are assigned to legacy or single-link STAs:
      In TIM element sent by AP2, these AIDs indicate buffer status of the STAs and there’s no issue.
    If AIDs 1 to (2^n-1) are assigned to non-AP MLDs:
      In TIM element sent by AP2, these AIDs indicate buffer status of the non-AP MLDs and there’s no issue.
      In TIM element sent by AP1, these AIDs are doubly defined for both non-AP MLDs and the nontransmitted BSSIDs.

## Slide 5: Solution
As AID is assigned to an MLD level:
  The AID assigned to a non-AP MLD shall be unique and shall be not reserved on any link
    An AID less than 2^n where n is the maximum value of the MaxBSSID Indicator in a multiple BSSID set is reserved
In other words, if there are N configured links for an AP MLD:
  AIDs from 1 to max(2^n_1, 2^n_2, … 2^n_N) - 1 are not allocated to a non-AP MLD, where the maximum possible number of BSSIDs on i-th link is an integer power of 2, n_i = log2(maximum possible number of BSSIDs on i-th link)

## Slide 6: Operation example
MLD1 includes 3 APs in 3 links (Link1/2/3).
  BSSID of AP1a on Link1 is transmitted BSSID and AP2b on Link2 and AP3c on Link3 ARE nontransmitted BSSIDs.
The number of nontransmitted BSSIDs within a set of Multiple BSSID set on each link is different:
  AP1a: 1, AP2a: 3, AP3a: 3
AIDs from 1 to max(1, 3, 3)=3 are not assigned to a non-AP MLD by MLD1.
  AID = 2 & 3 still can be assigned to legacy STA or a single-link STA on link1.
Link1
Link2
Link 3
: MLD1
AP1a
AP1b
AP2a
AP2b
AP2c
AP3a
AP3b
AP3c
AP3d
AP2d
: transmitted BBSID
: nontransmitted BBSID

## Slide 7: Summary
Baseline AID allocation rule is extended to cover non-AP MLDs.

## Slide 8: SP
Do you support in TGbe SFD that
  The AID assigned to a non-AP MLD shall be unique and shall be non-reserved on any link
    Note: An AID less than 2^n where n is the maximum value of the MaxBSSID Indicator in a multiple BSSID set is reserved.