## Slide 1: EHT-STF Sequences
Date: 2020-05-20
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1], several straw polls relevant to EHT-STF were passed and the remaining issue is to decide 1x/2x EHT-STF sequences for 240/160+80/320/160+160 MHz
We propose those sequences which are designed based on 1x/2x 80MHz/160MHz HE-STF sequences with additional phase rotation to improve PAPR
  We optimize the additional phase rotation coefficients assuming the tone plan proposed in [2]
In addition, we compare PAPRs between the proposed EHT-STF sequences and the data part to verify their feasibility

## Slide 3: 1x/2x EHT-STF Sequence for 240/160+80 MHz (1/6)
1x/2x 80MHz HE STF sequence (80HES) is repeated and second and third 80MHz segments are multiplied by additional coefficients
  [80HES a*80HES b*80HES]
  Candidates of a and b are 1 and -1 as in 11ax
  Utilizing 80HES may be beneficial to implementation and PAPR of the 80MHz portion in the non-contiguous mode

## Slide 4: 1x/2x EHT-STF Sequence for 240/160+80 MHz (2/6)
Proposed 1x EHT-STF sequence for contiguous 240MHz
  EHTS-1520:16:1520 = {M 1 -M 0 -M 1 -M -1*(0 M 1 -M 0 -M 1 -M) -1*(0 M 1 -M 0 -M 1 -M)} * (1+j) / sqrt(2)
  M = {-1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1}
  Coefficients are optimized by minimax approach (i.e., minimizing worst PAPR) considering all punctured cases approved in 11be as well as non-punctured one
All PAPRs of punctured and non-punctured cases are incorporated
Similar trend can be seen as in 80MHz and 160MHz shown in Appendix
PAPRs for the proposed EHT-STF sequence are way below that of the data part

## Slide 5: 1x/2x EHT-STF Sequence for 240/160+80 MHz (3/6)
Proposed 2x EHT-STF sequence for contiguous 240MHz
  EHTS-1528:8:1528 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M) -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M)} * (1+j) / sqrt(2)
    EHTS-1528 = EHTS-520 = EHTS-504 = EHTS504 = EHTS520 = EHTS1528 = 0
  Coefficients are optimized by minimax approach considering all RUs and RU combinations as well as all punctured and non-punctured cases
All PAPRs of RUs and RU combinations as well as punctured and non-punctured cases are incorporated
Similar trend can be seen as in 160MHz shown in Appendix
The amount of PAPRs higher than the median point of the data part is less than 10%

## Slide 6: 1x/2x EHT-STF Sequence for 240/160+80 MHz (4/6)
We propose to unify the sequence between contiguous and non-contiguous modes
  The unified sequence may be desirable from the implementation perspective
  For the 1x EHT-STF sequence, we obtained the same optimal coefficients when considering both contiguous and non-contiguous modes
    PAPR is shown in Appendix
  For the 2x EHT-STF sequence, certain RUs can be regarded as the non-contiguous portions which means we can consider that the selected coefficients shown in the previous slide are optimized under both contiguous and non-contiguous modes
    E.g., one of the 2x996 RUs can be regarded as the non-contiguous 160MHz portion

## Slide 7: 1x/2x EHT-STF Sequence for 240/160+80 MHz (5/6)
Proposed 1x EHT-STF sequence for non-contiguous 160+80 MHz
  Low 160MHz + high 80MHz mode
    Low 160MHz: EHTS-1008:16:1008 = {M 1 -M 0 -M 1 -M 0 -M -1 M 0 M -1 M} * (1+j) / sqrt(2)
    High 80MHz: EHTS-496:16:496 = {-M -1 M 0 M -1 M} * (1+j) / sqrt(2)
  Low 80MHz + high 160MHz mode
    Low 80MHz: EHTS-496:16:496 = {M 1 -M 0 -M 1 -M} * (1+j) / sqrt(2)
    High 160MHz: EHTS-1008:16:1008 = {-M -1 M 0 M -1 M 0 -M -1 M 0 M -1 M} * (1+j) / sqrt(2)

## Slide 8: 1x/2x EHT-STF Sequence for 240/160+80 MHz (6/6)
Proposed 2x EHT-STF sequence for non-contiguous 160+80 MHz
  Low 160MHz + high 80MHz mode
    Low 160MHz: EHTS-1016:8:1016 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 0 -M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
      EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0
    High 80MHz: EHTS-504:8:504 = {-M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
      EHTS-504 = EHTS504 = 0
  Low 80MHz + high 160MHz mode
    Low 80MHz: EHTS-504:8:504 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M} * (1+j) / sqrt(2)
      EHTS-504 = EHTS504 = 0
    High 160MHz: EHTS-1016:8:1016 = {-M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M 0 -M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
      EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0

## Slide 9: 1x/2x EHT-STF Sequence for 320/160+160 MHz (1/7)
We propose two options
  Option 1: 1x/2x 80MHz HE STF sequence (80HES) is repeated and second, third and forth 80MHz segments are multiplied by additional coefficients
    [80HES a*80HES b*80HES c*80HES]
    Candidates of a, b and c are 1 and -1 as in 11ax
    Utilizing 80HES may be beneficial to implementation
  Option 2: 1x/2x 160MHz HE STF sequence (160HES) is repeated and the second 160MHz segment are multiplied by an additional coefficient
    [160HES a*160HES]
    Candidates of a are 1 and -1 as in 11ax
    Utilizing 160HES may be beneficial to implementation and PAPR of the 160MHz portion in the non-contiguous mode

## Slide 10: 1x/2x EHT-STF Sequence for 320/160+160 MHz (2/7)
Proposed 1x EHT-STF sequence for contiguous 320MHz
  Option 1: EHTS-2032:16:2032 = {M 1 -M 0 -M 1 -M 1*(0 M 1 -M 0 -M 1 -M) -1*(0 M 1 -M 0 -M 1 -M) -1*(0 M 1 -M 0 -M 1 -M)} * (1+j) / sqrt(2)
  Option 2: EHTS-2032:16:2032 = {M 1 -M 0 -M 1 -M 0 -M -1 M 0 -M 1 -M -1*(0 M 1 -M 0 -M 1 -M 0 -M -1 M 0 -M 1 -M)} * (1+j) / sqrt(2)
  Coefficients are optimized by minimax approach considering all punctured cases approved in 11be as well as non-punctured one
All PAPRs of punctured and non-punctured cases are incorporated
Both options have a similar trend as in 240MHz
PAPRs for both options are way below that of the data part
Both options have a similar PAPR

## Slide 11: 1x/2x EHT-STF Sequence for 320/160+160 MHz (3/7)
Proposed 2x EHT-STF sequence for contiguous 320MHz
  Option 1: EHTS-2040:8:2040 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M) -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M) -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M)} * (1+j) / sqrt(2)
    EHTS-2040 = EHTS-1032 = EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = EHTS1032 = EHTS2040 = 0
  Option 2: EHTS-2040:8:2040 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 0 -M 1 -M 1 M 1 -M 0 -M 1 M 1 -M 1 -M -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 0 -M 1 -M 1 M 1 -M 0 -M 1 M 1 -M 1 -M)} * (1+j) / sqrt(2)
    EHTS-2040 = EHTS-1032 = EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = EHTS1032 = EHTS2040 = 0
  Coefficients are optimized by minimax approach considering all RUs and RU combinations as well as all punctured and non-punctured cases

## Slide 12: 1x/2x EHT-STF Sequence for 320/160+160 MHz (4/7)
Proposed 2x EHT-STF sequence for contiguous 320MHz (cont.)
All PAPRs of RUs and RU combinations as well as punctured and non-punctured cases are incorporated
Both options have a similar trend as in 240MHz
The amount of PAPRs higher than the median point of the data part is less than 10%
Option 2 is slightly better than option 1

## Slide 13: 1x/2x EHT-STF Sequence for 320/160+160 MHz (5/7)
In the same manner of 240/160+80 MHz, we propose to unify the sequence between contiguous and non-contiguous modes
  The unified sequence may be desirable from the implementation perspective
  For the 1x EHT-STF sequence, we obtained the same optimal coefficients when considering both contiguous and non-contiguous modes
    PAPR is shown in Appendix
  For the 2x EHT-STF sequence, certain RUs can be regarded as the non-contiguous portions which means we can consider that the selected coefficients shown in the previous slide are optimized under both contiguous and non-contiguous modes
    E.g., one of the 2x996 RUs can be regarded as the non-contiguous 160MHz portion

## Slide 14: 1x/2x EHT-STF Sequence for 320/160+160 MHz (6/7)
Proposed 1x EHT-STF sequence for non-contiguous 160+160 MHz
  Option 1
    Low 160MHz: EHTS-1008:16:1008 = {M 1 -M 0 -M 1 -M 0 M 1 -M 0 -M 1 -M} * (1+j) / sqrt(2)
    High 160MHz: EHTS-1008:16:1008 = {-M -1 M 0 M -1 M 0 -M -1 M 0 M -1 M} * (1+j) / sqrt(2)
  Option 2
    Low 160MHz: EHTS-1008:16:1008 = {M 1 -M 0 -M 1 -M 0 -M -1 M 0 -M 1 -M} * (1+j) / sqrt(2)
    High 160MHz: EHTS-1008:16:1008 = {-M -1 M 0 M -1 M 0 M 1 -M 0 M -1 M} * (1+j) / sqrt(2)

## Slide 15: 1x/2x EHT-STF Sequence for 320/160+160 MHz (7/7)
Proposed 2x EHT-STF sequence for non-contiguous 160+160 MHz
  Option 1
    Low 160MHz: EHTS-1016:8:1016 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M} * (1+j) / sqrt(2)
      EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0
    High 160MHz: EHTS-1016:8:1016 = {-M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M 0 -M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
      EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0
  Option 2
    Low 160MHz: EHTS-1016:8:1016 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 0 -M 1 -M 1 M 1 -M 0 -M 1 M 1 -M 1 -M} * (1+j) / sqrt(2)
      EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0
    High 160MHz: EHTS-1016:8:1016 = {-M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M 0 M -1 M -1 -M -1 M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
      EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0

## Slide 16: Further Discussion
AGC issue
  When HE-STF was designed in 11ax, it was verified that 1x and 2x STF have sufficient performance for SU/MU PPDU and TB PPDU, respectively [3]
  Even for the proposed 240/320MHz EHT-STF sequences, the PAPR trend is similar to that of the 160MHz HE-STF sequences and the existing HE-STF sequences are reused, and thus, there may be no critical issue on AGC
320MHz EHT-STF sequence
  Option 2 which reuses the 160MHz HE-STF sequence has a bit lower PAPR than option 1 which reuses the 80MHz one but the gap is negligible
  Most of the features in 11be have been designed based on the 80MHz channel, for example, tone plan, EHT-SIG/U-SIG, etc.
  It would be better to design the 320MHz EHT-STF sequence based on the 80MHz one, and thus, we prefer option 1

## Slide 17: Conclusion
We have proposed 1x/2x EHT-STF sequences in 240/160+80/320/160+160 MHz
For 240/160+80 MHz, we have proposed to repeat the 80MHz HE-STF sequence and apply the additional coefficient to each 80MHz segment
For 320/160+160 MHz, we have proposed two options
  Option 1: repeating the 80MHz HE-STF sequence and applying the additional coefficient to each 80MHz segment
  Option 2: repeating the 160MHz HE-STF sequence and applying the additional coefficient to the highest 160MHz segment
    This option has a slightly better PAPR performance in the 2x case
  Note that there is a discussion on a unified sequence between 240MHz and 320MHz, and we obtained the same coefficients as in the proposed options even in case where the 240MHz puncturing patterns are incorporated into 320MHz PPDU
We have verified that all of the proposed sequences have acceptable PAPR performance

## Slide 18: Straw Poll #1
Do you agree to add the following text to the TGbe SFD?
  1x and 2x 240/160+80MHz EHT-STF sequences are designed by repeating 1x and 2x 80MHz HE-STF sequences, respectively
    Additional coefficients for phase rotation are TBD
Y/N/A: //

## Slide 19: Straw Poll #2
Do you agree to add the following text to the TGbe SFD?
  1x and 2x 320/160+160MHz EHT-STF sequences are designed by repeating 1x and 2x 80MHz HE-STF sequences, respectively
    Additional coefficients for phase rotation are TBD
Y/N/A: //

## Slide 20: Straw Poll #3
Do you agree to unify the EHT-STF sequence between contiguous and non-contiguous modes?
  It is not intended for SFD
Y/N/A: //

## Slide 21: Straw Poll #4
Do you agree to add the following text to the TGbe SFD?
  M = {-1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1}
  1x EHT-STF sequence for contiguous 240MHz PPDU
    EHTS-1520:16:1520 = {M 1 -M 0 -M 1 -M -1*(0 M 1 -M 0 -M 1 -M) -1*(0 M 1 -M 0 -M 1 -M)} * (1+j) / sqrt(2)
  1x EHT-STF sequence for non-contiguous 160+80MHz PPDU
    Low 160MHz + high 80MHz mode
      Low 160MHz: EHTS-1008:16:1008 = {M 1 -M 0 -M 1 -M 0 -M -1 M 0 M -1 M} * (1+j) / sqrt(2)
      High 80MHz: EHTS-496:16:496 = {-M -1 M 0 M -1 M} * (1+j) / sqrt(2)
    Low 80MHz + high 160MHz mode
      Low 80MHz: EHTS-496:16:496 = {M 1 -M 0 -M 1 -M} * (1+j) / sqrt(2)
      High 160MHz: EHTS-1008:16:1008 = {-M -1 M 0 M -1 M 0 -M -1 M 0 M -1 M} * (1+j) / sqrt(2)
Y/N/A: //

## Slide 22: Straw Poll #5
Do you agree to add the following text to the TGbe SFD?
  M = {-1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1}
  2x EHT-STF sequence for contiguous 240MHz PPDU
    EHTS-1528:8:1528 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M) -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M)} * (1+j) / sqrt(2)
      EHTS-1528 = EHTS-520 = EHTS-504 = EHTS504 = EHTS520 = EHTS1528 = 0
  2x EHT-STF sequence for non-contiguous 160+80MHz PPDU
    Low 160MHz + high 80MHz mode
      Low 160MHz: EHTS-1016:8:1016 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 0 -M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
        EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0
      High 80MHz: EHTS-504:8:504 = {-M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
        EHTS-504 = EHTS504 = 0
    Low 80MHz + high 160MHz mode
      Low 80MHz: EHTS-504:8:504 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M} * (1+j) / sqrt(2)
        EHTS-504 = EHTS504 = 0
      High 160MHz: EHTS-1016:8:1016 = {-M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M 0 -M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
        EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0
Y/N/A: //

## Slide 23: Straw Poll #6
Do you agree to add the following text to the TGbe SFD?
  M = {-1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1}
  1x EHT-STF sequence for contiguous 320MHz PPDU
    EHTS-2032:16:2032 = {M 1 -M 0 -M 1 -M 1*(0 M 1 -M 0 -M 1 -M) -1*(0 M 1 -M 0 -M 1 -M) -1*(0 M 1 -M 0 -M 1 -M)} * (1+j) / sqrt(2)
  1x EHT-STF sequence for non-contiguous 160+160MHz PPDU
    Low 160MHz: EHTS-1008:16:1008 = {M 1 -M 0 -M 1 -M 0 M 1 -M 0 -M 1 -M } * (1+j) / sqrt(2)
    High 160MHz: EHTS-1008:16:1008 = {-M -1 M 0 M -1 M 0 -M -1 M 0 M -1 M } * (1+j) / sqrt(2)
Y/N/A: //

## Slide 24: Straw Poll #7
Do you agree to add the following text to the TGbe SFD?
  M = {-1 -1 -1 +1 +1 +1 -1 +1 +1 +1 -1 +1 +1 -1 +1}
  2x EHT-STF sequence for contiguous 320MHz PPDU
    EHTS-2040:8:2040 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M) -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M) -1*(0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M)} * (1+j) / sqrt(2)
      EHTS-2040 = EHTS-1032 = EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = EHTS1032 = EHTS2040 = 0
  2x EHT-STF sequence for non-contiguous 160+160MHz PPDU
    Low 160MHz: EHTS-1016:8:1016 = {M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M 0 M -1 M -1 -M -1 M 0 -M 1 M 1 -M 1 -M } * (1+j) / sqrt(2)
      EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0
    High 160MHz: EHTS-1016:8:1016 = {-M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M 0 -M 1 -M 1 M 1 -M 0 M -1 -M -1 M -1 M} * (1+j) / sqrt(2)
      EHTS-1016 = EHTS-8 = EHTS8 = EHTS1016 = 0
Y/N/A: //

## Slide 25: References
[1] 802-11-20/0585r0 Consideration on EHT-STF
[2] 802-11-20/0666r2 80MHZ OFDMA Tone Plan
[3] 802.11-15/0381r1 HE-STF Proposal

## Slide 26: Appendix
PAPR for 80MHz
1x
2x

## Slide 27: Appendix
PAPR for 160MHz
1x
2x

## Slide 28: Appendix
PAPR when considering both contiguous and non-contiguous cases
240/160+80 MHz
320/160+160 MHz