## Slide 1: Mandatory M-RU Support
Date: 2020-05-26
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Abstract
Previously, each major amendment had a PHY feature clearly differentiating that amendment from the previous one e.g. 80MHz in 11ac and OFDMA in 11ax
Propose to make M-RU a PHY differentiating feature of 11be relative to 11ax

## Slide 3: Discussion
The current SFD defines large M-RU and small M-RU that provide better scheduling efficiency in OFDMA (e.g. small M-RU) and support single user transmissions around spectrum holes in 5GHz (for Radar) and 6GHz (under AFC rules).
The proposals in the SFD provide good balance of implementation complexity and utility (limit to only the most useful cases)
It makes sense that 11be STA and AP devices support those cases to build an ecosystem around them. However when it comes to OFDMA (DL and UL) we can allow the AP the freedom to choose its preferred RU since this feature is totally under the control of the AP.
Hence the proposal differentiates between non-OFDMA and OFDMA transmissions

## Slide 4: Proposal
Propose to make the following RU combinations mandatory in:
  Non-OFDMA transmissions: for AP and non-AP STA
  OFDMA transmissions: for non-AP STA
Mandatory RU combinations:
  Small: {26+52, 106+26} for non-AP STA only
  Large: as shown in the table
Conditioned on device supporting 80, 160, 240 and 320MHz transmissions.
BW | RU | Mandatory in Non-OFDMA for: | Mandatory in OFDMA for:
80MHz | 484+242 | AP , STA | Non-AP STA only
160MHz | 996+(484+242), 996+484 | AP , STA | Non-AP STA only
240MHz | 3x996, 2x996+484, 2x996 (any 2) | AP , STA | Non-AP STA only
320MHz | 4x996, 3x996+484, 3x996 (any 3) | AP , STA | Non-AP STA only

## Slide 5: Straw Poll 1
Do you support the following mandatory RU combinations?
  Small: {26+52, 106+26} for non-AP STA only
  Large: as in the table below
  Conditioned on device supporting 80, 160, 240 and 320MHz transmissions
BW | RU | Mandatory in Non-OFDMA for: | Mandatory in OFDMA for:
80MHz | 484+242 | AP , STA | Non-AP STA only
160MHz | 996+(484+242), 996+484 | AP , STA | Non-AP STA only
240MHz | 3x996, 2x996+484, 2x996 (any 2) | AP , STA | Non-AP STA only
320MHz | 4x996, 3x996+484, 3x996 (any 3) | AP , STA | Non-AP STA only